## Slide 1
Network Environmental
(Connection mode and Pattern, Network and Settings, etc.)
1. This document can be disclosed to Panasonic Sales Partners 2. The specs might be changed without notice since it’s still under development.
Panasonic System Networks Co., Ltd.
Security System Business Division
For Panasonic Sales Company and Business Partner only
Ver.4.20

## Slide 2: History of Revision
Doc. Ver. | Contents | Date of Issue | Remarks
Ver. 4.00/4.10 | Issue of First Edition | Nov. 2015 | 
Ver. 4.15 | Increase Max. number of Routing tables (10 sites -> 50 sites) | Feb. 2015 | Page 18, 28, 44, 48
Ver. 4.20 | Add Max. Bandwidth Setting per site Bandwidth setting per site for each LAN interface can be made | Aug. 2015 | Page 08
 | Add IPv6 Support | Aug. 2015 | Page 54
 | Add Encryption Improvement in SIP Encryption setting can be set individually in SIP | Aug. 2015 | Page 55
Page 1

## Slide 3
Page 2
Connection Mode
HD Visual Communication system support followings 2 connection mode.
Choose suitable connection mode depends on customer’s requirement.
Mode | IP mode (Standard) | NAT Traversal Service mode (Easy Connection)
Outline | Connect HDVC, MPCS (Multi-point Connection Software) and Mobile Devices by using INTRANET (Closed Network: Corporate network or IP-VPN) and Internet (Internet VPN environmental so on) Static Private IP address is required. Operation by DHCP may be possible to use, but IP address might be changed with specific condition. Support Static NAT function as standard. | This is Panasonic proprietary cloud service system . Utilize Terminal ID (7 digit numbers like a telephone number) to make call to HDVC, MPCS (Multi-point Connection Software) and Mobile Devices. A License (Subscribed) is mandatory required. Static Public IP address is not required. Required Panasonic confirmed (recommended) router to use in NAT Traversal Service environmental to avoid any unexpected problem. It does not support in Firewall environmental. Not support multiple device operation under one router. (Multiple connection does not support under the same router.)
Remarks | Common connection mode in Video Conference system category. There is interoperability with other VC systems. Support both SIP and H.323 protocol. | Easy to connect from out side of office. Utilize communication with business partners and Overseas site anytime. No Interoperability with other VC systems. Support SIP protocol only.
Internet VPN
INTRANET

## Slide 4
Page 3
Mode | IP mode (Standard) | NAT Traversal Service mode (Easy Connection)
Network Configuration |  | 
IP Network | INTRANET (Closed Network: Corporate Network, IP-VPN) Internet (Internet VPN, etc.) | Internet
Calling by | IP Address | Terminal ID (7 digit numbers like a telephone number)
iOS
Site A
Android
Site B
VC1600
Head Office
Windows
INTRANET
Site C
Wi-Fi
LTE/Wi-Fi/
WiMAX
iOS
Router
Android
Internet
VC1600
Head Office
Windows
Site A
ISP
Business Partner
Site B
（Windows）
Router
Router
Router
Connection Mode
NAT Traversal Service

## Slide 5
Page 4
 | IP mode |  |  |  |  | NAT Traversal mode
 | Public IP Direct | Static NAT (Port Forward) | Internet VPN | Corporate Network (WAN) | Intranet (LAN) | NAT Traversal Service (Easy Connection)
Available Protocol | SIP / H.323 | SIP / H.323 | SIP / H.323 | SIP / H.323 |  | SIP only
Internet | YES | YES | YES | NO |  | YES
Static IP | YES (Public IP) | YES (Public IP) | YES (Public IP) | YES (Local IP) |  | NO*
Router | NO | YES | YES | NO |  | YES
Configuration | NO | YES (Port Forwarding) | YES (Little complicated) | NO |  | NO*
Security | Low | Mid. | High | High |  | Mid.
Interoperability | YES | YES | YES | YES |  | NO
Total Cost (Internet, Router, maintenance, etc.) | Little Costly (Public IP) | Little Costly (Public IP) | Relatively Costly | --- |  | Relatively Reasonable
Remarks | Easiest | Most Common | Secure |  |  | An activation key is required. (License) Support Panasonic systems only.
* Depends on Network environmental, some settings change are required.
Connection
Type
The following diagram shows possible connection pattern of HDVC system.
There are 7 patterns and can be selected communication protocol such as SIP or H.323.
Connection Mode and Pattern

## Slide 6
Page 5
Mode | IP mode and NAT Traversal Service mode
Network Configuration | 
IP Network | INTRANET + Internet
Calling | IP Address + Terminal ID (7 digit numbers)
IP mode Group
Use IP address
NAT Traversal Service Group
Use Terminal ID
LTE/Wi-Fi/
WiMAX
iOS
Router
Site A
Android
Internet
Site B
VC1600
Head Office
Windows
Site C
(Windows)
INTRANET
Site A
ISP
Business Partner
Site B
(Windows)
Router
Router
Router
Site D
(Tablet PC)
Wi-Fi
NAT Traversal Service
Connection Mode (Multi Protocols Support)
HDVC support Multi Protocols Connection such as IP mode and NAT Traversal Service mode at same time.

## Slide 7
Page 6
Supported Bandwidth / Rate Control
Minimum Required IP rate (Both Audio and Video Transmission)
  2 points connection : 256Kbps
  Multiple connection : 256kbps x # of connection site
Note: Above IP rate includes IP Header.
Heavy traffic
Heavy traffic
Automatic rate control depending on the effective bandwidth
Usable Bandwidth
Packet Loss
Without control
Bandwidth is exceeded at peak communication.
With control
Transfer rate is adjusted to match traffic condition.
Rate Control
The generation of packet losses is prevented by a rate control function, and lost packets are restored by the combined use of Forward Error Correction (FEC) and Automatic Repeat reQuwst (ARQ). Image disruptions and audio interruptions are suppressed for both Intranet and Internet connections to ensure stable connection.
Maximum Supported IP rate
  Maximum Supported IP rate : 18Mbps
AV-QoS (Rate Control) works to control the rate up to 256Kbps

## Slide 8
Page 7
Max. Bandwidth Setting
< Max. Bandwidth Setting (IP bit rate) >
This is setting of Maximum value of IP packet (Video, Audio and QoS) that the HDVC send / receive against to all destination.
HDVC will control based on this setting value to obtain high video and audio quality among available bandwidth of the network.
A
B
C
IP bit rate of line
Stream of HDVC
Other Stream
(ftp, etc.)
=> Enough bandwidth is required against Max. setting value.
IP bit rate
*Try to reach up to Max. setting value.
< Max. Bandwidth of Base site = A + B + C >
< Max. Bandwidth Setting >
Available setting: 256kbps ～ 18Mbps
(Default: 9Mbps)

## Slide 9
In addition to band setting for HDVC, band setting per site for each LAN interface(LAN1/LAN2) can be done, with this new function, communication band for connecting terminals can be controlled by base unit which has MCU.
＜So far＞
＜Ver4.2＞
Band per site is determined as follows. Max. band assigned to HDVC ÷ number connected to built-in MCU
Band per site is determined with max. band per site set to HDVC, regardless of the terminal number connected to built-in MCU.
Intranet VPN
Internet
VC1600
LAN1
LAN2
Communication carrier
Inside
Outside
Max. band
9Mbps
Basic band：1.5Mbps/site
（ 9Mbps÷（Inside:3 units＋Outside:3 units））
# When the band of connecting terminals(including band at contact list/direct dial) is smaller than basic band, each terminals connect with its band.
Intranet VPN
HDVC connection
service
Internet
VC1600
LAN1
LAN2
Communication carier
Inside
Outside
Max. band
9Mbps
LAN2 Max.1Mbps per site
LAN1 Max.512kbps per site
# Below configuration is one example.
# Below configuration is one example.
HDVC connection
service
# When the band of connecting terminals(including band at contact list/direct dial) is smaller than band per site, each terminals connect with its band.
Max. Bandwidth Setting per site
This is new!
Page 8

## Slide 10
Page 9
Bandwidth Control
< Available Bandwidth per site >
In case of multiple connection, available bandwidth per site will be as follows.
  Value of Max. Bandwidth setting / # of connection site = Available Bandwidth / site
  Example: Max. Bandwidth setting: 10M / 5 sites = 2Mbps / site
①
③
Add site
②
①
Max. Bandwidth
Stream of HDVC
Max. Bandwidth/site =
Max. Bandwidth / # of site
Stream of HDVC
Stream of HDVC
②
①
Add site
Base site
Max. Bandwidth Setting
12M
Base site
Max. Bandwidth Setting
12M : 12M / 2 sites = 6M/site
Base site
Max. Bandwidth Setting
12M : 12M / 3 sites = 4M/site
Remote site
Max. Bandwidth Setting
3M
Remote site
Max. Bandwidth Setting
5M
Remote site
Max. Bandwidth Setting
8M
Remote site
Max. Bandwidth Setting
5M
Remote site
Max. Bandwidth Setting
8M
Remote site
Max. Bandwidth Setting
8M
Negotiated Bandwidth
8M
Re-Negotiated Bandwidth
6M
Re-Negotiated Bandwidth
5M
Re-Negotiated Bandwidth
4M
Re-Negotiated Bandwidth
4M
Re-Negotiated Bandwidth
3M

## Slide 11
Page 10
Relation between Bandwidth and Resolution
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Motion mode | 1080p | 60p～10p | ◎ | ◎ | ◎ |  |  |  |  |  |  | 
 | 720p | 60p～10p |  |  | ○ | ◎ | ◎ | ◎ | ◎ |  |  | 
 | w432p | 30p～3.75p |  |  |  |  |  |  | ○ | ◎ | ◎ | ◎
 | w288p | 30p～3.75p |  |  |  |  |  |  |  |  | ○ | ○
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Sharpness mode | 1080p | 60p～10p | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ |  |  |  | 
 | 720p | 60p～10p |  |  |  |  |  | ○ | ◎ | ◎ | ◎ | 
 | w432p | 30p～3.75p |  |  |  |  |  |  |  |  | ○ | ◎
 | w288p | 30p～3.75p |  |  |  |  |  |  |  |  |  | 
< Video Quality: Motion Mode> (Default mode)
< Video Quality: Sharpness Mode >
◎ … Usual Resolution
○ … Available Resolution (QoS=ON)
Support high resolution with low bandwidth, but weak for motion due to low frame rate.
H.264 HighProfile / BaselineProfile (Non-interleave mode)
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Full HD fixed | 1080p | 60p～3.75p | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎
< Video Quality: Resolution (Full HD) >
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
HD fixed | 720p | 60p～3.75p | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎
Fix the resolution as 1080p. It weak for motion due to low frame rate.
< Video Quality: Resolution (HD) >
Note: Available frame rate will be different depends on receiving capability of connection site.
Fix the resolution as 720p. It weak for motion due to low frame rate.

## Slide 12
Page 11
Relation between Bandwidth and Resolution
H.264 BaselineProfile (SingleNAL mode)
 | Resolution | Frame reate | Bandwidth [bps] |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 3M | 2.5M | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Motion mode | 720p | 30/15p | → | → | → | 30p | 30p | 30p | 30p | 30p |  |  |  | 
 | w432p | 30/15p | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 30p | 15p | 
 | w288p | 30/15/10p | → | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 15p | 15/10p
 | SIF(4:3) | 30/15p | → | → | → | → | → | → | 30p | 30p | 30p | 30p | 15p | 15p
< Video Quality: Motion Mode > (Default)
< Video Quality: Sharpness Mode >
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 3M | 2.5M | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Sharpness mode | 720p | 30/15/10/7.5p | → | → | → | 30p | 15p | 15p | 10p | 10p | 10p | 7.5p |  | 
 | w432p | 30/15/10p | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 15p | 15/10p | 10p
 | w288p | 30/15/10p | → | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 15p | 15/10p
 | SIF(4:3) | 30/15p | → | → | → | → | → | → | 30p | 30p | 30p | 30p | 15p | 15p
< Video Quality: Resolution (Full HD / HD) >
 | Resolution | Frame rate | Bandwidth [bps] |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 18M | ～ | 3M | 2.5M | 2M | 1.5M | 1.2M | 1M | 768k | 512k | 384k | 256k
Full HD fixed / HD fixed | 720p | 30～3.75p | → | → | → | 30p | 15p | 15p | 10p | 10p | 10p | 7.5p | 5p | 3.75ｐ
 | w432p | 30/15/10p | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 15p | 15/10p | 10p
 | w288p | 30/15/10p | → | → | → | → | → | 30p | 30p | 30p | 30p | 30p | 15p | 15/10p
 | SIF(4:3) | 30/15p | → | → | → | → | → | → | 30p | 30p | 30p | 30p | 15p | 15p
more than 720p
more than w432p and below 720p
more than w288p and below w432p
more than SIF and below w288p
[ Receiving capability of connection site ]
Note: Available frame rate will be different depends on receiving capability of connection site.
Support high resolution with low bandwidth, but weak for motion due to low frame rate.
Resolution will be fixed as 1080p or 720p. It weak for motion due to low frame rate.

## Slide 13
Page 12
Relation between Bandwidth and Resolution
Bandwidth |  |  |  |  |  |  |  |  |  |  |  |  | 
Video Quality | ２sites ３sites ４sites 5 sites 6 sites 7 sites 8 sites 9 sites 10 sites |  |  |  |  |  |  |  |  |  |  |  | 
SD Quality
HD Quality
Full-HD Quality
1M
4M
8M
Video Quality: Motion Mode
* Available Video Quality will be different depends on line condition and settings of HDVC so on.
18M
2M
16M
6M
10M
12M
14M
768K
Transmission Capability |  | # of site | 1 | 2 | ３ | ４ | ５ | ６ | ７ | ８ | 9
 |  | IP rate | 18.0 | 9.0 | 6.0 | 4.5 | 3.6 | 3.0 | 2.6 | 2.3 | 2.0
Single Stream |  | Resolution | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 720p | 720p
 |  | Max. fps | 60p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
Dual Stream | Camera | Resolution | 1080p | 1080p | 1080p | 1080p | 720p | 720p | 720p | 720p | 720p
 |  | Max. fps | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
 | PC | Resolution | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p
 |  | Max. fps | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
In case of Single Stream

## Slide 14
Page 13
Relation between Bandwidth and Resolution
Bandwidth |  |  |  |  |  |  |  |  |  |  |  |  | 
Video Quality | ２ sites ３ sites ４ sites 5 sites 6 sites 7 sites 8 sites 9 sites 10 sites |  |  |  |  |  |  |  |  |  |  |  | 
SD Quality
HD Quality
Full-HD Quality
1M
4M
8M
18M
2M
16M
6M
10M
12M
14M
Video Quality: Sharpness Mode
512K
Transmission Capability |  | # of site | 1 | 2 | ３ | ４ | ５ | ６ | ７ | ８ | 9
Single Stream |  | Resolution | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p
 |  | Max. fps | 60p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
Dual Stream | Camera | Resolution | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 720p
 |  | Max. fps | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
 | PC | Resolution | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p | 1080p
 |  | Max. fps | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p | 30p
* Available Video Quality will be different depends on line condition and settings of HDVC so on.
In case of Single Stream

## Slide 15
Page 14
Network I/F Specification
Items | Model | # of port | Remarks | 
LAN | VC1600 | 2 Port | RJ45 100BASE-TX (Full Duplex) Default: Auto Negotiation (Setting change can be done by CLI as 100M Full-Duplex) Non-support for Auto MDI/MDI-X | 1000Bas-T support by Auto Negotiation: TBD
 | VC1300 | 1 Port |  | 
VLAN (IEEE802.1Q) |  |  | Non-support | 
Items | Mode | Remarks | 
IP Address | IP mode | Static IP Address / DHCP (VC1600 LAN2: Static IP Address) | IPv6: Non-support
 | NAT Traversal Service mode | Static IP Address / DHCP | 
DNS | IP mode | Use in case of firmware version update via Internet Use in case of communication start and registration of SIP Server / GateKeeper | 
 | NAT Traversal Service mode | Use in case of firmware version update via Internet It is mandatory for NAT Traversal Service | 
Tos (Type of Service) /DiffServe |  | Support (Setting change can be done by CLI) | 
Communication Protocol | IP mode | SIP / H.323 | 
 | NAT Traversal Service mode | SIP only | 

## Slide 16
Page 15
Use Port Information
IP Mode (Static NAT setting: OFF)
Intended Purpose |  | Protocol | Use Port Number | Remarks
SIP | SIP | TCP/UDP | 5060 | 
 | BFCP | UDP | 5800~5899 (VC1600 (9 ports) / VC1300 (3 ports)) | Max. 1 port is required for 1 session
H.323 | H.225 (Q.931) | TCP | 1720 | 
 | H.225 (RAS) | UDP | 1719 | 
 | H.245 | TCP | 5500~5599 (VC1600 (20 ports) / VC1300 (10 ports)) | Max. 2 ports + backup are required for 1 session
Audio | RTP/RTCP | UDP | 5100~5199 (VC1600 (36 ports) / VC1300 (12 ports)) | RTCP Port: RTP port + 1 4 ports per 1 stream is required (RTP + RTCP + Alternatives of Session change (RTP + RTCP))
Video | RTP/RTCP | UDP | 5200~5299 (VC1600 (36 ports) / VC1300 (12 ports)) | 
Video (Sub) | RTP/RTCP | UDP | 5400~5499 (VC1600 (36 ports) / VC1300 (12 ports)) | 
Camera | RTP/RTCP | UDP | 5300~5399 (VC1600 (36 ports) / VC1300 (12 ports)) | 
Intended Purpose |  | Protocol | Use Port Number | Remarks
SIP | SIP | TCP/UDP | 5060 Setting range: 5000～5099 | 
 | BFCP | UDP | 5800-5808 (VC1600 (9 ports) / VC1300 (3 ports)) Setting range: 5800~5890 | Max. 1 port is required for 1 session
H.323 | H.225 (Q.931) | TCP | 1720 | 
 | H.225 (RAS) | UDP | 1719 | 
 | H.245 | TCP | 5500~5519 (VC1600 (20 ports) / VC1300 (10 ports)) Setting range: 5500~5580 | Max. 2 ports + backup are required for 1 session
Audio | RTP/RTCP | UDP | 5100~5135 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5100~5164 | RTCP Port: RTP port + 1 4 ports per 1 stream is required (RTP + RTCP + Alternatives of Session change (RTP + RTCP))
Video | RTP/RTCP | UDP | 5200~5235 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5200~5264 | 
Video (Sub) | RTP/RTCP | UDP | 5400~5435 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5400~5464 | 
Camera | RTP | UDP | 5300~5335 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5300~5364 | 
IP Mode (Static NAT setting: ON)

## Slide 17
Page 16
Use Port Information
Intended Purpose |  | Protocol | Use Port Number | Remarks
External Control (Maintenance) | Web Server (HTTP) | TCP | 80 | Setting change and system control from external.
 | Telnet | TCP | 23 (Port number is changeable) | 
Maintenance | Automatic Firmware Update (DNS) | UDP | Any (32768~61000) (Access to DNS Server) | It is needed in case of firmware download from remote site.
 | Firmware Update (Version Check, Download) | TCP + SSL | Any (32768~61000) (Access to DL Server) | 
Network Diagnosis | Network Diagnosis | ICMP | Network Diagnosis | 
Intended Purpose |  | Protocol | Use Port Number | Remarks
SIP | SIP | TCP | 50000~50999 | Destination Port: 5060
 | BFCP | TCP | 5800~5808 (VC1600 (9 ports) / VC1300 (3 ports)) Setting range: 5800~5890 | Max. 1 port is required for 1 session
Audio | RTP/RTCP | UDP | 5100~5135 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5100~5164 | RTCP Port: RTP port + 1 4 ports per 1 stream is required (RTP + RTCP + Alternatives of Session change (RTP + RTCP))
Video | RTP/RTCP | UDP | 5200~5235 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5200~5264 | 
Video (Sub) | RTP/RTCP | UDP | 5400~5435 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5400~5464 | 
Camera | RTP | UDP | 5300~5335 (VC1600 (36 ports) / VC1300 (12 ports)) Setting range: 5300~5364 | 
NAT Traversal Service | NAT Traversal Service (DNS) | UDP | Any (32768~61000) (Access to DNS Server) | It is needed for server address settlement of NAT Traversal server (Admin. Server)
 | NAT Traversal Service (Download of Configuration Information) | TCP + SSL | Any (32768~61000) (Access to NAT Traversal Service Server) | It is needed for downloading of configuration information from NAT Traversal server (Admin. Server)
NAT Traversal Service Mode
Other Use Ports

## Slide 18
Page 17
Multi Protocol /Dual Network Support
Utilize IP Address
Utilize Terminal ID (7 digits number)
LTE/Wi-Fi/
WiMAX
iOS
Router
Branch Office A
Android
Internet
Branch Office B
VC1600
Head Office
Windows PC
Sales Company
(Windows PC)
INTRANET
Site A
ISP
External
Company
Site B
(Windows PC)
Router
Router
Router
Sales Company D
(Tablet)
Wi-Fi
Support both INTRANET and Internet (NAT Traversal Service) Network environmental
  Simultaneous operation of IP mode and NAT Traversal Service mode is possible
  Two different network environmental can be made with two LAN interface (KX-VC1600 only)
NAT Traversal Service
(Easy Connection)

## Slide 19
Page 18
Dual Network Support
Router
Internet
VC1600
INTRANET
LAN2
LAN1
Interface | NAT Traversal Service mode | IP mode | Remarks
LAN1 | YES | YES | NAT Traversal Service mode can be used in only LAN1. IP mode with Static NAT setting can be used in only LAN1. Default Gateway can be set only LAN1. DHCP can be supported in only LAN1.
LAN2 | NO | YES | Routing setting is required in LAN2 interface (INTRANET) (Routing setting can be made up to 50 sites.)
< Restriction >
In case of H.323 protocol, there are following restrictions to compatible between connection via a Gatekeeper and direct connection.
When Gatekeeper registration is succeeded among same network interface, all communication will be taken via Gatekeeper.
Link between contact list and call history cannot be made.
(Default GW)
Two LAN Interface support (KX-VC1600 only)
  Two different network environmental can be made with two LAN interface
NAT Traversal Service
(Easy Connection)

## Slide 20
Page 19
Network / Protocol Support (Supported Protocol by I/F)
*1: Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) cannot be used simultaneously..
*2: When static NAT function is used in IP mode, Local IP Address judgment function will be available
*3: NAT Traversal Service mode can be used in only LAN1.
*4: IP mode with Static NAT setting can be used in only LAN1.
2 LAN Interface (KX-VC1600 only, LAN1: enable, LAN2: enable)
LAN | Connection Mode and Protocol |  |  |  |  |  | 
 | IP Mode |  |  |  |  |  | NAT Traversal Service
 | SIP | SIP (SIP Server) | SIP (Static NAT) | H.323 | H.323 (Gatekeeper) | H.323 (Static NAT) | 
LAN1 | YES | YES *1 | YES *2 | YES | YES *1 | YES | YES *1
LAN2 | YES | YES *1 | NO *4 | YES | YES *1 | NO *4 | NO *1, *3
LAN | Connection Mode and Protocol |  |  |  |  |  | 
 | IP Mode |  |  |  |  |  | NAT Traversal Service
 | SIP | SIP (SIP Server) | SIP (Static NAT) | H.323 | H.323 (Gatekeeper) | H.323 (Static NAT) | 
LAN 1 | YES | YES *1 | YES *2 | YES | YES *1 | YES *2 | YES *1
*1: Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) cannot be used simultaneously.
*2: When static NAT function is used in IP mode, Local IP Address judgment function will be available.
(The system is judged to be an NAT unnecessary IP address, then operate without NAT)
Automatic setting exclusion range: 192.168.0.0/16 (192.168.0.0-192.168.255.255)
172.16.0.0/12 (172.16.0.0-172.31.255.255)
10.0.0.0/8 (10.0.0.0-10.255.255.255)
1 LAN Interface (KX-VC1300, KX-VC-1600 with LAN1: enable, LAN2: disenable)

## Slide 21
Page 20
Multi Protocols Support
Operating outline
Various endpoints can be connected simultaneously by operating the Multi protocols such as SIP, H.323.
Multi protocols can be on the same network simultaneously.
Communication using NAT traversal mode and IP mode simultaneously
Communication using two IP mode (2 NIC).
Dual networks can be simultaneously accessed by using 2 NIC in case of VC1600.
One of NAT traversal mode, SIP server or H.323 Gate Keeper can be used. Plural Server Connection cannot be used simultaneously.
Protocol combination that can be used simultaneous is shown below in detail.
 |  | Protocol 1 |  |  |  | 
 |  | SIP | SIP server | H.323 | H.323 Gatekeeper | NAT traversal mode
Protocol 2 | SIP | YES |  |  |  | 
 | SIP server | YES | NO *1 |  |  | 
 | H.323 | YES | YES | YES |  | 
 | H.323 Gatekeeper | YES | NO *1 | YES | NO *1 | 
 | NAT traversal mode | YES | NO *1 | YES | NO *1 | NO *1
*1 : Plural servers such as NAT traversal mode, SIP server, Gate Keeper cannot be used simultaneously.

## Slide 22
Page 21
Multi Protocol / Dual Network Support (Configuration)
INTRANET
LAN1
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
Case 1 (INTRANET)
Case 2 (INTRANET)
INTRANET
LAN1
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
Gatekeeper
Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) cannot be used simultaneously.
1 LAN Interface (KX-VC1300, KX-VC-1600 with LAN1: enable, LAN2: disenable)

## Slide 23
Page 22
Multi Protocol / Dual Network Support (Configuration)
HDVC
(NAT Traversal Service)
Internet
HDVC Mobile
(NAT Traversal Service)
NAT Traversal Service mode
INTRANET
LAN1
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
(Default Gateway)
Case 3 (Internet + INTRANET)
Set up Default Gateway settings of HDVC towards Internet side (NAT Traversal Service).
Set up Routing configuration required for communication with the network in INTRANET by the router side.
Use Panasonic recommended router for NAT Traversal Service.
Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) can not be used simultaneously.
1 LAN Interface (KX-VC1300, KX-VC-1600 with LAN1: enable, LAN2: disenable)

## Slide 24
Page 23
Internet
HDVC
(H.323)
Other VC
(H.323)
IP mode
H.323 connection
(Static MAT)
HDVC
(SIP)
HDVC Mobile
(SIP)
IP mode
SIP connection
(Static NAT)
INTRANET
LAN1
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
(Default Gateway)
Case 4 (Internet + INTRANET)
1 LAN Interface (KX-VC1300, KX-VC-1600 with LAN1: enable, LAN2: disenable)
Set up Default Gateway settings of HDVC towards Internet side (NAT Traversal Service).
Set up Routing configuration required for communication with the network in INTRANET by the router side.
Set up Local Address judgment function of the HDVC, because NAT is not required communication with the network in INTRANET.
When static NAT function is used, install one HDVC system to one router as basic.
  (From technical point of view, plural installation can be made. But there is possibility that other VC systems may not be communicated because port setting change is required.
Multi Protocol / Dual Network Support (Configuration)

## Slide 25
Page 24
Case 1 (INTRANET + INTRANET)
2 LAN Interfaces (KX-VC-1600 with LAN1: enable, LAN2: enable)
INTRANET 2
LAN1
HDVC (H.323)
IP mode
H.323 connection
INTRANET 1
Other VC (H.323)
HDVC (H.323)
Other VC (H.323)
IP mode
H.323 connection
LAN２
HDVC (SIP)
HDVC Mobile (SIP)
IP mode
SIP connection
Set up Default Gateway settings of HDVC towards LAN 1 side.
Set up Routing configuration required for communication with the network in LAN 2 side.
Multi Protocol / Dual Network Support (Configuration)
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)

## Slide 26
Page 25
2 LAN Interfaces (KX-VC-1600 with LAN1: enable, LAN2: enable)
Set up Default Gateway settings of HDVC towards LAN 1 side.
Set up Routing configuration required for communication with the network in LAN 2 side.
Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) can not be used simultaneously.
Multi Protocol / Dual Network Support (Configuration)
Case 2 (INTRANET + INTRANET)
INTRANET 2
LAN1
HDVC (H.323)
IP mode
H.323 connection
INTRANET 1
Other VC (H.323)
HDVC (H.323)
Other VC (H.323)
IP mode
H.323 connection
LAN２
HDVC (SIP)
HDVC Mobile (SIP)
IP mode
SIP connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
Gatekeeper

## Slide 27
Page 26
2 LAN Interfaces (KX-VC-1600 with LAN1: enable, LAN2: enable)
HDVC
(NAT Traversal Service)
Internet
HDVC Mobile
(NAT Traversal Service)
NAT Traversal Service mode
INTRANET
LAN2
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
(Default Gateway)
LAN1
Case 3 (Internet + INTRANET)
Set up Default Gateway settings of HDVC towards Internet side (NAT Traversal Service).
Set up Routing configuration required for communication with the network in LAN 2 side.
Set up router configuration as necessary.
Use Panasonic recommended router for NAT Traversal Service.
Plural Server Connection (NAT traversal mode, SIP server or H.323 Gate Keeper) can not be used simultaneously.
Multi Protocol / Dual Network Support (Configuration)

## Slide 28
Page 27
2 LAN Interfaces (KX-VC-1600 with LAN1: enable, LAN2: enable)
Internet
HDVC
(H.323)
Other VC
(H.323)
IP mode
H.323 connection
(Static NAT)
HDVC
(SIP)
HDVC Mobile
(SIP)
IP mode
SIP connection
(Static NAT)
INTRANET
LAN2
Other VC
(H.323)
HDVC
(H.323)
IP mode
H.323 connection
HDVC
(SIP)
IP mode
SIP connection
HDVC Mobile
(SIP)
(Default Gateway)
LAN1
Set up Default Gateway settings of HDVC towards Internet side (NAT Traversal Service).
Set up Routing configuration required for communication with the network in LAN 2 side.
Set up router configuration as necessary.
Since the Interface is separated, Local Address judgment function of the HDVC is not required.
When static NAT function is used, install one HDVC system to one router as basic.
  (From technical point of view, plural installation can be made. But there is possibility that other VC systems may not be communicated because port setting change is required.
Case 4 (Internet + INTRANET)
Multi Protocol / Dual Network Support (Configuration)

## Slide 29
Page 28
Network Settings
Network Settings (LAN1)
Network Settings (LAN2) (KX-VC1600 only)
Routing Settings
Routing List (Max. up to 50 sites can be registered)
IP Address
IP Address
Subnet mask
LAN 2
Default Gateway
DNS Server
Primary DNS Server
Secondary DNS Server
IP Address
Subnet mask
Router Settings
It will be appeared after inputting IP Address and Subnet mask of LAN 2, then press Green button.
Destination
Subnet mask
Gateway

## Slide 30
Page 29
Static NAT Settings (Port Forward)
NAT: Network Address Translation
NAT has function that changes Private (Local) IP address and port number inside LAN, and Public (Global) address and port number on internet.
Basic Network Configuration
Site A
Site B
Private IP Address (X)
Private IP Address (Y)
Router
Router
Internet
Public IP Address (Y)
Public IP Address (X)
Static NAT (Port Forwarding) Setting
Static NAT (Port Forwarding) Setting
NAT/FW
What is NAT/FW Traversal?
NAT: Cannot connect from outside (WAN) to inside (LAN).
FW : For security, control ports to open.
Outside: WAN
Inside: LAN
Forward data from outside “WAN” to inside “LAN” by using a “port forwarding” supported router.
Simple NAT/FW Traversal
Port forwarding supported Router
Passing data by router setting
Fixed IP Address

## Slide 31
Page 30
Site B (Initiator)
Site A (Receiver)
Local IP Address
（Fixed IP）
Public IP Address
1. Send SIP from site B to Site A
IP Header
To IP 122.1.63.91
From IP 192.168.0.2
SIP Information
To IP 122.1.63.91
From IP 114.10.229.61
(Simple Static NAT overwrites From IP in SIP)
IP 192.168.0.1
IP 192.168.0.2
Router
2. Router will change From IP Address to its own Public IP (114.10.229.161) Address since Private IP Address (192.168.0.2) is useless once packet go into the Internet world.
This is called “NAT”.
3. Packet from Site B to A converted by NAT
IP Header
To IP 122.1.63.91
From IP 114.10.229.161 (NAT convert it)
SIP Information
To IP 122.1.63.91
From IP 114.10.229.161
IP 122.1.63.91
IP 114.10.229.161
5. Packet from Site A to B converted by NAT
IP Header (IP Information)
To IP 192.168.0.2 (NAT convert it)
From IP 122.1.63.91
SIP Information
To IP 114.10.229.161
From IP 122.1.63.91
Simple Static NAT Setting
Static Port Forward Setting
Internet
4. Send SIP from Site A to B
IP Header
To IP 114.10.229.161
From IP 122.1.63.91
SIP Information
To IP 114.10.229.161
From IP 122.1.63.91
Static NAT Settings (Port Forward)
Outline of NAT (How does it work)

## Slide 32
Page 31
NAT Traversal Function (Static NAT) can be used in IP Mode.
NAT Traversal Function makes possible communication in NAT Environmental together with Static NAT Function of Router.
Internet
Router for Static NAT
(Port Forwarding)
HDVC： In IP Mode (Static NAT Settings)
・・・Public IP
・・・Private IP (Static)
Applicable Devices | Availability of NAT Traversal Function | Type of Public IP Address | 
 |  | Static | Dynamic
HDVC | YES | YES | YES
Multi-Point Connection Software（MPCS） | NO | NO | NO
HDVC Mobile for Android / iOS | YES | YES | YES
HDVC Mobile Windows | YES | YES | YES
Note:
Up to 2 HDVCs (include HDVC Mobile) can be installed under the same router. But it not allowed simultaneous connection at same time.
Static IP Address is surely required to assign HDVC. (DHCP does not support)
Dynamic IP address support with following firmware version.
  HDVC: From Ver.3.10 onward,
  HDVC Mobile for Android: From Ver.2.00 onward
  HDVC Mobile for Windows: From Ver.2.00 onward
Automatic Local IP Address judgment function: When HDVC is judged as a local IP address, it is regarded as the system in INTRANET, and NAT operation is not performed.
Forward
LAN to WAN
Forward
WAN to LAN
Comparison (Relationship with Devices)
Static NAT Settings (Port Forward)

## Slide 33
Page 32
Static NAT Settings (Port Forward)
NAT Traversal Service
IP mode
(Static NAT Setting: OFF)
Static Port Forward Setting
It cannot be connected with Non-static NAT setting systems.
It cannot be connected with NAT Traversal Service mode systems.
It cannot be connected with Dynamic Port Forwarding systems.
IP mode
(Static NAT Setting: ON)
Dynamic Port Forward Setting only
It cannot be connected between the systems installed under the same router. But it can be made if the router support NAT loopback (hairpin NAT).
Up to 2 HDVCs (include HDVC Mobile) can be installed under the same router. But it not allowed simultaneous connection at same time.
Restriction (Non-supported Network Environmental for NAT)
Static Port Forward Setting
IP mode
(Static NAT Setting: OFF)
IP mode
(Static NAT Setting: ON)
X
X
X
？？？
Internet
Internet

## Slide 34
Page 33
Static NAT Settings
NAT Settings Menu (Page 1)
Setting Item | Setting Value
RTP and RTCP for Audio | 5100-5135 (VC1600: 16 ports / VC1300: 12 ports)
RTP and RTCP for Video | 5200-5235 (VC1600: 16 ports / VC1300: 12 ports)
Camera Control | 5300-5335 (VC1600: 16 ports / VC1300: 12 ports)
RTP and RTCP for Video (Sub) | 5400-5435 (VC1600: 16 ports / VC1300: 12 ports)
BFCP | 5800-5808 (VC1600: 9 ports / VC1300: 3 ports)
SIP | 5060
H.245 | 5500-5519 (VC1600: 20 ports / VC1300: 10 ports)
Setting Item | Setting Value
Static NAT | ON / OFF
WAN IP Address | 
Local Address Judgment | OFF / Auto
Local Address Judgment | Setting Value
Disable | Conduct NAT operation against all IP address
Auto | When the system is judged as private IP address (10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16), NAT operation won’t be conducted because the system recognize as a endpoint that installed in INTRANET environmental.
Manual | For the manual inputted endpoint, the system recognize as a endpoint that installed in INTRANET environmental, then NAT operation won’t be conducted. (Manual setting can be done by CLI only)
Go to “Menu” => “Settings” => “Admin Login” => NAT Settings”
NAT Settings Menu (Page 2)
RTP and RTCP for Audio
RTP and RTCP for Video
Camera Control
RTP and RTCP for Video
BFCP
SIP
H.245
Local Address Judgment
WAN IP Address
Static NAT

## Slide 35
Page 34
Static NAT Settings Procedure
5100
5115
5200
5215
5300
5316
5400
5415
5800
5804
5600
5600
Step 2: Static NAT Settings
Step 1: Input IP address
Step 3: Router configuration
5500
5515
TCP
Note 1: Setting menu will be different depends on router.
Note 2: If the router has “SIP ALG” function, set “SIP ALG” setting as “Disable” in the router as necessary.
Menu -> Settings -> Network Settings
Then input Local IP Address, Subnet Mask and Default Gateway.
Menu -> Settings -> Admin -> Static NAT Settings
Then input WAN IP Address. Change Port Information as necessary.
Input specific Port Number based on port information that is assigned to the HDVC system at step 2. And select Protocol and IP Address where to forward.
RTP and RTCP for Audio
RTP and RTCP for Video
Camera Control
RTP and RTCP for Video
BFCP
SIP
H.245
These are default port numbers that HDVC system uses.
Basically, it is not necessary to change these port numbers.
1720
1720
192.168.1.10
192.168.1.1
255.255.255.0
192.168.1.10
192.168.1.10
192.168.1.10
192.168.1.10
192.168.1.10
192.168.1.10
192.168.1.10
192.168.1.10

## Slide 36
Page 35
Gatekeeper Function
Gatekeeper
H.323 Name: hdcom01
H.323 Extension:1111
Register to Gatekeeper
H.323 Name: hdcom02
H.323 Extension: 2222
H.323 Name: VC03
H.323 Extension: 3333
INTRANET
Other VC
(H.323)
Connection is possible at the connection method with which the IP Address, H.323 Extension (E.164) and H.323 ID were intermingled.
(Depends on Gatekeeper settings)
When registration fails in a Gatekeeper, the independent calling by an IP address is possible for HDVC.
Setting of the concurrent use of SIP server and Gatekeeper cannot be performed.
< Panasonic investigated Model >
TANDBERG：Video Communication Server（VCS） Ver7.2
VCS-Control / VCS-Expressway
(VCS-Expressway does not support Firewall Traversal connection.)
Outline of Gatekeeper Function
The device which manages and control the endpoints on H.323 networks.
Connection control, authentication, address translation, bandwidth control and fee collection management are performed.
Unified management of the video conferencing system is possible by connecting Gatekeeper installed in the INTRANET side.
HDVC
HDVC

## Slide 37
Page 36
H.460 Client Function
Support NAT / Firewall Traversal by implementing the H.460 client function.
Connection with existing video conferencing systems via H.460 server.
Coordinate with multiple connection cloud service connected via H.460 server.
H.460 Server/
Gate Keeper
FW
H.460 Client
FW
H.460 Client
FW
H.460 Client
Other VC
(H.323)
Internet
Other VC
(H.323)
MCU
(H.323)
< Panasonic investigated Model >
TANDBERG：Video Communication Server（VCS） Ver7.2
VCS-Control / VCS-Expressway
(VCS-Expressway does not support Firewall Traversal connection.)
Outline of H.460 Client Function
Standard protocol for NAT / Firewall Traversal on H.323 networks.
Communication with the video conferencing system of the INTRANET side is possible beyond the Firewall by connecting H.460 Server installed in the Internet (Global Network) side.
HDVC
HDVC

## Slide 38
Page 37
H.323 Settings (Gatekeeper / H.460)
Setting Item | Setting Value
Gatekeeper | ON / OFF
Gatekeeper Address | (Essential in case of use Gatekeeper)
H.323 Name | 
H.323 Extension | 
Authentication | ON / OFF
Authentication ID | 
Authentication Password | 
H.460 | ON / OFF （(Using Gatekeeper is mandatory)
Set up Gatekeeper based on setting information of TANDBERG Video Communication Server (VCS).
Settings are required when communicating via a Gatekeeper.
  Gatekeeper Address (Essential)
  H.323 Name (H.323 ID)
  H.323 Extension (E.164)
  Authentication (ID and Password)
Use of H.460:
*Using Gatekeeper is mandatory
H.323 Settings Menu (System settings (Admin. Menu))
Authentication ID
H.323 Extension
Authentication Password
H.323 Name
H.460
Authentication
Gatekeeper Address
Gatekeeper

## Slide 39
Page 38
Codec Settings
Setting Item | Setting Value
SIP / Video System | H.264 / Baseline Profile (Single NAL Unit) H.264 / Baseline Profile (Non-Interleaved) H.264 / High Profile (Non-Interleaved) H.263 H.261
SIP／音声方式 | G.711 (A-Law) G.711 (μ-Law) G.722 G.722.1 G.722.1 Annex C (48 kbps) G.722.1 Annex C (24 kbps) AAC-LD
SIPのQoS | ON / OFF
Setting Item | Setting Value
H.323 / Video System | H.264 / Baseline Profile (Single NAL Unit) H.264 / Baseline Profile (Non-Interleaved) H.264 / High Profile (Non-Interleaved) H.263 H.261
H.323 / Audio System | G.711 (A-Law) G.711 (μ-Law) G.722 G.722.1 G.722.1 Annex C (48 kbps) G.722.1 Annex C (24 kbps) AAC-LD
H.323 / QoS | ON / OFF
Codec Settings Menu (System settings (Admin. Menu))

## Slide 40
Page 39
Call Type / Connection Mode Settings
Setting Item | Setting Value
SIP | ON / OFF
H.323 | ON / OFF
Priority for connection mode | NAT Traversal Service Mode IP Mode (SIP) IP Mode (H.323)
Call Type Settings Menu (System settings (Admin. Menu))
Connection mode Settings Menu (System settings (Admin. Menu))
Setting Item | Setting Value
Connection Mode | IP Mode NAT Traversal Mode IP / NAT Traversal Mode
Priority for connection mode
H.323
SIP
Connection mode

## Slide 41
Page 40
Multi Protocol / Dual Network Settings Example 1
LTE/Wi-Fi/
WiMAX
iOS
Router
Branch Office A
192.168.11.0/24
Android
Internet
Branch Office B
192.168.12.0/24
192.168.1.0/24
Head Office
Windows PC
192.168.13.210
Sales Office C
192.168.13.0/24
INTRANET
Site A
ISP
Site B
(Windows PC)
Router
Router
Sales Office D
192.168.14.0/24
Wi-Fi
192.168.12.201
192.168.11.201
192.168.1.201
192.168.14.210
192.168.1.253
192.168.1.254
LAN1
Set up Default Gateway toward Internet
Conduct routing settings for INTRANET at router side.
192.168.12.254
192.168.13.254
192.168.14.254
192.168.11.254
Case 1: 1 LAN Interface (NAT Traversal Service mode and IP mode)
NAT Traversal Service
(Easy Connection)

## Slide 42
Page 41
LAN | Connection mode | Network Settings |  |  | Remarks
LAN１ | NAT Traversal / IP mode | Manual | IP Address | 192.168.1.201 | Manual set up for HDVC
 |  |  | Subnet Mask | 255.255.255.0 | 
 |  |  | Default Gateway | 192.168.1.254 | 
 |  | Manual | Primary DNS server | 8.8.8.8 (Reference) | Manual set up for HDVC
 |  |  | Secondary DNS server | 8.8.4.4 (Reference) | 
Network Configuration at each site
Network Settings at Head Office (VC 1300)
*The following routing settings are needed at Router side
Item | IP address | Subnet Mask | Gateway Address
Set Point | 192.168.11.0 | 255.255.255.0 | 192.168.1.253
 | 192.168.12.0 | 255.255.255.0 | 192.168.1.253
 | 192.168.13.0 | 255.255.255.0 | 192.168.1.253
 | 192.168.14.0 | 255.255.255.0 | 192.168.1.253
Multi Protocol / Dual Network Settings Example 1
 | Site | Network |  | Connection mode | Network Address | IP Address (HDVC) | Subnet Mask | Gateway Address | Remarks
１ | Head Office | Internet | WAN | NAT Traversal / IP mode | DHCP |  |  |  | Use recommended router
 |  | INTRANET | LAN |  | 192.168.1.0 | 192.168.1.201 | 255.255.255.0 | 192.168.1.254 | Manual set up for HDVC
２ | Branch Office A | INTRANET |  | IP mode | 192.168.11.0 | 192.168.11.201 | 255.255.255.0 | 192.168.1.254 | 
３ | Branch Office B | INTRANET |  | IP mode | 192.168.12.0 | 192.168.12.201 | 255.255.255.0 | 192.168.1.254 | 
４ | Sales Office C | INTRANAT |  | IP mode | 192.168.13.0 | 192.168.13.210 | 255.255.255.0 | 192.168.1.254 | 
５ | Sales Office D | INTRANET |  | IP mode | 192.168.14.0 | 192.168.14.210 | 255.255.255.0 | 192.168.1.254 | 

## Slide 43
Page 42
LTE/Wi-Fi/
WiMAX
iOS
Router
Branch Office A
192.168.11.0/24
Android
Internet
Branch Office B
192.168.12.0/24
172.16.1.0/24
192.168.1.0/24
Head Office
Windows PC
192.168.13.210
Sales Office C
192.168.13.0/24
INTRANET
Site A
ISP
Site B
（Windows PC）
Router
Router
Sales Office D
192.168.14.0/24
Wi-Fi
192.168.12.201
192.168.11.201
192.168.1.201
192.168.14.210
192.168.1.254
172.16.1.254
172.16.1.xxx
(DHCP)
LAN1
LAN2
Set up Default Gateway for LAN 1 only. Set up Default Gateway toward Internet.
192.168.12.254
192.168.13.254
192.168.14.254
192.168.11.254
Multi Protocol / Dual Network Settings Example 2
Case 2: 2 LAN Interface (NAT Traversal Service mode and IP mode)
NAT Traversal Service
(Easy Connection)
Conduct routing settings for INTRANET by “Routing settings” of HDVC.

## Slide 44
Page 43
LAN | Connection mode | Network Settings |  |  | Remarks
LAN１ | NAT Traversal / IP mode | Auto (DHCP) | IP Address |  | Assigned by DHCP server
 |  |  | Subnet Mask |  | 
 |  |  | Default Gateway |  | 
 |  | Auto (DHCP) | Primary DNS server |  | 
 |  |  | Secondary DNS server |  | 
LAN2 |  | Manual | IP Address | 192.168.1.201 | 
 |  |  | Subnet Mask | 255.255.255.0 | 
ネットワーク構成
Multi Protocol / Dual Network Settings Example 2
 | Site | Network |  | Connection mode | Network Address | IP Address (HDVC) | Subnet Mask | Gateway Address | Remarks
１ | Head Office (LAN 1) | Internet | WAN | NAT Traversal / IP mode | DHCP |  |  |  | Use recommended router
 |  | INTRANET | LAN |  | 192.168.1.0 | 192.168.1.201 | 255.255.255.0 | 192.168.1.254 | 
2 | Branch Office A | INTRANET |  | IP mode | 192.168.11.0 | 192.168.11.201 | 255.255.255.0 | 192.168.1.254 | 
3 | Branch Office B | INTRANET |  | IP mode | 192.168.12.0 | 192.168.12.201 | 255.255.255.0 | 192.168.1.254 | 
4 | Sales Office C | INTRANAT |  | IP mode | 192.168.13.0 | 192.168.13.210 | 255.255.255.0 | 192.168.1.254 | 
5 | Sales Office D | INTRANET |  | IP mode | 192.168.14.0 | 192.168.14.210 | 255.255.255.0 | 192.168.1.254 | 
Network Configuration at each site
Network Settings at Head Office (VC 1600)
Routing | IP address | Subnet Mask | Gateway Address | Remarks
1 | 192.168.11.0 | 255.255.255.0 | 192.168.1.253 | Router setting is required for INTRANET site
2 | 192.168.12.0 | 255.255.255.0 | 192.168.1.253 | 
3 | 192.168.13.0 | 255.255.255.0 | 192.168.1.253 | 
4 | 192.168.14.0 | 255.255.255.0 | 192.168.1.253 | 

## Slide 45
Destination
Subnet mask
Gateway
Page 44
Choose Select Connection mode as “IP mode / NAT Traversal mode”.
Multi Protocol / Dual Network Settings Example 2
192.168.1.201
255.255.255.0
Go to “Network settings”, then input necessary IP address for LAN 1. Choose “Auto” “Auto” as basic setting.
Press “Red button” (Next), then input necessary IP address for LAN 2. (KX-VC1600 only)
192.168.11.0 255.255.255.0 192.168.1.254
192.168.12.0 255.255.255.0 192.168.1.254
192.168.13.0 255.255.255.0 192.168.1.254
192.168.14.0 255.255.255.0 192.168.1.254
“Routing settings” (Max. 50 sites can be registered)
“Routing settings” menu
Set up remote site network segment among INTRANET.
LAN 2
IP Address
Subnet mask
Router Settings

## Slide 46
Page 45
LTE/Wi-Fi/
WiMAX
iOS
Router
Branch Office A
192.168.11.0/24
Android
Internet
Branch Office B
192.168.12.0/24
172.16.1.0/24
192.168.1.0/24
Head Office
Windows PC
192.168.13.210
Sales Office C
192.168.13.0/24
INTRANET
Site A
ISP
Site B
(Windows PC)
Router
Router
Sales Office D
192.168.14.0/24
Wi-Fi
192.168.12.201
192.168.11.201
192.168.1.201
192.168.14.210
192.168.1.254
172.16.1.254
172.16.1.201
LAN1
LAN2
192.168.12.254
192.168.13.254
192.168.14.254
192.168.11.254
Router
Other VC
(H.323)
152.142.132.122
(Static Public IP Address)
Multi Protocol / Dual Network Settings Example 3
Case 3: 2 LAN Interface (NAT Traversal Service mode and IP mode with Static NAT setting)
Conduct routing settings for INTRANET by “Routing settings” of HDVC.
Set up Default Gateway for LAN 1 only. Set up Default Gateway toward Internet.
NAT Traversal Service
(Easy Connection)

## Slide 47
Page 46
Multi Protocol / Dual Network Settings Example 3
ネットワーク構成
 | Site | Network |  | Connection mode | Network Address | IP Address (HDVC) | Subnet Mask | Gateway Address | Remarks
１ | Head Office | Internet | WAN | NAT Traversal / IP mode with Static NAT | 152.142.132.122 |  |  | 0.0.0.0 | Static Public IP is required. Use recommended router
 |  | INTRANET | LAN |  | 192.168.1.0 | 192.168.1.201 | 255.255.255.0 | 192.168.1.254 | 
2 | Branch Office A | INTRANET |  | IP mode | 192.168.11.0 | 192.168.11.201 | 255.255.255.0 | 192.168.1.254 | 
3 | Branch Office B | INTRANET |  | IP mode | 192.168.12.0 | 192.168.12.201 | 255.255.255.0 | 192.168.1.254 | 
4 | Sales Office C | INTRANAT |  | IP mode | 192.168.13.0 | 192.168.13.210 | 255.255.255.0 | 192.168.1.254 | 
5 | Sales Office D | INTRANET |  | IP mode | 192.168.14.0 | 192.168.14.210 | 255.255.255.0 | 192.168.1.254 | 
Network Configuration at each site
Setting of Router 1
Remarks
The followings are use port information of HDVC and Port forward settings are required accordingly. UDP/5100～5135 Audio RTP・RTCP UDP/5200～5235 Video RTP・RTCP UDP/5300～5335 Camera Control UDP/5400～5435 Sub Camera RTP・RTCP TCP/5800～5808 BFCP TCP・UDP/5060 SIP TCP/1720 H.225 TCP/5500～5519 H.245

## Slide 48
Page 47
LAN | Connection mode | Network Settings |  |  | Remarks
LAN１ | NAT Traversal / IP mode | Auto (DHCP) | IP Address | 172.16.1.201 | Manual setting is required when Static NAT function is selected.
 |  |  | Subnet Mask | 255.255.255.0 | 
 |  |  | Default Gateway | 172.16.1.254 | 
 |  | Auto (DHCP) | Primary DNS server | 8.8.8.8 (Reference) | 
 |  |  | Secondary DNS server | 8.8.4.4 (Reference) | 
LAN2 |  | Manual | IP Address | 192.168.1.201 | 
 |  |  | Subnet M | 255.255.255.0 | 
Network Settings at Head Office (VC 1600)
Routing | IP address | Subnet Mask | Gateway Address | Remarks
1 | 192.168.11.0 | 255.255.255.0 | 192.168.1.253 | Router setting is required for INTRANET site
2 | 192.168.12.0 | 255.255.255.0 | 192.168.1.253 | 
3 | 192.168.13.0 | 255.255.255.0 | 192.168.1.253 | 
4 | 192.168.14.0 | 255.255.255.0 | 192.168.1.253 | 
Multi Protocol / Dual Network Settings Example 3
NAT Settings | Use of Static NAT | WAN IP Address | Local IP Address Judgment | Remarks
Static | YES | 152.142.132.122 | Auto | Local IP Address Judgment: Auto *When HDVC is judged as Private IP Address such as 10.0.0.0/8, 172.16.0.0/12 and 192.168.0.0/16, it is regarded as the endpoint in intranet. In fact, NAT operation is not performed.
Audio RTP/RTPC | Video RTP/RTPC | Camera Control | Sub Camera RTP/RTPC | Remarks
5100~5135 | 5200~5235 | 5300~5335 | 5400~5435 | Basically it will not be changed
BFCP | SIP | H.245 |  | 
5800~5808 | 5060 | 5500~5519 |  | 

## Slide 49
Page 48
Choose Select Connection mode as “IP mode / NAT Traversal mode”.
Multi Protocol / Dual Network Settings Example 3
Go to “Network settings”, then input necessary IP address for LAN 1.
Press “Red button” (Next), then input necessary IP address for LAN 2. (KX-VC1600 only)
8.8.8.8
172.16.1.254
255.255.255.0
172.16.1.201
192.168.11.0 255.255.255.0 192.168.1.254
192.168.12.0 255.255.255.0 192.168.1.254
192.168.13.0 255.255.255.0 192.168.1.254
192.168.14.0 255.255.255.0 192.168.1.254
“Routing settings” (Max. 50 sites can be registered)
“Routing settings” menu
Destination
Subnet mask
Gateway
192.168.1.201
255.255.255.0
Set up remote site network segment among INTRANET.
LAN 2
IP Address
Subnet mask
Router Settings
IP Address
IP Address
Subnet mask
Default Gateway
DNS Server
Primary DNS Server
Secondary DNS Server
8.8.4.4

## Slide 50
Page 49
NAT Settings (Page 1)
NAT Settings (System settings (Admin. Menu))
Multi Protocol / Dual Network Settings Example 3
NAT Settings (Page 2)
Authentication ID
H.323 Extension
Authentication Password
H.323 Name
H.460
Authentication
Gatekeeper Address
Gatekeeper
These are default port numbers that HDVC system uses.
Basically, it is not necessary to change these port numbers.
And conduct Port Forward settings based on these information at router side.
Local Address Judgment
WAN IP Address
Static NAT
Static
Auto
152.142.132.122

## Slide 51
Page 50
Note:
It can be used the administrator menu to hide the select local site screen.
It can be used the administrator menu to disable the addition, editing, and deletion of local sites on the select local site screen.
Select Local Site Function
Outline of Local Site Settings
The same unit can be used in multiple meeting rooms without the need to change the network or connection mode settings.
Up to 10 local sites can be registered.
The system will restart automatically when changing connection mode.
The system operation after restarting will be different depends on setting of “Same setting after restart”.
  ON: Setting contents will be remain right before restarting.
  OFF: Setting contents back to default.
Setting menu of Select Local site (Admin. Menu))
Setting menu of Select Local site (to Add)

## Slide 52
Page 51
Case 1: Use one HDVC in different meeting room
Easy to change network settings depends on meeting room.
HDVC (Remote site)
HDVC (Local Site)
Meeting Room A
192.168.1.1/24
Select Local Site
HDVC (Local Site)
Meeting Room B
192.168.11.1/24
Case Study of Select Local Site Function
HDVC (Local Site)
HDVC (Remote site A)
HDVC (Remote site B)
Select Local Site Function
Case 2: Change Encryption Key depends on Remote site
Easy to make secure communication depends on remote site.
Enc. Key: 1111
Enc. Key: 2222
Select Local Site
In IP mode
In NAT Traversal mode
HDVC (Local Site)
HDVC (Remote site A)
Select Local Site
Mobile for Windows (Remote site B)
In IP mode
In NAT Traversal mode
Case 3: Use IP mode and NAT Traversal mode depends on Remote site and use devices of Remote site.
Case 4: Change Network setting depends on connection pattern and use protocol of Remote site.
Other VC system
(H.323)
IP mode, H.323
Internet and with Static NAT setting
HDVC (Local Site)
Select Local Site
HDVC (Remote site)
IP mode,
INTRANET

## Slide 53
Page 52
Panasonic Recommended Routers
Maker / Model | DRAM / flash | IOS | Feature Set/License
CISCO 1812 | 256MB/64MB | 12.4(24)T2 | ADVANCED IP SECURITY
CISCO 892-K9 | 256MB/64MB | 15.0(1)M3 | ADVANCED SECURITY
CISCO ISR 1841-SEC/K9 | 256MB/64MB | 12.4(24)T2 | ADVANCED SECURITY
CISCO ISR 2801-SEC/K9 | 256MB/64MB | 12.4(24)T2 | ADVANCED SECURITY
CISCO 1921-SEC/K9 | 256MB/64MB | 15.0(1)M3 | IP Base License + Security License
CISCO 1941-SEC/K9 | 256MB/64MB | 15.0(1)M3 | IP Base License + Security License
As of Nov. 2014
CISCO 1941
CISCO 2951
CISCO 892
The following routers are Panasonic recommended routers especially for center site of Multiple connection, MPCS server site and for VPN connection.
Note: In case of CISCO routers, port 5100 cloud be used. If communication cannot be made, try to use alternative port instead of port 5100.

## Slide 54
Page 53
Router Selection (Reference)
The following is reference to select suitable router depends on use case.
In case of VPN connection in IP mode
Max. Bandwidth Settings | VC1300 (4 sites) | VC1600 (6 sites) | VC1600 (10 sites)
4M | CISCO892 | CISCO892 | CISCO1941
9M | CISCO892 | CISCO892 | CISCO1941
18M | CISCO1941 | CISCO1941 | CISCO1941
In case of NAT Traversal Service mode
Max. Bandwidth Settings |  | VC1300 (4 sites) | VC1600 (6 sites) | VC1600 (10 sites)
4M | NAT Traversal mode / IP mode | CISCO892 | CISCO892 | CISCO1941
 | NAT Traversal mode only | CISCO892 | CISCO892 | CISCO1941
9M | NAT Traversal mode / IP mode | CISCO892 | CISCO892 | CISCO1941
 | NAT Traversal mode only | CISCO892 | CISCO892 | CISCO1941
18M | NAT Traversal mode / IP mode | CISCO1941 | CISCO1941 | CISCO1941
 | NAT Traversal mode only | CISCO1941 | CISCO1941 | CISCO1941

## Slide 55
Network specification required for tenders：IPv6 （IPv6 shall become necessary for VC system for tenders）
IPv6 supporting situation |  |  |  |  | 
 | Panasonic | SONY | Polycom | CISCO | Lifesize
CODEC | VC1600 VC1300 | XG100 XG77 XC1 | Group700 Group500 Group300 | SX80 SX20 C40 | Room220 Team220 Express220
IPv6 | ○ | ○ | ○ | ○ | ○
HDVC support dual stack of IPv4 and IPv6.
All VCS supplier support IPv6 with their main model.
VC1600/VC1300
Ver4.2
What is IPv6？ Internet Protocol Version 6
Technical solution for IP address depletion
IPv4 IPv6
・Following service does not support IPv6.
NAT Traversal Service mode, ALM, Version up via network (firmware download) # These service work with IPv4, even if IPv6 is set.
IPv6 Support
Page 54
This is new!

## Slide 56
While applying two mode, IP mode/inside and NAT Traversal mode/outside, by using dual network function, following encryption setting can be done. IP mode(SIP)/inside : no encryption, NAT Traversal mode(SIP)/outside : encryption
# Static NAT(SIP) is treated same as IP mode.
＜So far＞
＜Ver4.2＞
[Encryption for IP/NAT Traversal mode] ・Encryption（SIP)：On/Off ・Encryption key（SIP）:max.256 character
[Encryption for IP/NAT Traversal mode] ・Encryption（SIP)：On/Off ・Encryption(NAT Traversal mode) : On/Off ・Encryption key(SIP/NAT Traversal) : max.256 character
It is essential to set encryption ON at all inside site, if encryption is set to ON due to NAT Traversal Service use.
It is possible to set encryption ON for NAT Traversal mode and to set OFF for inside site.
Intranet VPN
HDVC connection
Service
Internet
VC1600
Encryption : ON
LAN1
LAN2
Communication carrier
Inside
Outside
Encryption：ON
Intranet VPN
Internet
VC1600
Encryption : OFF
LAN1
LAN2
Communication
carrier
Inside
Outside
Encryption : ON
# Same as dual network with 1NIC
# It is impossible to set separately for IP mode and NAT Traversal mode.
# It is possible to set separately for IP mode and NAT Traversal mode.
HDVC connection
Service
# Same as dual network with 1NIC
Encryption Improvement in SIP
This is new!
Page 55

## Slide 57
Thank You !
Panasonic System Networks Co., Ltd.
Security System Business Division