## Slide 1
ALM
(Application Layer Multicast)
1. This document can be disclosed to Panasonic Sales Partners 2. The specs might be changed without notice since it’s still under development.
Panasonic System Networks Co., Ltd.
Security System Business Division
For Panasonic Sales Company and Business Partner only
Ver.4.20

## Slide 2: History of Revision
Doc. Ver. | Contents | Date of Issue | Remarks
Ver. 4.20 | Issue of First Edition | Aug. 2015 | 
Page 1

## Slide 3
Page 2
Outline
NW Cost Saving
High Video/Audio Quality
Easy Operation
Provide High Video and Audio Quality with Full HD Resolution same as ordinary videoconferencing.
Server less solution
Stress Free for Network with unique Multicasting method (Application Layer Multicast)
Easy Operation by HDVC’s Remote Controller
Easy creation of Multicast Tree
Multicasting Solution by using HD Visual Communication.
Up to 30 sites with Full HD Resolution
Cost saving of Network (Server less, Min. Bandwidth Requirement: 2Mbps/site for FHD)

## Slide 4
Page 3
Page 3
Category | Place |  | Video Delivery (Multicast) | Video Transmission
Business Enterprise (Manufacture, Finance, Construction） | Office |  | ◎ | 
 | Factory |  | ◎ | 
 | Construction site |  | ◎ | △
 | Bank |  | ◎ | △
 | Communication Station |  |  | ◎
 | Broadcasting Station |  |  | ◎
Government | Government Office |  | ◎ | 
 | Police Dept. |  | ◎ | 
 | Fire Dept. |  | ◎ | 
 | Prison |  |  | ◎
 | Court |  |  | ◎
Service Business (Outlet, Distribution) | Hotel |  | ◎ | ○
 | Party Hall |  | ◎ | ◎
 | Casino |  | ○ | ◎
 | Distribution Center |  | ◎ | ○
 | Railway Station |  | ◎ | ◎
 | Airport |  | ◎ | ◎
Medical | Hospital |  | ○ | 
 | Nursing Care Facility |  |  | 
 | Home Care |  |  | 
Education | School |  | ◎ | 
 | Cram School |  | ◎ | ◎
 | Training / Church |  | ◎ | ◎
Others | House |  |  | 
 | Parking Area |  |  | △
Target Customer
Video Delivery Market
Office
Office
HQ
Multicast
Multicasting System
Cram School / Internal Training
Remote Lecture
Remote Education System
Vertical (Education) Market
Church Market
Branch
Branch
Multicast
・・・
教会

## Slide 5
Page 4
Use Case 1
The Vision of Company president and Company’s Goal can transmit to each employees in real time
1
2
Morning Assembly / Policy Meeting
Camera
Microphone
HDVC
Projector
Screen
Internet
Router
Head Quarters
Branch Office A
Branch Office B
Local Office A
Local Office B
Local Office C
Local Office D

## Slide 6
Page 5
Use Case 2
Explanation of New Product and Internal Staff Training can be made to share the information easily with branch office.
Remote Education / Company Internal Training
Camera
Wireless
Microphone
HDVC
Projector
Screen
Router
Internet
Branch Office A / Branch School A
Branch Office B / Branch School B
Head Quarters / School

## Slide 7
Page 6
1
2
5
6
Camera
Microphone
4
3
15
16
17
18
19
20
21
22
23
24
25
26
27
28
HDVC
11
12
13
14
10
7
8
9
System & Network Outline
Projector
Screen
Internet
Router
29
30
Features: Up to 30 sites Multicast / Add, Escape and Reconversion of Multicast Tree
Supported Connection Mode: IP mode (Not supported for Static NAT and NAT Traversal Service mode)
Recommended Network: Intranet, VPN (Closed Network) *Encryption is not supported.
Distribution Method: Bucket bridge (IN x 1, OUT x 2)
Connection Method: Full Mesh
License: Required at all sites (KX-VCS302)
Max. Video Quality: Full HD (1080p)
Minimum Required Bandwidth:
1Mbps / site for HD, 2Mbps / site for Full HD

## Slide 8
Page 7
Network Requirement
Full Mesh Type Network
Branch Office A
Branch Office B
VC1600
HQ
Sales Office A
Sales Office B
Branch Office C
Sales Office C
Intranet
(Closed Network)
When trouble is occurred
(Re-establish the multicast route)
Branch Office A
Branch Office B
VC1600
HQ
Sales Office A
Sales Office B
Branch Office C
Sales Office C
Disconnect
Change Multicasting route
Intranet
(Closed Network)
（フルメッシュ型ネットワークが必須です）
Full Mesh Type Network is essential.
It is adapting two trees distribution structure for making Multicast route (Multicast Tree).
Note: When trouble is occurred during connection such as network failure, fixed route multicasting method can not be guaranteed to re-establish the multicast route (multicast tree) and keep connection. Full Mesh does support.

## Slide 9
Page 8
Network (Multicast Tree and Node)
< Multicast Tree >
It is defining the arrangement of the terminals in the one-way multicasting system
Distribute Video + Audio data / Arrangement of the receiving and relay terminals
Configuration: Max.31 sites (Distribution terminal: 1 system, Relay / Receiving terminals: 30 systems, up to 5 levels)
Performs the data transfer between the respective terminal in bucket bridge, therefore the initial route must be determined before starting connection.
When the trouble is occurred during connection:
  When the relay terminal is disconnected during connection due to network failure so on, the system automatically re-establish multicast tree to keep connection.
Terminal Type | Description
Distribution Terminal | Node of the Top, distribute video and audio data.
Relay Terminal | Relay (Transfer) received video and audio data from the upper node to the lower node.
Receiving Terminal | Receive video and audio data from the upper node.
< Multicast Setting File >
Available Settings: GUI or Web Console
Multicast Tree (Initial Distribution Route): Up to 10 different multicast trees can be set
Max. IP rate and Max. Resolution, etc.
Interface Setting of the distribution site (XML format)
Relationship of Multicast Tree and Node Positioning

## Slide 10
Page 9
Network (Multicast Tree and Node ID)
Distribution Terminal
1
2
3
5
4
6
Multicast Tree: 0-30
Distribution Terminal: 0
Relay Terminals: 1-14
Receiving Terminals: 1-30
11
7
13
9
< Node ID >
Distribution terminal position of the multicast tree is displayed in the Node ID
8
12
10
14
15
23
19
27
17
25
21
29
16
24
20
28
18
26
22
30
Node ID: 0
Receiving Terminals
Relay Terminals
Max.31 sites (Distribution terminal: 1 system, Relay / Receiving terminals: 30 systems, up to 5 levels)

## Slide 11
Page 10
Network (Multicast Tree and Node ID)
1
2
3
5
4
6
7
11
9
13
8
12
10
14
Upper node of terminal 5: Terminal 0 and 1
Lower node of terminal 2: Terminal 4,6,8,12,10 and 14
Guest node of terminal 6: Terminal 10
Host node of terminal No.7: Terminal 3
Node | Description
Host node | Distribute or Transfer video and audio data to own site terminal
Guest node | Destination terminals to distribute or transfer video and audio data
Upper node | Distribute or Transfer video and audio data to own site terminal or the Upper node of the Host node to be transferred
Lower node | Distribute video and audio data, or guest node of the destination to be transferred, or lower node of the guest node
Node ID Relationship
Node ID: 0

## Slide 12
Page 11
Bandwidth and Resolution, Audio Codec
Supported Resolution: 1080p and 720p only
Does not support for 1080i.
However, 1080i receiving is possible as receiving or relay terminal.
Max. Resolution Bandwidth | Full HD (1080/30p) | HD (720/60p)
5Mbps | ○ (Recommended) | 
4Mbps | ○ (Recommended) | 
3Mbps | ○ (Recommended) | 
2Mbps | ○ (Recommended) | ○ (Recommended)
1.2Mbps |  | ○ (Recommended)
1Mbps |  | ○ (Recommended)
Relationship between Bandwidth and Max. Resolution
< Audio Input >
Distribution site: Microphone’s pickup will be monaural sound.
(L/R separate input is possible from RCA input)
Relay / Receiving site: It will be invalid during distribution due to one-way multicast distribution.
< Audio Output >
Distribution site: Audio output is disabled.
Relay / Receiving site: Same as normal mode.
Bandwidth | Audio Codec
4Mbps and above | AAC-LD (96Kbps×2ch)
4Mbps below | AAC-LD (64Kbps×2ch)
Always it will be output in 2 channels
(L/R separate input is possible from RCA input)
Relationship between Bandwidth and Audio Codec
< Important >
Recommended bandwidth described in the left diagram is for receiving only per site. For the case of the distribution, bandwidth requirement will be double. Because the host terminals distribute the data to two guest terminals at same time.

## Slide 13
Page 12
< Notice >
During connection, it can not be made any calling / receiving from receiving and relay terminals.
(Embedded MCU function does not work when the system in ALM function mode.)
ALM function does not support dual stream.
Distribution site: Display only own site
(When PC content sharing is made, display own PC content)
  Single Monitor : Own site
  Dual Monitor : Own site + Own site (Clone image output)
Relay / Receiving site: Display only received image
  Single Monitor : Remote site
  Dual Monitor : Remote site + Remote site (Clone image output)
Available Resolution of HDMI output:
  VC1600 HDMI1: Depends on settings, HDMI2: 1080i
  VC1300 HDMI1: 1080p, HDMI2: 1080i
Screen Layout
Available Screen Layout

## Slide 14
Page 13
    Multicast Tree Settings (Create initial distribution route)
    Preparation for Distribution (Connection Check (Call-over))
    Data Distribution Start
    End
Start data distribution automatically when all terminals are answered.
(Even if all terminals could not answer, the system will re-try
in 90 sec. by re-establish Multicast Tree.)
Send distribution route information (Data receiving terminal, Transferred terminal)
Command distribution start
Start AV stream transfer
Choose Multicast Tree, then press “Start” button.
=> Start Call over
(Press “End” button to cancel Call Over)
Create Multicast Tree and setting files
Press “End” button
Command distribution end (End AV stream transfer)
Distribution Terminal
Delivery Incoming: Sound ringtone once at the time of call reception (Auto Answering)
Reply incoming response to distribution terminal
(It will be manual answering while system in stand-by or other
than Home screen)
Move to distribution mode
End receiving / transfer, then back to normal mode
Receive distribution route information
Prepare for receiving / transfer (Response reply)
Start a bucket relay delivery
Operation Flow
Receiving / Relay Terminal
    * The system not in the Multicast Tree file can not join when starting call over is conducted.
* Receiving / Relay terminal can not disconnect themselves by remote controller to avoid operation mistake by receiving / relay terminal site.

## Slide 15
Page 14
Abnormal detection
If the receiving terminal is abnormally detached, the system re-establish multicast tree to the guest terminals to continue distribution.
  The distribution terminal detect abnormal condition (Power down, Network failure, etc.) of the receiving terminals by ALM heartbeat function after starting distribution. The distribution terminal detect receiving terminal in abnormal if the receiving terminal can not receive the data in certain period times (Interval / The number of Retries: each 250ms / 15 times), then remove from delivery target as abnormal withdrawal.
If the receiving terminal can not receive video / audio data in 60 sec., exit the delivery reception to migrate to the normal mode.
1
2
3
5
4
6
7
11
9
13
8
12
10
14
Terminal 13 upgraded as host node
1
2
3
5
4
6
7
11
9
13
8
12
10
14
Node ID: 0
Distribution Terminal
×
Terminal 5 Abnormal Withdrawal
×
Manage all receiving terminals by ALM Heartbeat Function
If the abnormal withdrawal terminal was relay terminal, distribution route under the its relay terminal will be changed.
  Bigger node number’s terminal will be upgraded as host node.
Although video is displayed stopped for a while, it will be retuned right after changing distribution route is completed.
Receiving Terminal Abnormal Withdrawal
Node ID: 0
Distribution Terminal

## Slide 16
Page 15
1
2
3
5
4
6
7
11
9
13
8
12
10
14
Terminal 5 Recovered
○
1
2
3
5
4
6
7
11
9
13
8
12
10
14
The terminal with abnormal withdrawal will automatically recover and receive the data by ALM Heartbeat Function of the distribution terminal when the system is back to normal condition.
  It is automatically assigned to the lowest node number that is a free of the multicast tree.
The system with following conditions can not be made automatic recovery.
  Manually disturbed, Version Mismatch, Encryption Enable, Other VC endpoint, Forced withdrawal from distribution terminal (Delete from the multicast tree) / Non-activated terminal / Any other connection failure, etc.
Terminal 5 Recovered
○
Receiving Terminal (Automatic Recovery)
Automatic Recovery
Node ID: 0
Distribution Terminal
Node ID: 0
Distribution Terminal
Manage all receiving terminals by ALM Heartbeat Function
Terminal 13 upgraded as host node
Terminal 13 upgrade as host node

## Slide 17
Page 16
Multicast Tree Settings: Go to “Admin Login” => “Multicast Settings”
Menu | Content / Remarks
Multicast Name | Setting of Multicast Tree Name
Max. Bandwidth | 5,4,3,2,1.2,1Mbps
Max. Resolution | Full HD / HD
Multicast Default Video | Main Camera / Sub Camera / PC
Multicast Def. Noise Reduction | ON / OFF
MIC detection | ON / OFF
IP Address | Input IP Address
Target | Change to registration screen
Up to 10 Multicast Tress can be set
Menu | Content / Remarks
No. | Choose Multicast Tree destination can be distributed.
Multicast Name | Setting of Multicast Tree Name
Choose specific created Multicast Tree and press “Start” button, then distribution will be started.
Note:
Both LAN1 and LAN2 interface can be used for ALM function on VC1600.
But suimaltinious operation is not supported.
Routing setting is required when LAN2 interface is used.
GUI Image (Multicast Tree)
Multicast Tree Sel.
Multicast Tree Sel.
Multicast Name
Multicast Name
Max. Bandwidth
Max. Resolution
Multicast Default Video
Multicast Def. Noise Reduction
MIC detection
IP Address
Target

## Slide 18
Page 17
Menu | Content / Remarks
Selection | Choose Multicast Tree destination can be distributed.
Node ID | Position of Multicast Tree inside
Multicast Target | Display site name
Menu | Content / Remarks
Multicast Target Mame | Input Site Name
IP Address | Input IP Address
Registration Procedure:
Input IP Address (Direct input)
Import from Address Book
Applicable (Supported) IP Address Information:
IP Address with IPv4 style and SIP protocol
* Non supported IP Address information will be displayed with
gray out in the address book list.
Up to 30 sites can be set
GUI Image (Multicast Tree)
Multicast Tree Settings: Go to “Admin Login” => “Multicast Settings”
Multicast Tree Sel.
Multicast Target
Node ID
Select.
Multicast Target
Multicast Target Name
IP Address
Input IP Address
Import Add. Book

## Slide 19
Page 18
Display connection status of the each site
(You can check the connection status display of each site by pressing [Site] (Green button))
Screen of Connection Status
[Back to Previous Menu]
[Choose site where you want to check the status]
It can be confirmed such as transmit resolution, transmit frame rate and connection status from the remote site.
(Display receiving connection status from one upper level terminal of the multicast tree.)
Menu | Content / Remarks
Multicast Target | Distribution Site Name
Node ID (Set / Current) | Assigned Terminal ID in Multicast Tree file / Position of the Multicast Tree by node ID
Video Loss (Host / Multicast Term.) | Link loss ratio of video from the host terminal / Total loss ratio of video from distribution terminal
Audio Loss (Host / Multicast Term.) | Link loss ratio of audio from the host terminal / Total loss ratio of audio from distribution terminal
RTT | Estimated RTT value from the host terminal
Jitter | Jitter from the host terminal
Receive Rate | Reception IP rate (Average )
Link Used | Display node ID of the host / guest terminal
GUI Image (Connection Status)
Connection Status Display: Go to “Admin Login” =>
System info.
System info.
Multicast Target
Node ID (Set/Current)
Video Loss (Host/Multicast Term.)
Audio Loss (Host/Multicast Term.)
RTT
Jitter
Receive Rate
Link Used

## Slide 20
Thank You !
Panasonic System Networks Co., Ltd.
Security System Business Division