## Slide 1
MPCS
(Multi-points Connection Software)
Version 2.00/2.10
1. This document can be disclosed to Panasonic Sales Partners 2. The specs might be changed without notice since it’s still under development.
Panasonic System Networks Co., Ltd.
Security System Business Division
For Panasonic Sales Company and Business Partner only

## Slide 2: History of Revision
Doc. Ver. | Contents | Date of Issue | Remarks
Ver. 2.00/2.10 | Issue of First Edition | Nov. 2014 | 
Page 1

## Slide 3
Page 2
Table of Contents
MPCS Specification Detail
3
Overview of MPCS
1
MPCS Key Feature Overview
2
MPCS Settings
4
MPCS Operation
5
Linux Installation
6
MPCS Installation
7

## Slide 4
Page 3
One Concurrent Conference Room for IP Mode and NAT Traversal Service (Easy Connection) mode. IP Mode and NAT Traversal Service (Easy Connection) Mode work simultaneously. (New)
Two-encoder accommodates lower and higher bandwidth endpoints simultaneously. (New)
Up to 16 Participants in a Conference Room.
HDVC, Android/iOS and PC Application are supported. (New)
Panasonic Proprietary Solution. (Other vendor’s VCs are not tested)
Two Conference Room Operation mode are available
Normal Mode:
  Permission required to join to the conference in advance. Various Conference Operations are supported for Administrator while Conferencing.
Ad-Hoc Mode:
  Anybody can join to the conference. Available Conference Operations for Administrator are Show/Hide site name and Dial in / Dial out only.
Available access Interface
Web Console and API (External Control Interface) are available.
MPCS Ver.2.0/2.1 provides simple Multi-Party Conferencing environment to HDVC network.
MPCS Key Features Overview

## Slide 5
Page 4
MPCS
Server
Mobile Solutions
HDVC
HDVC
HDVC
2. Integrated two images
3. Send Integrated images
Star Network Diagram provides effective bandwidth usage
Target Network is Internet, Intranet and VPN
Both IP and Easy Connect Mode supported simultaneously.
1. Higher bandwidth devices send HD image.
Image for
HD Endpoint
Image for SD Endpoint
4. SD image sent to lower bandwidth devices
1. Lower bandwidth devices send SD image
4. HD image sent to higher bandwidth devices
Network
System Diagram Overview (Two Encoder)

## Slide 6
Page 5
NAT Traversal Servers
Mobile Solution
HDVC
SIP
Router
WiFi Router
WiFi Router
Mobile Solution
HDVC
MPCS V2.0
LAN
Corporate Network
Router
Mobile Solution
WiFi Router
HDVC
IP Mode Video/Audio
NAT Traversal Service Video/Audio
IP Mode
MPCS provides HDVC Mobile Solution Multi-Party Conference environment
System Diagram Overview (IP mode + NAT Traversal Service)

## Slide 7
Page 6
System Outline
1. Improve multi-Point connection AV quality
HD (High Definition) AV quality @512kbps (Lower Bandwidth Operation)
AV-QoS makes system configured with Internet with reducing network cost.
Supports Dual Speed with eliminating influence from lower speed network sites.
2. Easy 16 sites connection of HDVCs and Tablets
Participate meetings via tablets on business trip in easy & economical manner.
HDVC in Intranet can easily be connected to outside via NAT Traversal Service.
Support Dual Networks to communicate with internal Intranet & outside Internet.
Head Office
Multi-Points Connection MPCS Ver.2.0/2.1
Internet
Intranet IP-VPN
Branch Offices
Overseas
Offices
Business
Customers
HDVC mobile
Max. 16 sites with HD quality, One Meeting Room
SD Image
HD Image
Tablet / Smart Phone (Android Terminal)
WiFi/4G-LTE/WiMax
Note
HDVC mo bile also support IP mode connection
Easy Connection
Dual
Network
NAT Traversal
Max.
16sites

## Slide 8
Page 7
System Outline (Multi-point Connection)
Internal Intranet
(VPN network)
Multi-Points
Connection MPCS
HDVC
Head Office
Max. 16 sites Connection
(One Meeting Room)
Branch
Office
HDVC
HDVC
Wireless LAN Access Point
Tablet
Smart Phone
HDVC Mobile
Select line-up to meet customer’s needs
Router
Router
Router
Internet
Sales Office
HDVC
Mobile
IP Mode
NAT Traversal
Service Mode
NAT Traversal Service
Router
Router
@Own Desk | Meeting Space | Conference Room
Smart Phone (Android / iOS) | Tablet / Windows PC | HDVC

## Slide 9
Page 8
System Outline (Multi-point Connection AV Quality)
360
240
Provide HD quality @512kbps lower bandwidth per site (MPCS transmission rate) in Multi-Points Connection operation.
Multi-Points
Connection （MPCS）
HDVC
Intranet/VPN
or
HDVC” Easy Connection” Service
This function works together with MPCS Ver.2.0/2.1 and HDVC ver.3.1 onward. HDVC mobile Ver.2.0 will be connected in SD quality and H.264 baseline profile.
HDVC@720p image
HDVC@4SIF image
HDVC Mobile @QVGA (Horizon)
HDVC Mobile @QVGA (Vertical)
640
480
320
270
<4 partition(CP4)Screen Image>
SD, HD Image : Composed image of different definition will be displayed to adapt Dual Speed or multi definition images.
HDVC
<Required bandwidth at MPCS center site>
Ver.1.0 : 1Mbps x 16 sites = 16 Mbps
Ver.2.0/2.1 : 512kbps x 16 sites = 8Mbps
Provide HD quality with half of bandwidth Required.
1280
720
HD Quality (720P)
AV quality improved by H.264 high profile. Router load also reduced with less packet process.
HDVC
HD Quality @512kbps
Note: in case combination use of HDVC mobile V.2.0 or HDVC V3.0 (or earlier), H.264 base line operation to be applied.
NAT Traversal Service

## Slide 10
Page 9
System Outline (Multi-point Connection AV Quality)
HDVC core technology, AV-QoS works on multi-Points connection for better AV quality & stable internet connection.
Multi-Points connection software (MPCS) Ver.2.0/2.1 supports dual networks. IP mode and NAT traversal mode works simultaneously. AV-QoS works on both networks.
Multi-Points
Connection Software
（MPCS）
HDVC
This function works together with MPCS Ver.2.0/2.1 and HDVC ver.3.1 onward, and won’t work at combination use of HDVC mobile Ver.1.0 nor HDVC Ver.3.0 (or earlier version).
Note FIR QoS control will be applied at combination use of HDVC mobile Ver.1.0 or HDVC Ver.3.0 (or earlier version).
<Bandwidth Estimation>
This is a core technology to prevent packet loss and to minimize AV data cut-off nor block noise.
AV-QoS Technology
Note Although HDVC QoS applies FEC as packet loss recovery technology, this FEC won’t be applied for multi-points connection (MPCS) in order to improve AV quality at lower bandwidth operation.
Note MPCS TX resolution and frame rate is fixed, and it controls AV quality based on bandwidth.
HDVC
HDVC
Intranet/VPN
HDVC Easy Connection Service
NAT Traversal Service
Available Bandwidth
With control
Adjust TX data Rate
with NW congestion
No control
TX data excess BW
at NW congestion
Packet Loss
Congestion
Congestion
Congestion
time
<ARQ (Packet re-send control>
Core technology to re-transmit lost packet and to prevent AV cut-off or block noise.

## Slide 11
Page 10
System Outline (Multi-point Connection AV Quality)
Optimize AV quality when low band width sites or mobile terminals are in multi-points connection. (HD, SD mixed)
  MPCS automatically analyzes bandwidth from each terminal, and adjusts image quality in such HD for HDVC or SD for HD mobile. Resolution of HD or SD can be assigned for each screen layout (CP1 to CP16).
SD and HD Encoder selection will be done as following.
  HDVC Mobile for Android/iOS will be connected to SD encoder regardless of its bandwidth settings.
  HDVC and HDVC Mobile for Windows will be connected to the encoder based on their bandwidth settings.
  If HDVC and HDVC Mobile fro Windows bandwidth settings are above HD encoder setting, they will be connected to HD encoder.
  If not, they will connected to SD encoder. If endpoint bandwidth setting is lower than 256kbps, the endpoint can not connect to MPCS.
Multi-Points Connection (MPCS)
HDVC
Mobile
HDVC
HD Image
SD image
Narrow Bandwidth
Wide Bandwidth
Ex : CP4
Ex : CP8
Recommended is to set overseas HDVC (usually low BW) in SD group. HDVC mobile to be connected in SD group.
Resolution | BW setting | TX resolution | QoS apply
HD | 2Mbps – 512kbps | HD(720p)/30fps | 512kbps or up
SD | 1.5Mbps – 374kbps | SD(w432p)/20fps | 256kbps or up
Note SD image BW setting needs to be lower than HD image BW setting. (HD 720p : 1280 x 720, SD w432p : 768 x 432)
MPCS requires BW need to be set for each of HD and SD connection.
HD or SD setting won’t be changed during communication.
PC resolution | VGA | SVGA | HD, XGA, WXGA1/2
HD | 640 x 480 | 800 x 608 | 1280 x 720
SD | 640 x 480 | 640 x 480 | 768 x 432 (w432p)
Note: PC image of contents sharing to be re-sized in resolution above.
Note: HD or up of PC image sharing requires HDVC ver.3.0 or up.

## Slide 12
Page 11
System Outline (Multi-point Connection AV Quality)
Multi-Point SW (HDVC-MPCS)
B/W set : 1Mbps
HDVC
B/W set : 2Mbps
Connection
@1Mbps
Described below is the relationship between bandwidth and resolution of Multi-Point Connection SW (MPCS) by dual speed HD group and SD group.
2M
1M
Line Rate
IP Rate
600K
1.16M
2.3M
1.75M
HD(720p)
30fps
1M
2M
512K
1.5M
< HD Resolution Group >
1.5M
512K
Line Rate
IP Rate
458K
600K
1.75M
w432p
20fps
512K
1.5M
384K
< SD Resolution Group >
Available BW Setting : 512Kbps - 2Mbps
Available BW Setting : 384Kbps - 1.5Mbps
Multi-Point SW
(HDVC-MPCS)
Resolution : HD Bandwidth : 1Mbps
Resolution : SD Bandwidth : 512kbps
HDVC
Bandwidth 2Mbps
Bandwidth 512kbps
Resolution and frame rate of MPCS TX image are fixed, and it controls image quality based on the bandwidth.
Equal or lower than SD group BW setting SD resolution Group
Equal or higher than SD group BW setting HD resolution group
Bandwidth per site
Bandwidth per site

## Slide 13
Page 12
System Outline (Multi-point Connection AV Quality)
Consider the combination below as MPCS Ver.2.0/2.1 basic system configuration.
Multi-Points Connection SW (HDVC-MPCS)
HDVC
Ver.3.1 onward
Ver.2.0/2.1
HDVC Mobile
Ver.2.0 onward
＋
＋
Note: Ver.3.0 or earlier version of HDVC (includes VC500) can be connected to MPCS, but under some condition applied. Note: HDVC mobile Ver.1.0 can not be connected to MPCS Ver.2.0/2.1.
Described below are major conditions applied to connect HDVC Ver.3.0 or earlier version (includes VC500).
These particular HDVCs can’t send HD image at 512kbps, the resolution on the other side come down.
AV-QoS to provide stable connection on internet won’t work.
MCPS TX image to these particular HDVC will be via H.264 baseline profile, then won’t provide improved quality of image.
TX packet amount to MPCS won’t be decreased, then load on MPCS center router won’t be reduced.

## Slide 14
Page 13
System Outline
Provides up-to 16 sites of HDVCs and tablets multi-points video conference.
  MPCS Ver.2.0/2.1 will provide multi-site tele-conference not only with HDVC but with tablets, smart phones and Windows PC.
Multi-Point SW
(MPCS)
HDVC
Intranet/VPN
HDVC
HDVC Mobile
Wi-Fi AP
Up-to 16 of HDVC and Mobile
HDVC mobile Ver.2.0 onward supports IP mode connection.
Tablet, smart phones and Windows PC will work under intranet or
VPN network like HDVC via Wi-Fi connection.
HDVC-Mobile also can join MPCS multi-site conference.
This function works together with MPCS Ver.2.0/2.1, HDVC, and HDVC-Mobile Ver.2.0 onward.
(For HDVC, recommended is to up-grade to Ver.3.1 or later version.)
Note: Communication between HDVC-Mobile need to be via MPCS.
Note: Recommended is IEEE802.11n for HDVC-Mobile Wi-Fi connection.
Note: HDVC-Mobile connection will be in SD image group.
Wireless is the maximum benefit of Tablet or Smart Phones. Join the meeting from anywhere your are.
In addition, many valuable information and image can be shared from its out-sight camera.

## Slide 15
Page 14
System Outline
Multi-Point
Communication Software （MPCS）
HDVC
HDVC
HDVC Mobile
“NAT Traversal / Easy Connection” service. now supports Multi- Points Connection (MPCS). Register activation key as same as HDVC.
Multi-Points Connection (MPCS) requires network bandwidth concerned design as a center machine.
Each of MPCS and HDVC requires confirmed router for “NAT Traversal / Easy Connection” service.
通信キャリア
MPCS/HDVC $30.00/month/unit
HDVC mobile $2.50/month/unit
Ask dealers for exact pricing
“NAT Traversal / Easy Connection” service price reference
Assigned one Terminal ID to MPCS
Up-to 16 sites multi-point conference is available also with HDVC “NAT Traversal / Easy Connection” service.
  With using “NAT Traversal / Easy Connection” service, Tablet terminals or smart phone can join to MPCS multi-points conference from outside via carrier service.
Up-to 16 of HDVC and Mobile
This function works together with MPCS Ver.2.0/2.1, HDVC, and HDVC-Mobile Ver.2.0 onward.
(For HDVC, recommended is to up-grade to Ver.3.1 or later version.)
Intranet/VPN
NAT Traversal Service

## Slide 16
Page 15
System Outline
Multi-Points Connection (MPCS) supports dual operation of Intranet/VPN and “NAT Traversal / Easy Connection” service.
  As example, Intranet/VPN is dedicated for internal HDVC connection, and use “Easy Connection / NAT traversal” service via Internet for outside connection, such as overseas sites, customer’s sites, or HDVC mobiles on business trip.
HDVC
Intranet/VPN
Wi-Fi AP
HDVC
HDVC
HDVC mobile
HDVC
“Easy Connection” Service
ISP
LTE/WiMAX/ Wi-Fi
overseas
customer
Operation by IP address
Operation by Terminal ID (7-digits)
Inter-connection
Bandwidth concerned NW design required as a center machine.
One terminal ID (7-digits) to be assigned.
Note: 2 NICs (LAN ports) are required for this dual NW operation.
Inter-connection via MPCS
No connection between HDVC mobiles only.
NAT Traversal Service
Multi-Points Connection (MPCS)
HDVC
HDVC mobile

## Slide 17
Page 16
System Outline (Others)
Other features for Multi-Points Connection System (MPCS) are described below.
Ad-hoc mode dial out function by remote control operation
Once a moderator calls into MPCS meeting room, he/she can dial out to pre-assigned profile members (max. 10 profiles) by remote control operation. At the end of the conference, he/she also can have all members disconnected by remote control operation.
<Operation>
Dial out : While a moderator is connected to MPCS, dial #101～110 from a remote controller.
Disconnect : a moderator to dial #199 from a remote controller.
Note : It is required to pre-assign attendee’s IP address in the MPCS profiles. (#101-#110, max.10 profiles)
Note : It is possible to re-access same profile number in case that there is any un-answered attendees.
Note : Even after a meeting starts by Web console operation, this function will be available.
Note : The profile numbers #101-#110 (max.10 profiles) can be accessed either by Web console or ad-hoc mode calling out function.
Encryption function during meetings
Encryption key can be set-up to prevent any un-authorized attendees join the meeting.
Only when the encryption key matches to the one on MPCS, HDVC or HDVC mobile terminals can
be connect.
This will be useful to secure security both for Intranet/VPN connection and for Internet connection.
Ad-hoc mode automatic start function
It is possible to set Ad-hoc mode automatic start mode, which is MPCS to be at Ad-hoc mode
when MPCS is booted up or re-started. This is useful when MPCS re-started right after power failure.

## Slide 18
Page 17
Max. number of registration members in one profile
Both for normal mode and for ad-hoc mode, max. number of registration members is expanded from 16 members to 32 members. At the ad-hoc mode calling out from profile, priority to dial will be from top to the bottom, or to the max. number of connection assigned by MPCS license.
Traffic display function
Sending and receiving bit rates, frame rates, resolution, and packet loss rate of the sites connected to the MPCS can be verified on the Web console screen.
SIP connection by TCP protocol in normal mode
In order to adapt to various routers, SIP connection by TCP protocol is also available.
(“NAT Traversal Easy Connection” service use TCP protocol.)
Dial out check all function
Check all connection sites when dial out from MPCS Web console becomes available.
External control interface commands
To be matched to MPCS Ver.2.0/2.1 additional functions, external control commands are added accordingly.
Web console adapted browser change
Browsers adapted to MPCS Web console are changed to IE8.0 （Windows7）、IE10 （Windows7 and8）、Firefox.
System Outline (Others)

## Slide 19
Page 18
MPCS Licenses
MPCS is a software Product. Registration Key is required for Activation.
The Registration Key can be obtained from KMS system.
KMS URL: https://eww.netreg.panasonic.co.jp/hdcomkms/pc/
Products | Main Unit | Notes
MPCS Activation Keys |  | 
“NAT Traversal / Easy Connection” Service Activation Keys |  | One activation key is required for one MPCS. IP mode and “NAT Traversal / Easy Connection” service Dual NW operation requires two NIC (LAN ports).
“NAT Traversal / Easy Connection” Service (HDVC Mobile for Android / iOS) Activation Keys |  | The software to be downloaded from Google Play / Apple Store as free of charge. IP mode only use also requires minimum one year activation key registration.
“NAT Traversal / Easy Connection” Service (HDVC Mobile for Windows) Activation Keys |  | The software to be downloaded from Pansonic.net web site as free of charge. IP mode only use also requires minimum one year activation key registration.
KX-VCM206 ( 6 sites)
KX-VCM208 ( 8 sites)
KX-VCM212 (12 sites)
KX-VCM216 (16 sites)
KX-VCMS001 (add. 4 sites)
KX-VCS701 (for 1 year)
KX-VCS703 (for 3 year)
KX-VCS711 (for 1 year)
KX-VCS713 (for 3 years)
Tablet /Smart Phone （Android / iOS）
HDVC
Multi-Points Connection Software (HDVC-MPCS)
Multi-Points Connection Software (HDVC-MPCS)
KX-VCS781 (for 1 year)
KX-VCS783 (for 3 years)
Windows PC

## Slide 20
Page 19
MPCS Specification
Item |  |  |  | Specification | Note
Concurrent conferencing |  |  |  | One Conference Room | Two encoder for Wide and Narrow bandwidth at same time.
Number of participants |  |  |  | Up to 16 | Panasonic HDVC, Panasonic PC Application and Panasonic Android/iOS application are supported.
Connection mode |  |  |  | IP Mode and NAT Traversal Service (Easy Connection) Mode | To activate both mode need two Network Interface Card.
Maximum bandwidth |  |  |  | 2.0Mbps(IP Rate) 1920kbps (Video) 80kbps (Audio) | 
Call control | Protocol |  |  | SIP (UDP and TCP) | TCP support is new feature at MPCS ver.2.0
 | Connection methods |  |  | Dial-in Dial-out by Web Console and API | 
Video | Tx | Video Codec |  | H.264 Baseline Profile Level 3.1 H.264 High Profile Level 3.1 | 
 |  | Video Resolution |  | 720p(1280x720) / w432p (768 x 432) | Maximum resolution and frame rate is 720@30p
 |  | PC Resolution |  | VGA, SVGA, XGA, 720p | 
 | Rx | Video Codec |  | H.264 Baseline Profile Level 1.3 thru 3.1 H.264 High Profile Level 3.1 | 
 |  | Video Resolution |  | 720p, 4SIF, w432p, w288p, VGA, QVGA | 
 |  | PC Resolution |  | VGA, SVGA, XGA, 720p | 
 | RTP format |  |  | Single NAL Unit Mode Non-Interleaved Mode | 
 | QoS |  |  | Yes for HDVC Ver.3.1 | 
 | Layout |  | CPN | CP1/CP4/CP6/CP8/CP10/CP13/CP16 | CP stands for Continuous Presence. The number represents the Number of Windows.
Audio | Audio Codec |  |  | G.722, G722.1C | 
 | RTP/cycle |  |  | 20msec | 
 | QoS |  |  | Yes for HDVC Ver.3.1 and Android App. | 
(*) When only one HDVC with version 2.2, 2.21 or 2.3 connected to the Conference Room, the unit will be disconnected in 30 seconds due to no video data transmission from the MPCS.

## Slide 21
Page 20
MPCS Specification
Item |  | Specification | Note
Encryption |  | Yes | 
Camera control |  | No | 
Screen layout | Layout | CP1 CP4 CP6 CP8 CP10 CP13 CP16 | 
 | What is displayed | Mixed video mode Video of participants is mixed and displayed. | MPCS integrates received image then send it to each participants. All participants receive same image.
 | Image switching | Voice Activated (VA) Fixed Layout (in order of arrival) Manual Control via Web/API Auto (Automatically changing the layout) | 
Web UI | Setting/Management | Basic settings of MPCS Conference management（Status Display, Profile management） Conference mode setting | 
 | Operation | Start a conference (Dial-Out) Terminate a conference Layout control Display location control | 
 | Log | Log download | 
 | Language | Japanese, English | Additional Languages are considered in future version
License management |  | By Activation Key | Function activation(6/8/12/16 ports), and additional 4 ports activation

## Slide 22
Page 21
MPCS Specification Detail
3
Overview of MPCS
1
MPCS Key Feature Overview
2
MPCS Settings
4
MPCS Operation
5
Linux Installation
6
MPCS Installation
7

## Slide 23
Page 22
Screen Layout Settings
1
1
1
2
3
4
Seven screen layouts are available based on settings and number of participants.
Screen Layout Option. Auto, Fixed and Manual available.
  Auto : System decides number of windows based on number of participants.
  Fixed : Admin. decide number of windows before start conference.
  Manual : Allow admin. to change while conferencing (Normal Mode only)
Displaying Position Option. Voice Activation, Fixed and Manual available.
  Voice Activation : Speaking party to 1st place (top left). Other party's location number decrement accordingly.
  Fixed : Participants placed in joined order????
  Manual : Admin. to change where to place while conf. (Normal Mode only)
1
2
5
3
4
6
7
8
9
10
11
12
13
14
15
16
5
6
7
8
2
3
4
1
2
5
3
4
6
7
8
9
10
11
12
13
1
2
5
3
4
6
7
8
9
10
1
2
3
4
5
6

## Slide 24
Page 23
MPCS Bandwidth Setting determines MPCS Video Quality.
MPCS Bandwidth | Resolution for Camera | Maximum Frame rate for Camera
256kbps | w288p (512x288) | 10fps
384kbps | w432p (768x432) | 20fps
512kbps | 720p (1280x720) | 20fps
768kbps | 720p (1280x720) | 20fps
1.0Mbps | 720p (1280x720) | 20fps
1.5Mbps | 720p (1280x720) | 20fps
2.0Mbps | 720p (1280x720) | 30fps
Resolution for PC Screen Sharing is independent from MPCS Bandwidth. HDVC sends PC Image without modifying it. 720p (720x1280), XGA(1024x768), SVGA(800x600) and VGA(640x480) are supported. Narrow bandwidth reduces frame rate to keep original PC resolution. Users with HDVC Ver.3.0 or older have to press PC button then ‘*10’ to share PC Screen. After finish PC Screen Sharing, Press Main button then ‘*11’. (HDVC Ver.3.1 does not need thus operation)
Frame Rate for Camera and PC Screen Sharing will be decreased to keep Contents Resolution based on how much contents is busy.
Video Quality Settings

## Slide 25
Page 24
Other Settings
Total Bandwidth setting allows administrator to activate bandwidth usage warning. Administrator will get warning when MPCS uses more bandwidth than the value set as Total Bandwidth.
SIP Port number allows administrator to change SIP Port Number for Easy Connect. This settings is to avoid SIP ALG, SIP fixup and Packet Inspection affects on SIP Communication between MPCS and Easy Connect SIP Server.
Note: SIP Port number setting for IP Mode not available.
  Interval for VA Switching
  Window Switching Interval for Voice Activation.

## Slide 26
Page 25
Conference Mode
Normal Mode allows pre-registered parties in the Profile to join the conference. Web Console provides following settings for Normal Mode.
  Encryption Setting and Encryption Key
  Connecting Endpoint (Pre-registered allowed participants)
  Manual Control Enable/Disable (Need to enable for following two options)
  Screen Layout (Manual Control need to be enabled)
    Auto, CP1, CP4, CP6, CP8, CP10, CP13, CP16 are available. If the Manual Control is Disabled, Auto will be applied.
  Displaying Position Switching. (Manual Control need to be enabled)
    Voice Activation and Manual available. If the Manual Control Disabled, Fixed will be applied.
  Endpoint Bandwidth for HD and SD encoder.
  Site Name Display for HD and SD encoder.
MPCS has two types of Conference Room called “Normal” and “Ad-Hoc” Mode. They are available exclusively.

## Slide 27
Page 26
Conference Mode
Ad-Hoc Mode allows anybody to join to the conference. Web Console provides following settings for Ad-Hoc mode.
  Screen Layout (Auto/Fixed)
  Voice Activation.
    Speaking Party comes to top left when speaking if enabled.
  Auto start Ad-hoc mode upon server start.
  Voice Activated Switching
  Encryption setting and Encryption Key.
  Endpoint Bandwidth for HD and SD encoder.
  Endpoint Screen Layout for HD and SD encoder.
    CP1, CP4, CP6, CP8, CP10, CP13, CP16 are available.
  Site Name Display for HD and SD encoder.
  Note: HD and SD encoder settings are presented separately.

## Slide 28
Page 27
Conference Mode (Operation While Conference)
While Conferencing in Normal Mode and Ad-Hoc Mode, there are some options to change conference room settings.
Normal Mode provides various sort of options while video conferencing.
  Invite party in Allowed List, Disconnect current connected participant
  Display Position Switching
    Top (top left), Bottom (bottom right) and Hide are available.
    If Manual Control Disabled in the Profile, this option is not available and Displaying Position is set to Fixed. (order of join to the conf.)
  Mute/Unmute
    If Manual Control Disabled in the Profile, this option is not available.
  Screen Layout for HD and SD encoder.
    Auto, CP1, CP4, CP6, CP8, CP10, CP13, CP16 are available.
    If Manual Control is disabled when start conference, this option is not available and Screen Layout setting is set to Auto.
  Site Name Display for HD and SD encoder.
  Note: HD and SD encoder settings are presented separately.

## Slide 29
Page 28
Ad-Hoc Mode provides fewer options while video conferencing.
  Invite party by Contact List and IP, Disconnect current connected participant
  Site Name Display for HD and SD encoder
  Note: HD and SD encoder settings are presented separately.
Conference Mode (Operation While Conference)

## Slide 30
Page 29
MPCS Specification Detail
3
Overview of MPCS
1
MPCS Key Feature Overview
2
MPCS Settings
4
MPCS Operation
5
Linux Installation
6
MPCS Installation
7

## Slide 31
Page 30
Set Option and Select whom to dial out
Start Ad-Hoc Mode Conf.
Start Normal Mode Conf.
Available Operation
Dial Out / Dial In
Change Displaying position
Mute/Un-mute
Site Name Display
Change Screen Layout
Terminate Conference
Available Operation
Dial Out / Dial In
Site Name Display
Terminate Conference
Start
Operation Flow

## Slide 32
Page 31
Contents of Operation
Login
Basic
Settings
Profile
Settings
Login
  Login to the System
Status Screen
  Show Status of the System
Basic Settings
  Settings for Bandwidth Warning Threshold, SIP Port number, Window Switching Interval and some Ad-Hoc Mode settings
Profile Settings
  Profile Settings for Normal Mode
Status Screen

## Slide 33
Page 32
Login
Press “Settings” to go to Basic Settings Screen
To Refresh Status
After you login you will see this screen.
Input username and password then Click OK button
Access http://127.0.0.1/hdvc_mpcs/index.cgi on your browser.

## Slide 34
Page 33
Go to Profile setting.
Go to Address book.
Click to save changes.
Basic Settings

## Slide 35
Page 34
Basic Settings
Settings |  |  | Descriptions
Basic Settings |  |  | 
 | Total Bandwidth |  | When System bandwidth usage exceed this threshold, alert goes off in the Web Console.
 | NAT Traversal service server SIP port |  | Allow user to change SIP Port number to avoid conflict with other application and SIP ALG feature. Default = 5060. Alternate = 15060.
 | Interval for VA Switching |  | Window switching interval for Voice Activation.
Ad-Hoc Settings |  |  | 
 | Screen Layout Switching |  | Auto let server decide screen layout based on number of participants automatically. Fixed let admin. Decide fixed layout.
 | Voice Activated(VA) Switching |  | Bring talking party to left top of the screen automatically.
 | Auto conference start |  | Start Ad-hoc conference upon server start-up.
 | Encryption |  | Encrypt audio and video data.
 | Encryption Key |  | Encryption key.
Setting for HD Video |  |  | 
 | Bandwidth |  | Bandwidth setting for HD encoder.
 | Screen Layout |  | Screen layout setting for HD encoder. Screen Layout Switching should be set to Fixed.
 | Site Name Display |  | Display site name on the screen.
Setting for SD Video |  |  | 
 |  | Bandwidth | Bandwidth setting for SD encoder.
 |  | Screen Layout | Screen layout setting for SD encoder. Screen Layout Switching should be set to Fixed.
 |  | Site Name Display | Display site name on the screen.

## Slide 36
Page 35
Profile Settings (Normal mode only)
ID 1 to 10 are for Normal Mode.
Press ID to edit Profile.

## Slide 37
Page 36
Profile Settings (Normal mode only)
Press Set to save changes
Option to allow operation from Web Console while conferencing.
SD and HD Codec settings
Listed endpoint are allowed to participate conference.

## Slide 38
Page 37
Profile Settings (Normal mode only)
Settings |  | Descriptions
Edit Profile |  | 
 | Profile ID | ID of profile. Can not change.
 | Profile Name | Set profile name up to fifty letters. Blank is allowed.
 | Description | Description for Profile. Optional.
 | Encryption | On/Off Encryption of audio / video data
 | Encryption key | Pre-shared key for encryption
Endpoint List |  | 
 | Sites | List of allowed party to join to the conference. You can add using Address book or specifying IP Address.
Control Settings |  | 
 | Manual Control | Enable  Following “Screen Layout” and “Display Position Switching” will be selectable. Disable  “Screen Layout” will be Auto and “Display Position Switching” will be Auto.
 | Screen Layout Switching | Auto  Decide screen layout based on number of participants automatically. Manual  Allow administrator to select screen layout when start conference.
 | Display Position Switching | Voice activated  Speaking party will be displayed on top left of the screen automatically. Manual  Allow administrator to change displaying position via Web Console while conferencing.

## Slide 39
Page 38
Profile Settings (Ad-Hoc mode only)
101 to 110 are for Ad-Hoc Mode.
Press ID to edit Profile.
Profile for Ad-Hoc Mode allow participants to initiate call to endpoint who are listed in the Profile.

## Slide 40
Page 39
Profile Settings (Ad-Hoc mode only)
Press set to save changes.
While Ad-Hoc conferencing, Pressing ‘#’ and Profile ID then MPCS will dial out to these listed party.
E.g. If you would like to dial out using Profile ID 101, press #101.

## Slide 41
Page 40
Start Conference
Go to Home Screen
Start/End
Conference
Normal Mode
Starts
Ad-Hoc Mode
Starts
Go to Home Screen
  Start/End Tab is available in Home Screen
Start/End Conference
  Start Conference by choosing “Normal” or “Ad-Hoc” Mode
Normal Mode
  Only listed party in Allowed List can join to the conference. Various options available while conferencing
Ad-Hoc Mode
  Anyone can join to the conference. Fewer options available while conferencing.

## Slide 42
Page 41
Go to Home Screen
Press “Home” to go to Home Screen. Start/End Conference available there.

## Slide 43
Page 42
Go to Start/End Conference Screen
Press “Conference Start/End” Tab

## Slide 44
Page 43
Choose Conference Mode
1. Select “Ad-hoc” mode or “Normal Mode”
2. Select “Profile” if you choose “Normal Mode”
3. Press Next

## Slide 45
Page 44
Start Normal Mode Conference
Choose number of Windows
for two encoders.
Listed here allowed to join
Tick to dial
Press start to initiate conference
Listed here cannot join

## Slide 46
Page 45
Start Ad-Hoc Mode Conference
MPCS dial out to these listed party when conference starts
Add/delete endpoints to dial out

## Slide 47
Page 46
Start Screen
After you start conference you will see this screen.

## Slide 48
Page 47
How to Operate While Conference
Status Screen
Change Settings
End Conference
Status Screen
  Show current Conference Status
Change Settings
  Normal Mode and Ad-Hoc Mode provide difference options.e
End Conference
  Terminate Conference

## Slide 49
Page 48
Status Screen
Choose Conference Start/End Tab to terminate Conference
Choose Conference Operation to change Conference Settings.

## Slide 50
Page 49
End Conference
Press End Conference button to terminate Conference

## Slide 51
Page 50
Operate Normal Mode Conference
Choose which site to be operated.
Mute/Un-mute.
Change Screen Layout of HD encoder.
Show/Hide Site name of HD encoder.
Change Screen Layout of SD encoder.
Show/Hide Site name of SD encoder.
Change displaying position
Add/Disconnect Terminals
Choose which site to be operated.
Mute/Un-mute.
Change Screen Layout of HD encoder.
Show/Hide Site name of HD encoder.
Change Screen Layout of SD encoder.
Show/Hide Site name of SD encoder.
Change displaying position

## Slide 52
Page 51
Operate Ad-Hoc Mode Conference
Show/Hide Site name of HD encoder.
Show/Hide Site name of SD encoder.
Choose which site to be operated.
Add/Disconnect Terminals

## Slide 53
Page 52
Activation
  Add Activation Key to system
Network Status
  Show Network Status
Port Settings
  Static NAT Port Settings for Panasonic NAT Traversal Service
Language Settings
  Change Language. English and Japanese are supported.
Account Settings
  Manage user account
Log
  Show system log data
Configuration Data
  Backup and Restore settings
Shutdown
  Shutdown MPCS Software and/or Sever.
About
  Display MPCS Firmware version and AAA
Maintenance Tab

## Slide 54
Page 53
Go to Maintenance Tab
Click here to go to Maintenance

## Slide 55
Page 54
Activation Tab
License for MPCS Activation and Port number expansion.
License for Panasonic NAT Traversal Service

## Slide 56
Page 55
Network Status
55
Click here to change IP Address for IP Mode
This button will be displayed only when Panasonic NAT Traversal Service license is expired.
Execute connection test for Panasonic NAT Traversal Service.

## Slide 57
Page 56
Port Settings
To activate Panasonic NAT Traversal Service, need to fill following table.
Also need to configure “Port Forwarding” on Router.

## Slide 58
Page 57
MPCS Specification Detail
3
Overview of MPCS
1
MPCS Key Feature Overview
2
MPCS Settings
4
MPCS Operation
5
Linux Installation
6
MPCS Installation
7

## Slide 59
Page 58
Server Specification
Item1 |  | Entry Model | Middle / High Model
CPU | Model Name | Intel CPU Core i7 or Xeon E3-1280 or greater | Intel CPU Xeon X5690 or greater
 | CPU Core Clock (GHz) | 3.4 | 3.46
 | # of CPUs | 1 | 1
 | # of CPU Cores | 4 | 6
 | # of CPU Threads | 8 | 12
 | CPU L2 Cache(MB) | 8 | 12
Main Memory(GB) |  | 8GB or more | 8GB or more
Tested model |  | HP Pavilion PC h8-1280jp ( JPY 87,430) | HP DL160 G6 (JPY 438,900)
Bandwidth per a site | # of Conference room and Participants mixture | 6 Connections | 8 Connection | 12 Connections | 16 Connections
1Mbps | 1 Conf. room (HDVC + Android/iOS/Windows)* | Entry Model | Entry Model | Middle / High Model | Middle / High Model
2Mbps | 1 Conf. room (HDVC + Android/iOS/Windows) | Entry Model | Middle / High Model | Middle / High Model | Middle / High Model
Two Server Machines have been tested
Configuration and Applicable Model matrix
(*) HDVC + Android describe situation that HDVC and Android Soft Client are mixed in conference room.
Since HDVC and Android send different resolution image, need lots more computational power on server side when they are mixed in a conference room.

## Slide 60
Page 59
Server Network Configuration
Point for Designing Network.
To activate only IP Mode, Configure IP on I/F for IP Mode and assign Gateway for another subnet.
To activate both IP and NAT Traversal Mode, Specify Router to access internet as Default Gateway. Also need to configure Static IP Route of Linux for LAN Access.
Subnet A
Router (Default Gateway)
Subnet C
Subnet B
I/F for NAT Traversal Service
I/F for IP Mode
Router
(Gateway for other Subnet)

## Slide 61
Page 60
Operating System Selection
 | Cent OS | Red Hat Linux
Price | Free of Charge | US$ 1,000 / year / server
Support | Incident Base US$ 2,500 / 3 Incidents | 
Cent OS Ver.6.2 x86 64bit version is available at following URI and File name
  http://vault.centos.org/6.2/isos/x86_64/
  “CentOS-6.2-x86_64-bin-DVD1.iso”
Note :
HDVC-MPCS activation is not guaranteed on version other than recommended one and on Linux environment which is installed from unsupported Linux distribution.
Supported Operating System
  CentOS_6.2_final 64bit
  CentOS_6.4_final 64bit
  Red Hat Enterprise Linux Server release 6.2 64bit
  Red Hat Enterprise Linux Server release 6.4 64bit

## Slide 62
Page 61
CentOS
  OS Location
    Go to http://www.centos.org/ to download DVD ISO image
  OS Version
    Choose Right version Ver.6.2 final 64bit.
    Choose Right version Ver.6.4 final 64bit.
Red Hat Enterprise Linux
  OS Location
    Go to http://http://www.redhat.com to purchase product
  OS Version
    Choose Right version Ver.6x 64bit
Get Linux Operating System

## Slide 63
Page 62
Note :
Windows Internet Explorer 9.0, Google Chrome™ are not supported in MPCS V2.1.
Windows XP is not supported as platform to be operated browser.
Memo :
According to browser for use, display position such as text display, ruled line, input operation area, list display, pull-down menu and so on, and part of processing might be different.
Supported Browsers for HDVC-MPCS
  Windows Internet Explorer 8.0 (only Windows7)
  Windows Internet Explorer 10.0
  Mozilla Firefox 23
Browsers for Web Console

## Slide 64
Page 63
CentOS Installation
1. Choose this then press [Enter] key
2. If you wan to test Media, Choose [OK] then press [Enter] key. You can skip this if you want. (go next page)
3. Choose [Test] then press [Enter] key
Insert CentOS DVD and Boot Up the Server.
To boot from DVD you may need to change Server BIOS setting.
Proceed installation by following instruction hereunder.
4. Choose [Continue] then press [Enter] key

## Slide 65
Page 64
CentOS Installation
2. Choose English then Click Next
1. Click [Next]
3. Choose Preferred Keyboard Layout then Click Next
4. Choose Basic Storage Devices then Click Next
5. Click “yes, discard any data”

## Slide 66
Page 65
CentOS Installation
65
1. Click Configure Network
3. Tick “Connect automatically” Input 1280 on MTU, then select “IPv4 Settings” Tab
2. Choose Network Interface then Click Edit. If you install two I/F, do same settings for two I/F.
4. Choose “Automatic” or “Manual”. If you want to use DHCP, select Automatic. If you want to specify IP Address, select Manual.
5. If you choose Automatic, Click Apply button.

## Slide 67
Page 66
CentOS Installation
2. Click Close
3. Click Next
1. If you choose Manual, Click Add button then Specify IP, Subnet mask and Gateway. After that Click Apply button

## Slide 68
Page 67
CentOS Installation
1. Select preferred time zone
2. Click Next
Choose your Time Zone then click Next button
Input Password for root (administrator)
Remark:
Select Strong Password. No personal information like Birthday, anniversaries. Avoid any easy to guess letters. More letters is better.
Please note that the weakest point in any security is usually password.
Input Password then Click Next.
Choose root password
(root = administrator)
Choose Time Zone

## Slide 69
Page 68
CentOS Installation
1. Choose “Use All Space”
2. Click Next
Choose “Use All Space” then click Next button
Flashing modification to disk
Installation type selection
Click “Write changes to disk” button
3. Click “Write changes to disk”

## Slide 70
Page 69
CentOS Installation
2. Click Next
1. Choose “Desktop”
Choose “Desktop” then click “Next”

## Slide 71
Page 70
CentOS Installation
Wait Installation to be done
Continue Installation
Click Reboot to restart the system
Wait package installation to be done
Click Reboot to restart the system.
2. Click Reboot
After system restart, Click Forward button
3. Click Forward
Remove DVD from DVD Drive
System may boot up from DVD again.
Please remove DVD media before system
Boot up.
Wait Installation to be done
Click Reboot to restart the system
Remove DVD from DVD Drive

## Slide 72
Page 71
CentOS Installation
Agree to End User License Agreement
Kdump activation. You can skip it.
Set date and time
Choose “Yes, I agree to the License Agreement”
then Click Forward
1. Choose Yes
2. Click Forward
Configure Date and Time then click Forward
4. Click Forward
Click forward
5. Click Forward
3. Click Forward then answer Yes to Dialog
Skip Create User

## Slide 73
Page 72
MPCS Specification Detail
3
Overview of MPCS
1
MPCS Key Feature Overview
2
MPCS Settings
4
MPCS Operation
5
Linux Installation
6
MPCS Installation
7

## Slide 74
Page 73
MPCS Installation
4. Click Close
1. Select Other to login to system as root
2. Type “root” here then click Log In
3. Type your password then Click Log In

## Slide 75
Page 74
MPCS Installation
1. Insert CentOS Ver.6.2 Installation Disk 1. You will see following pop up.
If you do not see pop up, re-insert Disk or go to Appendix around end of this document.
2. Insert MPCS Installation media then you may see following file manager window

## Slide 76
Page 75
MPCS Installation
5. Double Click ethflwctrl_setup.sh
1. Configure Installation Environment
2. Configure Installation Environment
3. Click Run in Terminal. You will see new window pop up. Wait until the window closed. It will take around minutes. If pop up window close within few seconds, you may failed to mound DVD. See Appendix for how to Mount DVD.
1. Double Click yumsetup
2. Double Click yumsetup.sh
4. Double Click ethflwctrl_setup

## Slide 77
Page 76
MPCS Installation
4. Double Click RPM
5. Double Click hdvc-mpcs-0.1-0.0.x86_64.rpm
3. Start Install additional Packages

## Slide 78
Page 77
MPCS Installation
After you finish installation you will see two icons named as following on desktop.
  1. Start_HDVC-MPCS.sh
  2. Uninstall_HDVC-MPCS.sh
4. After installation double click
yumrestore.sh” to restore yum setting
3. Click Install
Need to Wait for a while.
Wait for a while
1. Click Continue Anyway
2. Click Install

## Slide 79
Page 78
MPCS Installation
3. Type “ifconfig” and press enter then you will see MAC
Address Information. This MAC address is required to register
MPCS License.
2. Click Terminal
1. Click Application

## Slide 80
Page 79
MPCS Installation
1. Go to web site
https://www.tsunagarunet.com/hdcom/main
2. Issue license by following instruction. MAC Address and License card information are required.
3. You will receive 16 digits Registration ID. Do not lost this information.
NAT Traversal Service License Registration

## Slide 81
Page 80
MPCS Installation
Select your language
Start Configuring MPCS
Input user/passwd for Web Console login.
Input Registration Keys
5. Enter MPCS 16-digit Registration Key
6. Click Next
8. Click Next
1. Click here to open Web Browser
2. Type “127.0.0.1/hdvc_mpcs/index.cgi”
then press Enter
3. You will see Web Console on the Browser
3. Select Language
4. Click Next
7. Enter MPCS administrator information here.
Username and Password must be 6 to 16 letters.

## Slide 82
Page 81
MPCS Installation
Input IP Address of your system
1. Enter IP Address for IP Mode
2. Press Finish then you are ready to use MPCS

## Slide 83
Page 82
MPCS Installation
Key Registration of NAT Traversal Service
To connect to NAT Traversal Service by using HDVC-MPCS, it is necessary to register the registration key.
Registration key should be acquired by using MAC address of PC that install activation key card information and HDVC-MPCS to NAT Traversal Service server in advance.
Click in the order of maintenance – activation on Web console, and display the following screen.
Input Registration key, acquired from server, at input position of Registration key for NAT Traversal Service.
NAT Traversal Service is activated by clicking registration button below input column.
Input Registration Key
1. Go to Maintenance Tab  Activation.
2. Enter Registration Key and Press Register.

## Slide 84
Page 83
MPCS Installation
Port Registration of NAT Traversal Service
Unless port settings are performed, NAT Traversal Service can not be used.
As for 6 ports model, it is necessary to be set 6 ports by all means. In case of auto input, 6 ports are set automatically.
As for other models, regardless of current maximum number of ports, 16 ports settings are required. In addition, in case of auto input, 16 ports settings are performed automatically.
Additionally, in case automatic setting is performed by clicking “Same port on WAN and LAN”, each of LAN port number is copied to WAN port number. Besides, in case of entering port number for Site1 and clicking “Auto input for WAN”, WAN port number for the rest of the Site will be automatically assigned sequential number.
1. Go to Maintenance  Port Settings.
2. Configure Port Settings. This information is required to configure “Port Forwarding” settings on your Router.
Port that is used for NAT Traversal Service is set. In the initial status, input boxes for WAN side are blanks before assigned WAN port number as follows.
Press “Same port on WAN and LAN” to fill port information automatically.

## Slide 85
Page 84
MPCS Installation
Connection Test of NAT Traversal Service
Click “Connection Test”
HDVC-MPCS have function for NAT Traversal Service connection test, to confirm connectivity in case of setting and failure.
This test can not be executed, if NAT Traversal Service is not activated and NAT Traversal port settings are not performed.
If you want to perform test, click button within encircling red line in the figure above.
Test start after clicking the button. The following screen is displayed during the test.
Periodically click “Refresh” button.
(Screen is not switched automatically.)
And if you want to stop test, please click “Stop” button.
Click “Refresh”

## Slide 86
Page 85
MPCS Installation
Connection Test of NAT Traversal Service
If screen switch to the following screen after clicking “Refresh” button, test is completed.
If you click “Show Results” button, port check result is displayed.
* If you click “Back” on this screen, screen is returned to network status screen. After returning to network status screen, you can not shift to this screen again. So, please note this. (If you want to confirm detailed test result, please perform test again.)

## Slide 87
Page 86
MPCS Installation
Connection Test of NAT Traversal Service
On this screen, check result for each port is displayed. Meaning of result is as follows.
  S：Success
  U：Undefined
  F：Fail
In case all ports are filled with “S”, test is successful. (All ports are confirmed to be connectable.)
In addition, as for detail of this result (S/U/F) viewpoint, please refer to “E03-03_v200doc_NAT Traversal Service Connection Test Manual”.
*If you click “Back” button on this screen, screen is shifted to network status screen.
After that, you can't shift to this screen again. So, please note this. If you want to confirm connection result again, please perform test again.

## Slide 88
Page 87
MPCS Installation
Recommended Router for NAT Traversal Service
The following routers are already confirmed operation check at PSN.
Area | Router
Japan | YAMAHA RTX1200 / RTX3500
Overseas and Japan | CISCO 2951 / 1941
Note:
When using CISCO router, restriction, that No.5100 port can't pass STUN check, is found. In spite of when NAT Traversal connection test result is failed, if connection is performed, No.5100 port also pass properly (cause is unknown.). When setting MPCS port (refer to 4.2), please set except No.5100 port.

## Slide 89
Page 88
MPCS Installation
Sample Configuration for NAT Traversal Service
The following is sample configuration of CISCO1941. In addition, please note that there may be necessary for this sample to be corrected according to customer’s network environment.
version 15.0
!
enable password password
!
no ipv6 cef
ip source-route
ip cef
!
ip domain name cisco
ip inspect name firewall https
ip inspect name firewall dns
ip inspect name firewall tcp
ip inspect name firewall udp
ip inspect name firewall icmp
!
multilink bundle-name authenticated
!
crypto pki token default removal timeout 0
!
license udi pid CISCO1941/K9 sn 12345678
!
archive
log config
hidekeys
!
redundancy
!
interface GigabitEthernet0/0
no ip address
duplex auto
speed auto
pppoe enable group global
pppoe-client dial-pool-number 1
no cdp enable
!
!
interface GigabitEthernet0/1
ip address 172.16.100.254 255.255.255.0
ip nat inside
ip virtual-reassembly
ip tcp adjust-mss 1356
duplex auto
speed auto
!
!
interface Dialer1
mtu 1438
ip address negotiated
ip access-group A-security in
ip nat outside
ip inspect firewall out
ip virtual-reassembly
encapsulation ppp
dialer pool 1
dialer-group 1
ppp authentication chap callin
ppp chap hostname USER@ocn.ne.jp
ppp chap password USERPassword
no cdp enable

## Slide 90
Page 89
MPCS Installation
ip forward-protocol nd
!
no ip http server
no ip http secure-server
!
no ip nat service sip tcp port 5060
ip nat inside source list 1 interface Dialer1 overload
ip nat inside source static udp 172.16.100.100 5101 interface Dialer1 5101
ip nat inside source static udp 172.16.100.100 5102 interface Dialer1 5102
ip nat inside source static udp 172.16.100.100 5103 interface Dialer1 5103
ip nat inside source static udp 172.16.100.100 5104 interface Dialer1 5104
ip nat inside source static udp 172.16.100.100 5105 interface Dialer1 5105
ip nat inside source static udp 172.16.100.100 5106 interface Dialer1 5106
ip nat inside source static udp 172.16.100.100 5107 interface Dialer1 5107
ip nat inside source static udp 172.16.100.100 5108 interface Dialer1 5108
ip nat inside source static udp 172.16.100.100 5109 interface Dialer1 5109
ip nat inside source static udp 172.16.100.100 5110 interface Dialer1 5110
ip nat inside source static udp 172.16.100.100 5111 interface Dialer1 5111
ip nat inside source static udp 172.16.100.100 5112 interface Dialer1 5112
ip nat inside source static udp 172.16.100.100 5113 interface Dialer1 5113
ip nat inside source static udp 172.16.100.100 5114 interface Dialer1 5114
ip nat inside source static udp 172.16.100.100 5115 interface Dialer1 5115
ip nat inside source static udp 172.16.100.100 5116 interface Dialer1 5116
ip nat inside source static udp 172.16.100.100 5117 interface Dialer1 5117
ip nat inside source static udp 172.16.100.100 5118 interface Dialer1 5118
ip nat inside source static udp 172.16.100.100 5119 interface Dialer1 5119
ip nat inside source static udp 172.16.100.100 5120 interface Dialer1 5120
ip nat inside source static udp 172.16.100.100 5121 interface Dialer1 5121
ip nat inside source static udp 172.16.100.100 5122 interface Dialer1 5122
ip nat inside source static udp 172.16.100.100 5123 interface Dialer1 5123
ip nat inside source static udp 172.16.100.100 5124 interface Dialer1 5124
ip nat inside source static udp 172.16.100.100 5125 interface Dialer1 5125
ip nat inside source static udp 172.16.100.100 5126 interface Dialer1 5126
ip nat inside source static udp 172.16.100.100 5127 interface Dialer1 5127
ip nat inside source static udp 172.16.100.100 5128 interface Dialer1 5128
ip nat inside source static udp 172.16.100.100 5129 interface Dialer1 5129
ip nat inside source static udp 172.16.100.100 5130 interface Dialer1 5130
ip nat inside source static udp 172.16.100.100 5131 interface Dialer1 5131
ip nat inside source static udp 172.16.100.100 5132 interface Dialer1 5132
ip nat inside source static udp 172.16.100.100 5200 interface Dialer1 5200
ip nat inside source static udp 172.16.100.100 5201 interface Dialer1 5201
ip nat inside source static udp 172.16.100.100 5202 interface Dialer1 5202
ip nat inside source static udp 172.16.100.100 5203 interface Dialer1 5203
ip nat inside source static udp 172.16.100.100 5204 interface Dialer1 5204
ip nat inside source static udp 172.16.100.100 5205 interface Dialer1 5205
ip nat inside source static udp 172.16.100.100 5206 interface Dialer1 5206
ip nat inside source static udp 172.16.100.100 5207 interface Dialer1 5207
ip nat inside source static udp 172.16.100.100 5208 interface Dialer1 5208
ip nat inside source static udp 172.16.100.100 5209 interface Dialer1 5209
ip nat inside source static udp 172.16.100.100 5210 interface Dialer1 5210
ip nat inside source static udp 172.16.100.100 5211 interface Dialer1 5211
ip nat inside source static udp 172.16.100.100 5212 interface Dialer1 5212
ip nat inside source static udp 172.16.100.100 5213 interface Dialer1 5213
ip nat inside source static udp 172.16.100.100 5214 interface Dialer1 5214
ip nat inside source static udp 172.16.100.100 5215 interface Dialer1 5215
ip nat inside source static udp 172.16.100.100 5216 interface Dialer1 5216
ip nat inside source static udp 172.16.100.100 5217 interface Dialer1 5217
ip nat inside source static udp 172.16.100.100 5218 interface Dialer1 5218
ip nat inside source static udp 172.16.100.100 5219 interface Dialer1 5219
ip nat inside source static udp 172.16.100.100 5220 interface Dialer1 5220
ip nat inside source static udp 172.16.100.100 5221 interface Dialer1 5221
ip nat inside source static udp 172.16.100.100 5222 interface Dialer1 5222
ip nat inside source static udp 172.16.100.100 5223 interface Dialer1 5223
ip nat inside source static udp 172.16.100.100 5224 interface Dialer1 5224
ip nat inside source static udp 172.16.100.100 5225 interface Dialer1 5225
ip nat inside source static udp 172.16.100.100 5226 interface Dialer1 5226
ip nat inside source static udp 172.16.100.100 5227 interface Dialer1 5227
ip nat inside source static udp 172.16.100.100 5228 interface Dialer1 5228
ip nat inside source static udp 172.16.100.100 5229 interface Dialer1 5229
ip nat inside source static udp 172.16.100.100 5230 interface Dialer1 5230
ip nat inside source static udp 172.16.100.100 5231 interface Dialer1 5231
ip route 0.0.0.0 0.0.0.0 Dialer1
!
ip access-list extended A-security
permit udp any any range 5101 5132
permit udp any any range 5200 5231
!
access-list 1 permit 172.16.100.0 0.0.0.255
dialer-list 1 protocol ip permit

## Slide 91
Page 90
MPCS Installation
Data Type | External Port | Internal Port | Protocol
Audio | 5100-5131 | 5100-5131 | UDP
Video | 5200-5231 | 5200-5231 | UDP
SIP | 5060, 15060 | 5060, 15060 | UDP and TCP
Table: Ports has to be port forwarded to MPCS IP Address
Configure Port Settings on your Router
Following Port need to port forward to MPCS IP Address which configured to access to Internet.

## Slide 92: Appendix Trouble Shooting

## Slide 93
Page 92
How to Mount DVD
1. Double Click “Computer”
2. Right Click DVD Icon. If you don’t see this Icon, you probably
have problem with your drive or media.
3. Click “Mount”

## Slide 94
Page 93
How to Check IP Address
3. Type “ifconfig” and press enter then you will see
IP Address information
2. Click Terminal
1. Click Application

## Slide 95
Page 94
How to Configure IP Address After Install
1. Go to System -> Preference -> Network Connections.
2. Click Add button or select existing interface
then press Edit.
3. Tick Connect Automatically and Available to all users
then Go to IPv4 Settings Tab.
4. Click Add button, input necessary information
then Click Apply button. After that, click Close to
finish setting.

## Slide 96
Page 95
How to Enable Network After Install
If still you have problem with network….
2. Click Terminal
1. Click Application
Check network interface is recognized by CentOS.
If network device is recognized by system, you will see eth0, eth1, eth2… depends on number of interfaces you have. If you see only lo, device is not recognized. You may need to install extra interface card or replace server.
3. Execute “ifconfig –a”

## Slide 97
Page 96
How to Enable Network After Install
If network interface is physically not connected or network interface is turned off by software, you won’t see the word “UP”
If you don’t properly configure IP Address, you won’t see this line
Example for properly configured network interface
Result of “ifconfig –a” command tells you interface situation.
Example of network interface not configured. IP Address is not assigned and interface is not activated.

## Slide 98
Page 97
How to Enable Network After Install
1. Execute “gedit /etc/sysconfig/network-scripts/ifcfg-eth0” if you would like to use eth1, replace “eth0” with “eth1” on above command
If ONBOOT=no, interface will not be activated when server start
Input necessary information like this. If you do not need GW, you can remove GATEWAY line.
If you don’t need DNS< you can remove these lines.
2. After you edit file, save it then restart system to reflect changes.

## Slide 99
Page 98
How to Enable Network After Install
1. You can also use setup command to change interface settings

## Slide 100
Page 99
How to Change Name “eth0” and “eth1”, etc.
1. Execute ifconfig –a to see current situation
Show how to change eth2 to eth1
2. Edit /etc/udev/rules.d/70-persistent-net.rules

## Slide 101
Page 100
How to Change Name “eth0” and “eth1”, etc.
Change eth2 to eth0 (change as you want)
Delete this line if you think this is useless
3. Change setting and save it.

## Slide 102
Page 101
How to Change Name “eth0” and “eth1”, etc.
4. Remove ifcfg-eth0, ifcfg-eth1, ifcfg-eth2 etc in /etc/sysconfig/network-scripts
5. Restart system
6. Start over IP address setup

## Slide 103
Page 102
1. Execute setup command on the console terminal
2. Execute Keyboard configuration then select desired one
Actual setting is written in
/etc/sysconfig/keyboard
How to Change Keyboard Setting

## Slide 104
Page 103
Command | Description | Example
passwd | Change password | passwd <- change current user’s password passwd username <- change Other user’s password
adduser | Add user | adduser username
top | Show CPU usage. Stop with ‘q’ | top
df | Show disk usage | df –h
ps | Show process | ps aux
less | Show file content | less /etc/sysconfig/network-scripts/ifcfg-eth0
halt | Turn off system | 
reboot | Restart system | 
Other Linux Commands

## Slide 105
Thank You !
Panasonic System Networks Co., Ltd.
Security System Business Division