## Slide 1: WV-ASF950 Camera angle adjustment
Jun. 2020
Panasonic i-PRO Sensing Solutions Co., Ltd.

## Slide 2: Easy Camera Setup Tool
2
Camera angle adjustment tool: One click setup solution by PTZ camera
When you use PTZ camera, you can setup angle of view by one click from the tool.
(It control PTZ automatically for detected face)
WV-S6130
Adjustment tool

## Slide 3
3
This is common for both registered detection & unregistered detection function.
We recommend a location where the person can walk straight towards the camera to capture the front face as much as possible.
The face width becomes 60 pixels or more by setting the field angle of about 3.5 m width which is twice the width widening both hands as a standard of field angle at the face detection start position.
《Recommended camera view angle》
1) Face width(‘a’) ≥ 60 pixels
2) 5 deg. ≤ (Angle of depression) ≤ 10 deg.
Recommended camera angle of view

## Slide 4
4
1. Position to installing a camera
Toward the store
5° - 10°
Lower the camera
as far as possible
Ceiling
Make a distance as far as possible.
15°
Face detection area
Direction of movement
End point
camera
Shot the subject face from the front as much as possible. Lower the position of the camera as much as possible by using such as a pole.
=> The face height is expected to be 1.6 m above the floor, and set the camera at 2.4 m above the floor.
The angle of depression of the camera at the face detection position should be within about 10 °.
=> Because Arctan [4.5 / 0.8] ≈ 10 °, so it is determined that the face detection end position is 4.5 m and the face detection start position is 8.5 m.
At the face detection start position, adjust the angle of view so that the width of the adult male face becomes 60 pixels.
=> The field angle width of the face detection start position is about 3.5 m. It is almost twice the distance when you spread both hands.
Start point
Gate
Floor
entrance (Outside)
8.5 m (27.9ft)
4.5 m (14.8ft)
1.6 m
(5.2ft)
0.8 m
(2.6ft)
2.4 m
(7.8ft)
Example of camera installation position 1
Notes: （万円） |  | ０７年度 | ０８年度 | ０９年度 | 年平均 下落率
ｾｷｭﾘﾃｨ | NWｶﾒﾗ | ５．４ | ５．０ | ４．５ | ▲ ８％
 | ｱﾅﾛｸﾞｶﾒﾗ | ２．６ | ２．４ | ２．０ | ▲１２％
ﾓﾋﾞﾘﾃｨ | R/W（組込） | ２．２ | ２．２ | ２．１ | ▲ ２％
 | R/W（端末） | ３．１ | ２．７ | ２．５ | ▲１０％
ﾌﾞﾛｰﾄﾞﾒﾃﾞｨｱ | 業務用ｶﾒﾗ | ２３０ | ２２４ | ２１８ | ▲ ３％
 | 放送用ｶﾒﾗ | ８３３ | ７５４ | ６８１ | ▲１０％

## Slide 5
11m (36ft)
2. Face width, distance between camera and subject
The angle of view at the face detection start position (the furthest position) is roughly twice (3.5 meters) of the width of widening both hands.
Field angle image ( : suitable)
Angle of depression | 38° |  |  | 14.9° |  | 10.1° | 6.5° | 5.1°
5m (16.4ft)
7m (23ft)
8.5m (27.9ft)
13m (42.6ft)
2.4m
(7.9ft)
0.2m
(0.65ft)
Entrance
Face width at face detection start position (farthest position): 60 pixels or more
Angle of depression at face detection end position (nearest position): 10 ° or less
13 m
11 m
◯
9 m
◯
◯
5
1.6m
Face detection
End point
Face detection Start point
0.8m
Recommended range of installation
Distance from face detection start position
9m 29.5ft
11m
36ft
13m
42.6ft
Example of camera installation position 2

## Slide 6
6
Increase the captured best shot images as much as possible at this face detection area.
Problem case1 | Countermeasure
No alarm triggered when unregistered person passes through the face detection camera | This is because ASF950 received less than 5 best shot images. In order to increase the number of captured best shot images, decrease the angle of depression about 5 to 8 degree by moving the camera installation position away from the face detection area or lower the camera installation height
Camera angle adjustment for Unregistered face detection

## Slide 7
7m
Reference: Depression angle difference according to the distance between camera & subject
Angle of depression |  |  |  |  | 11.3° |  | 8.8° |  | 7.3° |  | 6.1° |  | 5.3°
5m
9m
Start position of face detection
Distance from start position of face detection
3.0m
11m
13m
1.6m
Recommended range of camera installation
15m
Face detection area
Best shot
Estimated face detection area required is about 6.0m or more
= Walking speed (about 1.2m/s) x Travel time (5s)
7
Camera angle adjustment for Unregistered face detection

## Slide 8
<Before>
<After>
Adjust the camera angle
Problem case2 | Countermeasure
False alarm triggered In other words, registered person is recognized as unregistered person. | This is because similarity score is lower due to side face even ASF950 receives 5 best shot images. In order to increase the similarity score, try to capture front face and avoid capturing side face. Control the people flow Adjust camera angle by increasing the angle of depression within 10deg or zooming in.
8
Camera angle adjustment for Unregistered face detection

## Slide 9: Suitable environments for registered face & unregistered face detection
9
On top of camera angle adjustment, please consider these items.
Locations where no more than 8 people can pass through at the same time.
Locations where people are constantly moving and no congestion occurs
Indoors with the stable luminance (brightness) level
Notes: （万円） |  | ０７年度 | ０８年度 | ０９年度 | 年平均 下落率
ｾｷｭﾘﾃｨ | NWｶﾒﾗ | ５．４ | ５．０ | ４．５ | ▲ ８％
 | ｱﾅﾛｸﾞｶﾒﾗ | ２．６ | ２．４ | ２．０ | ▲１２％
ﾓﾋﾞﾘﾃｨ | R/W（組込） | ２．２ | ２．２ | ２．１ | ▲ ２％
 | R/W（端末） | ３．１ | ２．７ | ２．５ | ▲１０％
ﾌﾞﾛｰﾄﾞﾒﾃﾞｨｱ | 業務用ｶﾒﾗ | ２３０ | ２２４ | ２１８ | ▲ ３％
 | 放送用ｶﾒﾗ | ８３３ | ７５４ | ６８１ | ▲１０％

## Slide 10: Recommended camera and tested lens
Do not change camera settings and angle of view (Pan, Tilt, Zoom and Focus) after installation / setting is complete.
*1 : Since this lens is the C-mount type, the C/CS-mount lens adaptor is necessary.
*2 : The lens without L (short cable type) will be discontinued and will be replaced with L (long cable type) model.
*3 : This is the brightest combination at the recommended angle of view of face recognition.
*4 : Because it is a 1.3 MP compatible lens, please note that sharpness will be imparted when using imaging mode 3 MP.
However, it does not affect the accuracy of face recognition.
*5 : Vignetting occurs at the wide end because the sensor size is different. Please refrain from using at the WIDE end.
Lens |  |  |  |  |  | Camera |  |  | 
 |  |  |  |  |  | 1/2.8 inch | 1/3 inch |  | -
Maker | Model Name | Day/ Night | Sensor Size (inch) | Resolution | Focal Length (mm) | WV-S1132 WV-S1131 WV-S1112 WV-S1111 | WV-SPN531A WV-SPN631 | WV-SPN310A WV-SPN311A WV-SPN611 | WV-S6130 WV-S2531LTN WV-SFV631LT WV-SC385
FUJINON | YV3.3x15SR4A-SA2 *2 YV3.3x15SR4A-SA2L | D/N | 1/2.7 | 3MP | 15-50 | *3 |  |  | n/a
 | YV3.3x15SA-SA2 *2 YV3.3x15SA-SA2L | Day | 1/3 | 3MP | 15-50 | *5 |  |  | n/a
 | DV10x8SR4A-SA1 *1*2 DV10x8SR4A-SA1L *1 | D/N | 1/2 | 3MP | 8-80 |  |  |  | n/a
 | YV10x5HR4A-SA2 YV10x5HR4A-SA2L *2 | D/N | 1/3 | 1.3MP | 5-50 | *5 | *4 |  | n/a
TAMRON | M13VG550 | Day | 1/3 | 1.3MP | 5-50 | *5 | *4 | *3 | n/a
 | M13VG850IR | D/N | 1/2.7 | 3MP | 8-50 |  |  |  | n/a
Select megapixel network cameras and lenses for face recognition function from the following combinations.
By the firmware update, i-PRO EXTREME camera (yellow letters) will be able to detect masked face.
As of July 2018
Most suitable
suitable
acceptable
10
Notes: （万円） |  | ０７年度 | ０８年度 | ０９年度 | 年平均 下落率
ｾｷｭﾘﾃｨ | NWｶﾒﾗ | ５．４ | ５．０ | ４．５ | ▲ ８％
 | ｱﾅﾛｸﾞｶﾒﾗ | ２．６ | ２．４ | ２．０ | ▲１２％
ﾓﾋﾞﾘﾃｨ | R/W（組込） | ２．２ | ２．２ | ２．１ | ▲ ２％
 | R/W（端末） | ３．１ | ２．７ | ２．５ | ▲１０％
ﾌﾞﾛｰﾄﾞﾒﾃﾞｨｱ | 業務用ｶﾒﾗ | ２３０ | ２２４ | ２１８ | ▲ ３％
 | 放送用ｶﾒﾗ | ８３３ | ７５４ | ６８１ | ▲１０％

## Slide 11: Supported dome cameras with limited condition
11
1. Dome -Wall mount
2. Compact Dome -Wall mount
Camera | Model | Image setting | Installation
1. Dome | WV-S2130 WV-S2131 WV-S2131L WV-S2231L WV-S2531LN | Super D: OFF iA: ON Shutter: 1/100 | Wall mount
2. Compact Dome | WV-S3131L WV-S3531L | Super D: OFF iA: ON Shutter: 1/100 | Wall mount
Please check recommended camera installation position at next page.
Notes: （万円） |  | ０７年度 | ０８年度 | ０９年度 | 年平均 下落率
ｾｷｭﾘﾃｨ | NWｶﾒﾗ | ５．４ | ５．０ | ４．５ | ▲ ８％
 | ｱﾅﾛｸﾞｶﾒﾗ | ２．６ | ２．４ | ２．０ | ▲１２％
ﾓﾋﾞﾘﾃｨ | R/W（組込） | ２．２ | ２．２ | ２．１ | ▲ ２％
 | R/W（端末） | ３．１ | ２．７ | ２．５ | ▲１０％
ﾌﾞﾛｰﾄﾞﾒﾃﾞｨｱ | 業務用ｶﾒﾗ | ２３０ | ２２４ | ２１８ | ▲ ３％
 | 放送用ｶﾒﾗ | ８３３ | ７５４ | ６８１ | ▲１０％

## Slide 12: Supported dome cameras with limited condition
12
 | Angle of view | Distance from camera to face | Angle of side face (from front camera to face) | Installation height | Depression angle
1. Dome | Wide edge | From 0.5m to 2m | Front face only | height of face | 0 deg
 | Tele edge | From 2.5m to 7m | Right&Left: up to 50cm | within “height of face” + 1m | 0 to 10 deg
2. Compact Dome | Fixed focal length | From 0.5m to 1.5m | Front face only | height of face | 0 deg
0.5
1
0
1.5
2m
0.5m
1m
1.5m
2m
1. Dome -Wide edge
1. Dome -Tele edge
2. Compact Dome
From camera to face
From front camera to face
From front camera to face
From front camera to face
From camera to face
From camera to face
：recommended
：recommended
：recommended
Recommended camera installation position
Wall mounted
camera
Wall mounted
camera
Wall mounted
camera
*It is need to stop at this recommended area
*It is need to stop at this recommended area
Notes: （万円） |  | ０７年度 | ０８年度 | ０９年度 | 年平均 下落率
ｾｷｭﾘﾃｨ | NWｶﾒﾗ | ５．４ | ５．０ | ４．５ | ▲ ８％
 | ｱﾅﾛｸﾞｶﾒﾗ | ２．６ | ２．４ | ２．０ | ▲１２％
ﾓﾋﾞﾘﾃｨ | R/W（組込） | ２．２ | ２．２ | ２．１ | ▲ ２％
 | R/W（端末） | ３．１ | ２．７ | ２．５ | ▲１０％
ﾌﾞﾛｰﾄﾞﾒﾃﾞｨｱ | 業務用ｶﾒﾗ | ２３０ | ２２４ | ２１８ | ▲ ３％
 | 放送用ｶﾒﾗ | ８３３ | ７５４ | ６８１ | ▲１０％

## Slide 13
Revision History
Ver. | Date | Changes | Page
1.0 | Dec. 2018 | first edition | -
1.1 | Jun. 2020 | Add new pages: Supported dome cameras with limited condition | 11,12

## Slide 14: Thank you