## Slide 1
Edge Recording
Aug. 2021
Ver.1.10

## Slide 2
Target models
This document covers the camera models below.
In this document, "SD memory card" is used as a general term for SD, SDHC or SDXC type, unless otherwise noted.
Category | Camera Type | Model List | Supported Card
i-PRO EXTREME Series Group 1 | Box / Dome | S1111 / S1112 / S1131* / S1132* / S1432LH / S1511LN / S1531* S2111L / S2131* / S2132* / S2211L / S2231L / S2511LN / S2531* / S2532LH | SDXC/SDHC/SD
 | Compact Dome | S3111L / S3131L / S3511L / S3512LM / S3531L / S3532LM | micro SDXC
 | PTZ | S6111 / S6130* / S6131* / S6530* / S6532* / X6511N / X6531* / X6533* | SDXC/SDHC/SD
i-PRO EXTREME Series Group 2 | Box / Dome | S1550* / S1570* / S2250L / S2550* / S2270* / S2570L | SDXC/SDHC/SD
 | 360-degree | S4150 / S4550* / X4170* / X4171 / X4571* | SDXC/SDHC/SD
 | Multi-Sensor | S8530N / X8570 | SDXC/SDHC/SD
i-PRO EXTREME Series Group 3 (U Series) | Box / Dome | U1130 / U1132 / U1142 / U1532L / U1542L U2130L / U2132L / U2140L / U2142L / U2530L / U2532L / U2540L / U2542L | microSDXC/microSDHC/microSD
i-PRO EXTREME Series Group 4 | Box / Dome | S1552L / S1572L / S2252L / S2272L / S2552L / S2572L | SDXC/SDHC/SD
 | 360-degree | S4151 / S4551* / X4172 / X4173 / X4573* | SDXC/SDHC/SD
 | Multi-Sensor | S8531N / X8571N | SDXC/SDHC/SD
i-PRO with AI engine Series Group 1 | Box / Dome | X1551LN / X1571LN / X2251L / X2271L / X2551LN / X2571LN | SDXC/SDHC/SD
i-PRO with AI engine Series Group 2 | Box / Dome | S1136 / S1536 / S2136 / S2236L / S2536 | microSDXC/microSDHC/microSD
i-PRO SmartHD 4K | Box / Dome | SFV781L/SPV781L | SDXC/SDHC/SD
i-PRO SmartHD | Box / Dome | SW175 | SDHC/SD

## Slide 3
Table of contents
1. Overview
2. SD recording settings
4. Backup for NVR
5. Other functions
6. i-PRO SD memory cards
3. View recorded data (H.265/H.264/JPEG)
5.1 Password Lock
5.2 Alteration detection
6.1 i-PRO SD memory card line-ups
6.1 Advantage of 3D NAND TLC
6.2 Reference : Estimated Recording Hours(H.264/H.265)
6.3 Reference : Replacement cycle (continuous recording)
4.1 SD memory backup with recorder (NX-NVR)
3.2 Replay / Download : Camera browser (H.265/H.264/JPEG)
3.3 Replay : ASM300
3.4 Download MP4 : ASM300
3.5 Replay SD recorded data : PC
1.1 Recording trigger
1.2 Comparison table for recording modes
2.1 Setup procedure
2.3 Set Image
2.4 Set VMD area
2.5 Set Schedule
2.6 Start manual recording
2.2 Set SD memory card recording
3.1 Overview

## Slide 4
1. Overview

## Slide 5
1.1 Recording trigger
Camera can save video to SD memory card triggered by several events
Available recording trigger events are Alarm, Manual and Schedule
Recording trigger
Replay / Download
Alarm
Transmission priority:
Frame rate or CBR for most models (*)
  When “VBR” or “Best effort” is set, it will be changed to “Frame rate”.
  When “VBR” is set, “Max bit rate (per client) may be changed.
GOP Control:
Off
  When the GOP Control is other than “Off”, it will be changed to “Off”.
Refresh interval:
No more than 1s
  When “Refresh interval” is longer than “1s”, it will be changed to “1s”
Audio (in case 2 recording stream) :
  When recording audio, recording stream2 must be “Off”
Pre alarm duration:
  “Pre-alarm duration” differs depending on the bit rate.
When the camera loses network connection with NVR, starts recording to SD memory card for backup.
Manual
Schedule
Network failure
Camera browser
ASM300
PC
NX-NVR
Camera
Replay
File download
Replay
File download
Download
Password Lock
Alteration detection
Security Viewer
Replay
File download
TBD
(*) refer to Appendix

## Slide 6
1.2 Comparison table for recording modes
 | Camera Independent REC |  |  |  |  | Backup for NVR REC
Rec trigger | Alarm |  | Manual |  | Schedule | Network failure with NVR
Folder name in SD | M_ALARM, M_ALARM2 | ALARM | M_LOCAL, M_LOCAL2 | LOCAL | M_LOCAL, M_LOCAL2 | N_NWBKP
File format (*1) | .mp4 | .jpg | .mp4 | .jpg | .mp4 | .mp4
Video Encoder (*2) | H.265/H.264 | JPEG | H.265/H.264 | JPEG | H.265/H.264 | H.265/H.264
Audio Encoder | AAC-LC | - | AAC-LC | - | AAC-LC | AAC-LC
Max. Rec speed(*3) | 12Mbps (Panasonic SD) / 8Mbps (i-PRO SD) |  |  |  |  | 
Streaming condition (*3) | 24Mbps or less, 120fps or less, and 5 times or less. (3times or less with audio) |  |  |  |  | 
Setup | Setup camera browser |  |  |  |  | Setup NVR browser
Other conditions | Pre Recording: H.265/H.264 : Max. 120sec JPEG : 0-5frames Post Recording: H.265/H.264 : Max. 300sec JPEG : 10-3000frames |  | Note: Manual Recording will automatically restart if the camera reboots. |  |  | 
(*1) H.265/H.264 video data are saved in 20MB files.
(*2) If you want to change compression format of H.265/H.264 and JPEG, card re-formatting is required. H.265/H.264 file format is mp4.
(*3) In case of the SD memory card supports Class 10 with UHS-I. If the card support Class 6 to Class 10 without UHS-I, MAX. Rec speed is up to 6Mbps. Otherwise, recording may be intermittent. In a system using the ASM200, 14Mbps is the upper limit.

## Slide 7
2. SD recording settings

## Slide 8
2.1 Setup procedure
Camera Setting
Recording trigger |  |  |  | 
(A) Alarm input recording Automatically record when an alarm occurs | Yes | Yes | Yes | Yes
(B) Manual recording Manually record by operating browser buttons | Yes | Yes | --- | ---
(C) Schedule recording Record according to the specified day and time | Yes | Yes | --- | Yes
Camera Setting
Basic >
SD memory card
Image/Audi >
Image
Alarm > VMD area
Schedule > Schedule
Setup procedure for SD memory card recording
1
2
3
4
This chapter explains the case where the recording trigger is a VMD alarm

## Slide 9
2.2 Set SD memory card recording
(1) Basic > SD memory card
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(A) Alarm input recording
(B) Manual recording
(C) Schedule recording
Select whether or not to save audio data when saving video data in MP4 format
Audio (in case 2 recording stream) :
When recording audio, recording stream2 must be “Off”
Select a trigger to save images on the SD memory card
(A) Alarm input recording : Alarm input
(B) Manual recording : Manual
(C) Schedule recording : Schedule
Display setup menu
(2) Image/Audio > Image

## Slide 10
2.2 Set SD memory card recording
(1) Basic > SD memory card
(2) Image/Audio > Image
Display setup menu
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(A) Alarm input recording
(B) Manual recording
(C) Schedule recording
(A) Alarm input recording :
Set the duration to save image data on the SD memory card after an alarm occurrence
Pre alarm duration:
“Pre-alarm duration” differs depending on the bit rate

## Slide 11
2.3 Set Image
(1) Basic > SD memory card
(2) Image/Audio > Image
Display setup menu
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(A) Alarm input recording
(B) Manual recording
(C) Schedule recording
Frame rate or CBR
When “VBR” or “Best effort” is set, it will be changed to “Frame rate”
When “VBR” is set, “Max bit rate (per client) may be changed
When the GOP Control is other than “Off”, it will be changed to “Off”
Select an interval (I-frame interval; 0.2 - 5 seconds) to refresh the displayed H.265 (or H.264) images
When “Refresh interval” is longer than “1s”, it will be changed to “1s”

## Slide 12
2.4 Set VMD area
(1) Basic > SD memory card
(2) Image/Audio > Image
Display setup menu
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(A) Alarm input recording
(B) Manual recording
(C) Schedule recording
Set status to “On”
Set [Detection area] and [Detection sensitivity] as necessary

## Slide 13
2.5 Set Schedule
(1) Basic > SD memory card
(2) Image/Audio > Image
Display setup menu
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(A) Alarm input recording
(C) Schedule recording
(B) Manual recording
Set the recording time zone
Select days of a week by checking the respective checkboxes
(A) Alarm input recording : VMD permission
(C) Schedule recording : Recording to SD (Recording stream)

## Slide 14
2.6 Start manual recording
(1) Basic > SD memory card
(2) Image/Audio > Image
Display setup menu
End
(4) Schedule > Schedule
(3) Alarm > VMD area
Start Recording
(B) Manual recording
(A) Alarm input recording
(C) Schedule recording
Click the [Start] / [Stop] button to start / stop manual recording

## Slide 15
3. View recorded data (H.265/H.264)

## Slide 16
3.1 Overview
Notes:
- In case of "Backup for NVR REC", you can play back SD memory backup data on WJ-NX*** after the recorder get the video data from SD memory card automatically
- File format is "mp4", not "n3r" format
Image Compression | Method | Camera browser | ASM300 | PC file Explorer
JPEG | Replay | YES | N/A | YES
 | Download/Copy | YES | N/A | YES
H.265/H.264 | Replay | YES | YES | YES (*)
 | Download/Copy | YES | YES | YES
View recorded data
(*) H.265 images on SD memory card may not be played on Windows 10 due to "Windows 10 Fall Creators Update(Version 1709 / RS3)
See [C0303] for detail (https://security.panasonic.com/training_support/support/technical_information/)
 3.2
 3.2
 3.2
 3.3
 3.4
 3.5
 3.5
 3.5
 3.5
 3.2

## Slide 17
cvcv
3.2 Replay / Download : Camera browser (H.265/H.264/JPEG)
Step1. Click [Log/Play] to show recorded data
Step2 : Select recorded data
Step3 : Replay
Destination directory can be changed in setup menu "Basic>Log"
Notes:
- Only a single user can operate the log list window. Other users cannot access the log list window
- In this process, replay stream is output by TCP (over HTTP)
Replay/download recorded image files on web browser
Step1 : Click download Icon
Replay
Download

## Slide 18
Play on the operation monitor in ASM300
- In one of the camera, the playable Only one user (including browser access, etc.). During replay other users can not play
- It does not support audio replay
Live
3.3 Replay : ASM300
Step1. Select camera and click [SD] tab
Step2. Click [List/Play]
Step3. Set search criteria to narrow down
Step4. Click replay target to start playing
Replay
Live images will be switched to playback images
The live indication displayed in the information display area will turn to the playback indication.

## Slide 19
Download
Download MP4 file from operation monitor of ASM300
- If multiple alarm occurs in the same file, different list is created, but when you download, the same file is downloaded
3.4 Download MP4 : ASM300
Step1. Select camera and click [SD] tab
Step2. Click [List/Play]
Step3. Set search criteria to narrow down
Step4. Select replay target, then click [Download]
Step4. Select replay target, then click [Download]

## Slide 20
Replay : one file
3.5 Replay SD recorded data : PC
Take out SD memory card and view images on the PC
Step1.
Take out SD memory card from camera,
and insert it to the PC
Step2. Double click mp4 file to replay
Note:
Refer to the camera's operating instructions for the folder structure in the SD memory card
<Explorer>

## Slide 21
Replay : multiple files
3.5 Replay SD recorded data : PC - Continuous playback
How to replay multiple files continuously with Windows Media Player
Step2.
Drag and Drop the selected files to Viewer list
Viewer list
Step1.
Select all files to replay
<Explorer>
<Windows Media Player>

## Slide 22
4. Backup for NVR

## Slide 23
4. SD memory backup with recorder (NX-NVR)
Communication
Is disconnected
1
2
Camera start recording to the SD memory card when it fails to communicate with NVR.
NVR retrieve the image from SD memory card a quarter past every hour.
NX-NVR saves only image data to the HDD. Audio and VMD data will not be saved even SD has them
If the SD backup is used, set the operation mode of the SD memory card to "Overwrite On" from the camera side
It can also manually retrieve the image data from Maintenance > System management > Other
After the network is recovered :
The video data on the SD will be transmitted to the recorder automatically.

## Slide 24
4.1.1 Set SD memory card recording
Select “Audio recording” “On”/”Off” for MP4 format.
Audio (in case 2 recording stream) :
When recording audio, recording stream2 must be “Off”
<Do not change here>
End
(5) Recovery & Playback
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
(1) Camera
Basic > SD memory card

## Slide 25
4.1.2 Check SD memory card recording
End
(5) Recovery & Playback
<OK>
Log window is displayed.
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
(1) Camera
Basic > SD memory card
Click “Log/Play” button
<NG>
Alarm message is displayed. Please check if the SDHC memory card is inserted correctly.

## Slide 26
4.2 Set Camera’s time & date (time zone)
End
(5) Recovery & Playback
Synchronization with NTP server
Manual
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
(1) Camera
Basic > SD memory card
NX Recorder’s IP address

## Slide 27
4.3 Set Recorder’s SD backup rec.
(1) Camera
Basic > SD memory card
End
(5) Recovery & Playback
Select “ON”
“Network failure”
Display Camera setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
When above setting is done on NX recorder,
”Network failure” is displayed (gray out)
in save trigger on the SD memory card of [Basic] setup menu of camera.
Camera’s
Setup > Basic > SD memory card

## Slide 28
4.4 Set Recorder’s time & date (time zone)
(1) Camera
Basic > SD memory card
End
(5) Recovery & Playback
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
Time&date
Time zone

## Slide 29
4.5.1 Recovery
(1) Camera
Basic > SD memory card
End
(5) Recovery & Playback
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
Image data backed up on the SD memory card during network failure can be transmitted to the recorder automatically.
During operation of recording, live displaying, playback, the data on the SD memory card can be automatically transmitted to the recorder without interrupting the operation.
Backup data on a camera included pre-recording data(*1) on SD memory card is transmitted one by one every hour(*2) in the case of NX series recorder.
[SD -> HDD] is displayed on the browser when Backup data on a camera is transmitted to NX series recorder.
(*1)A few seconds images before network failure is automatically recorded in SD memory card
(*2)The data recovery (transmission) start every an hour such time as “0:15, 1:15, 2:15, 3:15, ………, 23:15”
Automatically

## Slide 30
4.5.2 Playback ( NX series Recorder )
End
(5) Recovery & Playback
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
(1) Camera
Basic > SD memory card
The data recovered on the recorder can be replayed as shown below
From the recorder’s Web browser : Search events
1.Go to last
2.Advanced setup
3.SD backup rec.

## Slide 31
4.5.3 Playback ( ASM300 )
End
(5) Recovery & Playback
Display setup menu
(2) Camera
Network > Advanced > NTP
(4) NX series recorder
Date/Language
(3) NX series recorder
REC & event > Advanced setup
(1) Camera
Basic > SD memory card
The data recovered on the recorder can be replayed as shown below
From ASM300 operation window : Quick Playback or Event Search
1.Quick Playback
2.SD memory rec.
2.SD memory rec.
1.Search
Quick Playback
Event Search

## Slide 32
5. Other functions

## Slide 33
5.2 Password Lock
Setting a password for the SD memory card, devices other than i-PRO camera will be unable to write or read the SD memory card. It prevent the information leak even if SD memory card is stolen.
[Lock the SD memory card]
By set the password to SD memory card data, the data cannot be read or written by any other equipment except for i-PRO cameras.
Available number of characters: 4-32 characters
Unavailable characters: " & : ;
[Set] :set the password
[Remove] :remove the password
[Change] :change the password
Note:
- This function is supported when using SDHC or SDXC memory card.
‐To replay the data by PC, unlock the SD memory card by the camera before removing the SD card

## Slide 34
5.3 Alteration detection
Alteration detection supports video data (MP4 format) only and can be checked using “MP4IntegrityVerifier” software. To use Alteration detection Certificate is required. (Self-signed Certificate or CA Certificate)
- Alteration detection is used for “Recording stream 1”, and “Off” must be selected for “Recording stream 2”.
- When Alteration detection is enabled, the maximum value of the available bit rate for “Stream” will be limited.
- To confirm alteration, you can download the software “MP4IntegrityVerifier” from website below
https://security.panasonic.com/support/info/
改竄検知情報付加 | Audio | Available bit rate
Off | Off | 12288kbps
 | On | 8192kbps
On | Off | 8192kbps
 | On | 8192kbps

## Slide 35
6. i-PRO SD memory cards

## Slide 36
6.1 i-PRO SD memory card line-ups
Type | Capacity | SD Standard | Model number | Spec | 
SD Memory Card | 32GB | SDHC | WV-SDA032G | 3D NAND TLC Flash Approx. 3000 rewriting times Operating Temperature : -25 degrees c to +85 degree c | Speed Class : Class 10 / U1 /V10 Max. Read : 100MB/s Max. Write : 50MB/s
 | 64GB | SDXC | WV-SDA064G |  | 
 | 128GB |  | WV-SDA128G |  | Speed Class : Class 10 / U3 /V30 Max. Read : 100MB/s Max. Write : 50MB/s
 | 512GB |  | WV-SDA256G |  | 
Micro SD Memory Card | 32GB | Micro SDHC | WV-SDB032G |  | Speed Class : Class 10 / U1 /V10 Max. Read : 100MB/s Max. Write : 50MB/s
 | 64GB | Micro SDXC | WV-SDB064G |  | 
 | 128GB |  | WV-SDB128G |  | Speed Class : Class 10 / U3 /V30 Max. Read : 100MB/s Max. Write : 50MB/s
 | 256GB |  | WV-SDB256G |  | 
https://security.panasonic.com/products_technology/products/function_extension_kits/i-pro_sd_memory_card/

## Slide 37
6.1 Advantage of 3D NAND TLC
Comparison among Flash memory types
capacity
endurance
High
High
SLC MLC TLC
(Single Level Cell) (Multi Level Cell) (Triple Level Cell)
capacity
endurance
High
2D NAND 3D NAND
Memory Type | SLC | MLC | TLC
Stored Information/ Memory Cell | 1 bit / cell | 2 bits / cell | 3 bits / cell
Stored information size per cell by memory type
3D NAND TLC realizes both high capacity and high endurance
Need smaller cell size for more capacity,
But smaller cell size reduce endurance
pile up cells can increase capacity
with keeping cell size

## Slide 38
6.2 Reference : Estimated Recording Hours(H.264/H.265)
Band-width | Size of SD memory card |  |  |  | 
(kbps) | 32GB | 64GB | 128GB | 256GB | 512GB
64 | 1008.3 | 2070.7 | 4152.1 | 8343.9 | 15859.9
96 | 672.0 | 1380.1 | 2767.2 | 5560.8 | 10569.9
112 | 575.9 | 1182.7 | 2371.5 | 4765.6 | 9058.4
128 | 503.8 | 1034.7 | 2074.7 | 4169.3 | 7924.9
192 | 335.7 | 689.4 | 1382.3 | 2777.7 | 5279.9
224 | 287.6 | 590.7 | 1184.4 | 2380.2 | 4524.2
256 | 251.6 | 516.7 | 1036.0 | 2082.0 | 3957.4
320 | 201.1 | 413.1 | 828.3 | 1664.5 | 3163.9
352 | 182.8 | 375.4 | 752.8 | 1512.7 | 2875.4
384 | 167.5 | 344.0 | 689.8 | 1386.2 | 2634.9
448 | 143.5 | 294.7 | 590.9 | 1187.4 | 2257.0
480 | 133.9 | 275.0 | 551.3 | 1107.9 | 2105.9
512 | 125.5 | 257.7 | 516.7 | 1038.3 | 1973.7
640 | 100.2 | 205.9 | 412.8 | 829.6 | 1576.9
768 | 83.4 | 171.4 | 343.6 | 690.5 | 1312.4
896 | 71.4 | 146.7 | 294.1 | 591.1 | 1123.5
1024 | 62.4 | 128.2 | 257.0 | 516.5 | 981.8
1280 | 49.8 | 102.3 | 205.1 | 412.2 | 783.4
1536 | 41.4 | 85.0 | 170.5 | 342.6 | 651.2
1792 | 35.4 | 72.7 | 145.7 | 292.9 | 556.7
2048 | 30.9 | 63.4 | 127.2 | 255.6 | 485.8
3072 | 20.4 | 41.9 | 83.9 | 168.6 | 320.5
4096 | 15.1 | 31.1 | 62.3 | 125.1 | 237.9
6144 | 9.9 | 20.3 | 40.6 | 81.7 | 155.2
8192 | 7.2 | 14.9 | 29.8 | 59.9 | 113.9
10240 | 5.7 | 11.6 | 23.3 | 46.9 | 89.1
12288 | 4.6 | 9.5 | 19.0 | 38.2 | 72.6
Unit: Hours

## Slide 39
6.3 Reference : Replacement cycle (continuous recording)
Bandwidth (kbps) | SD Memory Card |  |  |  | 
 | WV-SDA032G | WV-SDA064G | WV-SDA128G | WV-SDA256G | WV-SDA512G
64 | 5-year | 5-year | 5-year | 5-year | 5-year
96 |  |  |  |  | 
128 |  |  |  |  | 
192 |  |  |  |  | 
224 |  |  |  |  | 
256 |  |  |  |  | 
320 |  |  |  |  | 
352 |  |  |  |  | 
384 |  |  |  |  | 
448 |  |  |  |  | 
480 |  |  |  |  | 
512 |  |  |  |  | 
640 |  |  |  |  | 
768 |  |  |  |  | 
1,024 |  |  |  |  | 
1,280 |  |  |  |  | 
1,536 |  |  |  |  | 
1,792 |  |  |  |  | 
2,048 | 4-year 6-month |  |  |  | 
3,072 | 3-year |  |  |  | 
4,096 | 2-year 3-month |  |  |  | 
6,144 | 1-year 6-month | 3-year 10-month |  |  | 
8,192 | 1-year 1-month | 2-year 11-month |  |  | 
10,240 | 10-month + | 2-year 3-month + | 4-year 6-month + | 5-year + | 5-year +
12,288 | 9-month + | 1-year 11-month + | 3-year 10-month + | 5-year + | 5-year +
Please set the bitrate of recording stream
less than 6,144 kbps
(1) i-PRO S series / X series HD/FHD model

## Slide 40
6.3 Reference : Replacement cycle (continuous recording)
Bandwidth (kbps) | SD Memory Card |  |  |  | 
 | WV-SDA032G | WV-SDA064G | WV-SDA128G | WV-SDA256G | WV-SDA512G
64 | 5-year | 5-year | 5-year | 5-year | 5-year
96 |  |  |  |  | 
128 |  |  |  |  | 
192 |  |  |  |  | 
224 |  |  |  |  | 
256 |  |  |  |  | 
320 |  |  |  |  | 
352 |  |  |  |  | 
384 |  |  |  |  | 
448 |  |  |  |  | 
480 |  |  |  |  | 
512 |  |  |  |  | 
640 |  |  |  |  | 
768 |  |  |  |  | 
1,024 |  |  |  |  | 
1,280 |  |  |  |  | 
1,536 |  |  |  |  | 
1,792 |  |  |  |  | 
2,048 | 4-year 6-month |  |  |  | 
3,072 | 3-year |  |  |  | 
4,096 | 2-year 3-month |  |  |  | 
6,144 | 1-year 6-month | 3-year 10-month |  |  | 
8,192 | 1-year 1-month | 2-year 11-month |  |  | 
10,240 | 10-month + | 2-year 3-month + | 4-year 6-month + | 5-year + | 5-year +
12,288 | 9-month + | 1-year 11-month + | 3-year 10-month + | 5-year + | 5-year +
Please set the bitrate of recording stream less than 8,192 kbps
(2) i-PRO S series / X series 5M/4K model

## Slide 41
6.3 Reference : Replacement cycle (continuous recording)
Please set the bitrate of recording stream
less than 6,144 kbps
Bandwidth (kbps) | SD Memory Card |  |  | 
 | WV-SDB032G | WV-SDB064G | WV-SDB128G | WV-SDB256G
64 | 5-year | 5-year | 5-year | 5-year
96 |  |  |  | 
128 |  |  |  | 
192 |  |  |  | 
224 |  |  |  | 
256 |  |  |  | 
320 |  |  |  | 
352 |  |  |  | 
384 |  |  |  | 
448 |  |  |  | 
480 |  |  |  | 
512 |  |  |  | 
640 |  |  |  | 
768 |  |  |  | 
1,024 |  |  |  | 
1,280 |  |  |  | 
1,536 |  |  |  | 
1,792 |  |  |  | 
2,048 | 4-year 6-month |  |  | 
3,072 | 3-year |  |  | 
4,096 | 2-year 3-month |  |  | 
6,144 | 1-year 6-month | 3-year 10-month |  | 
8,192 | 1-year 1-month | 2-year 11-month |  | 
10,240 | 10-month + | 2-year 3-month + | 4-year 6-month + | 5-year +
12,288 | 9-month + | 1-year 11-month + | 3-year 10-month + | 5-year +
Please set the bitrate of recording stream
less than 6,144 kbps
(1) i-PRO U series model

## Slide 42
Appendix

## Slide 43
Differences in support functions
Category | Camera Type | Model List | Supported Card | # of Rec. stream on SD | VBR support in SD Rec.
i-PRO EXTREME Series Group 1 | Box / Dome | S1111 / S1112 / S1131* / S1132* / S1432LH / S1511LN / S1531* S2111L / S2131* / S2132* / S2211L / S2231L / S2511LN / S2531* / S2532LH | SDXC/SDHC/SD | 2 | -
 | Compact Dome | S3111L / S3131L / S3511L / S3512LM / S3531L / S3532LM | micro SDXC | 2 | -
 | PTZ | S6111 / S6130* / S6131* / S6530* / S6532* / X6511N / X6531* / X6533* | SDXC/SDHC/SD | 2 | -
i-PRO EXTREME Series Group 2 | Box / Dome | S1550* / S1570* / S2250L / S2550* / S2270* / S2570L | SDXC/SDHC/SD | 1 | -
 | 360-degree | S4150 / S4550* / X4170* / X4171 / X4571* | SDXC/SDHC/SD | 1 | -
 | Multi-Sensor | S8530N / X8570 | SDXC/SDHC/SD | 1 | -
i-PRO EXTREME Series Group 3 (U Series) | Box / Dome | U1130 / U1132 / U1142 / U1532L / U1542L U2130L / U2132L / U2140L / U2142L / U2530L / U2532L / U2540L / U2542L | microSDXC/microSDHC/microSD | 1 | -
i-PRO EXTREME Series Group 4 | Box / Dome | S1552L / S1572L / S2252L / S2272L / S2552L / S2572L | SDXC/SDHC/SD | 1 | -
 | 360-degree | S4151 / S4551* / X4172 / X4173 / X4573* | SDXC/SDHC/SD | 1 | -
 | Multi-Sensor | S8531N / X8571N | SDXC/SDHC/SD | 1 | -
i-PRO with AI engine Series Group 1 | Box / Dome | X1551LN / X1571LN / X2251L / X2271L / X2551LN / X2571LN | SDXC/SDHC/SD | 1 | -
i-PRO with AI engine Series Group 2 | Box / Dome | S1136 / S1536 / S2136 / S2236L / S2536 | microSDXC/microSDHC/microSD | 1 | Yes
i-PRO SmartHD 4K | Box / Dome | SFV781L/SPV781L | SDXC/SDHC/SD | 1 | -
i-PRO SmartHD | Box / Dome | SW175 | SDHC/SD | 1 | -
There are differences in support functions depending on the model.

## Slide 44
Related information
Contents | Media | URL
Support Information for SD memory card | - | SD_Memory_Card_1624504425.9162.pdf (panasonic.net)
Restriction on use of i-PRO SD Memory Card | - | i-PRO_SD_Restriction.pdf (psn-web.net)
Recording Hours on SD memory Card | H.264/H.265 | sd_h264h265-en.pdf (psn-web.net)
Estimated storable number | JPEG | sd_jpeg-en.pdf (psn-web.net)
Replacement Cycle (Guideline) | H.264/H.265 | SD_Mem_Card_Replacement_Cycle_H264H265_en.pdf (psn-web.net)
Replacement Cycle (Guideline) | JPEG | SD_Mem_Card_Replacement_Cycle_JPEG_en.pdf (psn-web.net)

## Slide 45
Version History

## Slide 46
Version History
No | Update contents | Page No. | Version | Update
1 | 1st Version | - | 1.00 | 26.Jul.2021
2 | Refine section 3 | P.15 - 20 | 1.10 | 23.Aug.2021
3 | Add “Related information” to Appendix | P.43 | 1.10 | 23.Aug.2021
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  |