## Slide 1
i-PRO 360-degree Fisheye Camera
with AI engine Material for SE
Aug. 2022
Document Ver.1.06
Model: WV-S4156 , WV-S4556L , WV-S4556LM WV-S4176 , WV-S4576L , WV-S4576LM

## Slide 2
Contents
Product Summary
Key Features
Specification Comparison
Other Specifications
AI Applications
Appearance
Standard Accessories
Optional Accessories
About icons
This icon is for brand new functions

## Slide 3
1. Product Summary

## Slide 4
1-1. Product Concept
Key features
High
Visibility
High Compression
AI Smart Object Coding
- The object detection accuracy has been improved, and the non-detection area can be further compressed. (Approx. 50 % reduction compared to conventional models.)
Intelligent Auto
- The visibility of blurring object (human and vehicles) has been improved by object detection.
By utilizing AI-based precision analytics, the new 360-degree camera can take advantage of high visibility, high compression, and various applications
High
Accuracy
AI Analytics
- Support new dedicated AI application.
(AI-VMD, People Counting, Heat Map, Occupancy Detection, AI Privacy Guard, AI Sound Classification )
Release in Nov. 2021
Indoor
WV-S4156
Outdoor
WV-S4556L
12MP model
Outdoor(transit)
WV-S4556LM
5MP model
360-degree camera with AI engine
Release in Nov. 2021
Indoor
WV-S4176
Outdoor
WV-S4576L
Outdoor(transit)
WV-S4576LM

## Slide 5
1-2. Model Transition
 | Conventional model |  |  | New model | 
Indoor | 1 | WV-S4151 |  | 1 | WV-S4156
Outdoor | 2 | WV-S4551L WV-S4551LM |  | 2 | WV-S4556L WV-S4556LM
 | Conventional model |  |  | New model | 
Indoor (elementary model) | 1 | WV-X4172 |  |  | 
Indoor | 1 | WV-X4173 |  | 1 | WV-S4176
Outdoor | 2 | WV-X4573L WV-X4573LM |  | 2 | WV-S4576L WV-S4576LM
Replace
Continue
Replace
5MP model
12MP model

## Slide 6
2. Key Features

## Slide 7
2-1. Intelligent Auto
The visibility of blurring object (human and vehicles) has been improved by object detection.
Automatically optimize the image depending on the environment
Intelligent Auto : ON
Intelligent Auto : OFF

## Slide 8
2-2. AI Smart Object Coding - Smart VIQS
The object detection accuracy has been improved, and the non-detection area can be further compressed. (Approx. 50 % reduction compared to conventional models)
Conventional model
Person on the image does not move
Image quality is adjusted to low
Swaying tree is recognized as a moving object
Increase data amount
New model
Swaying tree is NOT recognized as an object
Suppress data amount
Camera detect “face” and “human”
Adjusts the image quality of the face area to high
Measured bit rate: 6733kbps
Measured bit rate: 3855kbps
Automatically control the compression rate depending on the environment
Detects motion and automatically adjusts the image quality of moving objects to high and others to low.
Detects objects (face, human and vehicle) and adjusts the image quality of those objects to high and others to low.

## Slide 9
2-3. AI Smart Object Coding - GOP control
Control GOP using object detection instead of motion detection
GOP control | 
Low (Variable GOP 1s-8s) | I-picture interval variable between 1sec-8sec by detected object (People and vehicles). *VBR only
Mid (Variable GOP 4s-16s) | I-picture interval variable between 4sec-16sec by detected object. *VBR only
Advanced (Fixed GOP 60s w/1s key-frame) | I-picture interval fixed at 60s, key-frame inserted at 1sec intervals regardless of detected object. *Selectable in all transfer modes
Frame rate control (Variable GOP 4s-16s w/frame rate control) | If there is no detected object, reduce the frame rate to 1 fps. I-picture interval variable between 4sec-16sec by detected object. *VBR only
Object
No Object
Low / Mid
Advanced
Frame rate control
Object
No Object

## Slide 10
2-4. AI Analytics
 | App. #1 : AI-VMD / AI People Counting |  |  |  | App. #2 : AI Privacy Guard | Standard feature
Function | AI-VMD | People Counting | Heat Map | Occupancy Detection | AI Privacy Guard | AI Sound Classification
Detail | - Intruder detection - Line cross detection - Loitering detection | - Cross Line Counting - Area Counting | Visualization of loitering / passing | An alarm is issued when the number of people exceeds the set value | Cover people on the video stream | Identifying a specific sound among other noises
Target object | People / Vehicle | People | People | People | People | Sound
Output data | Alarm | Meta information | Meta information | Alarm | Stream | Alarm
Output method | ONVIF, CGI, TCP alarm protocol, Additional information in video stream | ONVIF *1, CGI, Additional information in video stream, HTTP POST, MQTT *2 | ONVIF *1, CGI | ONVIF, TCP alarm protocol, Additional information in video stream | Stream | ONVIF, CGI, TCP alarm protocol, Additional information in video stream
Support new dedicated AI application for 360-degree camera
30
25
*1 Data format is proprietary.
*2 Will be supported by firmware upgrade in the future.

## Slide 11
3. Specification Comparison

## Slide 12
3-1. Overview
 | New 360-degree camera (WV-S4156/WV-S4556L/WV-S4556LM/ WV-S4176/WV-S4576L/WV-S4576LM) | Conventional 360-degree camera (WV-S4151/WV-S4551L/WV-S4551LM/ WV-X4172/WV-X4173/WV-X4573L/WV-X4573LM)
Intelligent Auto | Yes (AI) | Yes (Non-AI)
Smart Coding | Smart VIQS (AI) GOP control (AI) | Auto VIQS (Non-AI) GOP control (Non-AI)
Scene change detection alarm | Standard feature | Option (i-VMD)
Audio alarm | Yes Detection by sound volume AI Sound Classification (Gunshot, Yell, Vehicle horn, Glass break) | No
Extension software | App. #1 : AI-VMD/People Counting/Heat Map/Occupancy Detection App. #2 : AI Privacy Guard | WV-SAE200W : i-VMD/People Counting (Non-AI) /Heat Map (Non-AI) WV-SAE303W : People Counting
No change in hardware except increase of Flash ROM/Memory (in comparison with conventional 360-degree camera)
Software specification
Hardware specification

## Slide 13
3-2. Comparison to other companies - vs Axis / Hanwha
5MP model
 | i-PRO |  | Axis |  | Hanwha | 
 | Outdoor | Indoor | Outdoor | Indoor | Outdoor | Indoor
 | WV-S4556L WV-S4556LM | WV-S4156 | M3057-PLVE Mk II | M3067-P | XNF-8010RV XNF-8010RVM | XNF-8010R
Video Codec | H.265/H.264/JPEG |  | H.265/H.264/JPEG |  | H.265/H.264/JPEG | 
Image Sensor | 1/2.8” 5MP |  | 1/1.8” 6MP |  | 1/1.8" 6MP | 
Max Resolution | 2192x2192 |  | 2016x2016 |  | 2048x2048 | 
Max Frame rate | H.265/H.264 : 30fps JPEG : 5fps (30fps *1) |  | H.265/H.264 : 30fps (60fps *2) JPEG : 30fps (60fps *2) |  | H.265/H.264 : 30fps JPEG : 15fps | 
Lens | F2.4 |  | F2.0 |  | F1.6 | 
Angular Field of view | 186 deg. |  | 183 deg. | 185 deg. | 192 deg. | 
Dynamic range | 120dB |  | 120dB |  | 120dB | 
Sensitivity (color) | 0.15 lx |  | 0.16lx | 0.18lx | 0.1lx | 
Display mode (other than fisheye) | Panorama, Double panorama, Single PTZ, Quad PTZ 4Quad streams |  | Panorama, Double panorama, Single PTZ, Quad PTZ, Corner left/right, Double corner, Corridor |  | Panorama, Double Panorama, Single PTZ, Quad PTZ | 
Smart Coding | Smart VIQS / GOP control |  | Zipstream |  | WiseStream II | 
Audio | In(mic in), Out | In(built-in mic), Out | - |  | In(selectable), Out | 
AI processor | Yes |  | No |  | No | 
Video Analytics | AI-VMD, People Counting, Heat Map, Occupancy Detection, AI Privacy Guard , AI Sound Classification |  | VMD, active tampering alarm, Motion Guard, Fence Guard, Loitering Guard, People Counter, Occupancy Estimator, Queue Monitor, Tailgating Detector, Direction Detector, Random Selector |  | Defocus detection, Motion detection, Tampering, People counting, Heat map, Directional detection, Appear/Disappear, Enter/Exit, Loitering, Virtual line, Audio detection, Sound classification | 
IR-LED | Yes (10m) | - | Yes (20m) | - | Yes(15m) | 
Operating Temperature | -40 to +60 deg.C | -10 to +50 deg.C | -40 to +50 deg.C | 0 to +40 deg.C | -40 to +55 deg.C | -10 to +55 deg.C
Railway standard | EN50155-TX | - | - |  | EN50155 | -
*1 H.265/H.264 Stream transmission: Off,
Display mode: fisheye/Panorama/Double panorama/Single PTZ/Quad PTZ
*2 WDR: Off, Display mode: only fisheye

## Slide 14
3-2. Comparison to other companies - vs Avigilon
5MP model
 | i-PRO |  | Avigilon | 
 | Outdoor | Indoor | Outdoor | Indoor
 | WV-S4556L WV-S4556LM | WV-S4156 | 8.0C-H5A-FE-DO1-IR | 8.0C-H5A-FE-DC1
Video Codec | H.265/H.264/JPEG |  | H.265/H.264/JPEG | 
Image Sensor | 1/2.8” 5MP |  | 1/1.8” 8MP | 
Max Resolution | 2192x2192 |  | 2048x2048 | 
Max Frame rate | H.265/H.264 : 30fps JPEG : 5fps (30fps *1) |  | H.265/H.264 : 30fps JPEG : 30fps | 
Lens | F2.4 |  | F2.0 | 
Angular Field of view | 186 deg. |  | 180 deg. | 
Dynamic range | 120dB |  | 120dB | 
Sensitivity (color) | 0.15 lx |  | 0.20lx | 
Display mode (other than fisheye) | Panorama, Double panorama, Single PTZ, Quad PTZ 4Quad streams |  | Adjustable dewarping | 
Smart Coding | Smart VIQS / GOP control |  | High Definition Stream Management | 
Audio | In(mic in), Out | In(built-in mic), Out | In(built-in mic), Out | 
AI processor | Yes |  | Yes | 
Video Analytics | AI-VMD, People Counting, Heat Map, Occupancy Detection, AI Privacy Guard , AI Sound Classification |  | Objects in Area, Loitering, Crossing Beam, Appears or Enters Area, Not Present in Area, Enter Area, Leave Area, Stops in Area, Direction Violated, Tamper Detection | 
IR-LED | Yes (10m) | - | Yes (17m) | -
Operating Temperature | -40 to +60 deg.C | -10 to +50 deg.C | -40 to +60 deg.C | -10 to +60 deg.C
Railway standard | EN50155-TX | - | - | 
*1 H.265/H.264 Stream transmission: Off,
Display mode: fisheye/Panorama/Double panorama/Single PTZ/Quad PTZ

## Slide 15
3-2. Comparison to other companies - vs Axis / Hanwha
12MP model
*1 H.265/H.264 Stream transmission: Off,
Display mode: fisheye/Panorama/Double panorama/Single PTZ/Quad PTZ
 | i-PRO |  | Axis |  | Hanwha | 
 | Outdoor | Indoor | Outdoor | Indoor | Outdoor | Indoor
 | WV-S4576L WV-S4576LM | WV-S4176 | M3058-PLVE | M3068-P | XNF-9010RV XNF-9010RVM | QNF-9010
Video Codec | H.265/H.264/JPEG |  | H.264/JPEG | H.265/H.264/JPEG | H.265/H.264/JPEG | 
Image Sensor | 1/1.7” 12MP |  | 1/1.7” 12MP |  | 1/2.3” 12MP | 
Max Resolution | 2992x2992 |  | 2992x2992 | 2880x2880 | 3008x3008 | 
Max Frame rate | H.265/H.264 : 30fps JPEG : 5fps (15fps *1) |  | H.265/H.264 : 15fps (30fps *2) JPEG : 15fps (30fps *2) |  | H.265/H.264 : 30fps JPEG : 30fps | H.265/H.264 : 30fps JPEG : 5fps
Lens | F1.9 |  | F2.2 | F2.8 | F2.2 | 
Angular Field of view | 183 deg. |  | 181 deg. | 185 deg. | 187 deg. | 
Dynamic range | 84dB |  | 120dB |  | 120dB | 
Sensitivity (color) | 0.3 lx |  | 0.19lx | 0.32lx | 0.39lx | 
Display mode (other than fisheye) | Panorama, Double panorama, Single PTZ, Quad PTZ 4Quad streams |  | Panorama, Double panorama, Single PTZ, Quad PTZ, Corner left/right, Double corner, Corridor |  | Panorama, Double Panorama, Single PTZ, Quad PTZ | 
Smart Coding | Smart VIQS / GOP control |  | Zipstream |  | WiseStream II | 
Audio | In(mic in), Out | In(built-in mic), Out | - |  | In(selectable), Out | -
AI processor | Yes |  | No |  | No | 
Video Analytics | AI-VMD, People Counting, Heat Map, Occupancy Detection, AI Privacy Guard , AI Sound Classification |  | VMD, active tampering alarm, Motion Guard, Fence Guard, Loitering Guard, (People Counter, Occupancy Estimator, Queue Monitor, Tailgating Detector, Direction Detector, Random Selector) * ( ) Is for M3068-P only |  | Defocus detection, Motion detection, Tampering, People counting, Heat map (Directional detection, Appear/Disappear, Enter/Exit, Loitering, Virtual line, Audio detection, Sound classification) * ( ) Is for XNF-9010RV/XNF-9010RVM only | 
IR-LED | Yes (10m) | - | Yes (15m) | - | Yes (10m) | -
Operating Temperature | -40 to +60 deg.C | -10 to +50 deg.C | -40 to +50 deg.C | 0 to +40 deg.C | -40 to +60 deg.C | -10 to +40 deg.C
Railway standard | EN50155-TX | - | - |  | EN50155 | -
*2 WDR: Off, Display mode: only fisheye

## Slide 16
3-2. Comparison to other companies - vs Avigilon
12MP model
*1 H.265/H.264 Stream transmission: Off,
Display mode: fisheye/Panorama/Double panorama/Single PTZ/Quad PTZ
 | i-PRO |  | Avigilon | 
 | Outdoor | Indoor | Outdoor | Indoor
 | WV-S4576L WV-S4576LM | WV-S4176 | 12.0W-H5A-FE-DO1-IR | 12.0W-H5A-FE-DC1
Video Codec | H.265/H.264/JPEG |  | H.265/H.264/JPEG | 
Image Sensor | 1/1.7” 12MP |  | 1/2.3” 12MP | 
Max Resolution | 2992x2992 |  | 3008x3008 | 
Max Frame rate | H.265/H.264 : 30fps JPEG : 5fps (15fps *1) |  | H.265/H.264 : 30fps JPEG : 30fps | 
Lens | F1.9 |  | F2.0 | 
Angular Field of view | 183 deg. |  | 180 deg. | 
Dynamic range | 84dB |  | 120dB | 
Sensitivity (color) | 0.3 lx |  | 0.38lx | 
Display mode (other than fisheye) | Panorama, Double panorama, Single PTZ, Quad PTZ 4Quad streams |  | Adjustable dewarping | 
Smart Coding | Smart VIQS / GOP control |  | High Definition Stream Management | 
Audio | In(mic in), Out | In(built-in mic), Out | In(built-in mic), Out | 
AI processor | Yes |  | Yes | 
Video Analytics | AI-VMD, People Counting, Heat Map, Occupancy Detection, AI Privacy Guard , AI Sound Classification |  | Objects in Area, Loitering, Crossing Beam, Appears or Enters Area, Not Present in Area, Enter Area, Leave Area, Stops in Area, Direction Violated, Tamper Detection | 
IR-LED | Yes (10m) | - | Yes (12m) | -
Operating Temperature | -40 to +60 deg.C | -10 to +50 deg.C | -40 to +60 deg.C | -10 to +60 deg.C
Railway standard | EN50155-TX | - | - | 

## Slide 17
3-3. Comparison with conventional models
 | New 5MP Camera (WV-S4156 / S4556L / S4556LM) | Conventional 5MP Camera (WV-S4151 / S4551L / S4551LM) | Conventional 5MP Camera (WV-S4150 / S4550L / S4550LM)
Image capture mode | Fisheye / Double Panorama(DP) / Panorama(P) / Quad PTZ / Single PTZ / Fisheye + DP / Fisheye + P / Fisheye + Quad PTZ / Quad stream |  | 
Compression method | H.265[or H.264](1)(2) / JPEG(1)(2) |  | 
Dynamic range | Super-D 120dB |  | Super-D 108dB
Sensitivity (color) | 0.15lx |  | 0.3lx
Transmission mode | VBR / CBR / Framerate / Best Effort *Default : VBR |  | VBR / CBR / Framerate / Best Effort *Default : Framerate
Intelligent Auto | Yes (AI) | Yes (Non-AI) | 
Smart Coding | Smart VIQS (AI) / GOP control (AI) | Auto VIQS (Non-AI) / GOP control (Non-AI) | 
SD recording | Yes (JPEG / H.264 / H.265) |  | 
IO terminal / Monitor output | Yes |  | 
Power Source | PoE / DC12V |  | 
Scene change detection alarm | Standard feature | Option (WV-SAE200W) | 
Audio alarm | Yes (Audio Detection / AI Sound classification) | No | 
Extension software | App. #1 : AI-VMD / People Counting / Heat Map / Occupancy Detection App. #2 : AI Privacy Guard | WV-SAE200W : i-VMD / People Counting (Non-AI) / Heat map (Non-AI) WV-SAE303W : People Counting (Non-AI) | 
ONVIF | Profile S / G / T / M *1 | Profile S / G / T | 
FTP | No *2 |  | Yes
5MP model
*1 Will declare profile M support after we got certified by ONVIF.
*2 SFTP will be supported by firmware upgrade in the future.

## Slide 18
3-3. Comparison with conventional models
 | New 12MP Camera (WV-S4176 / S4576L / S4576LM) | Conventional 12MP Camera (WV-X4172 / X4173 / X4573L / X4573LM) | Conventional 12MP Camera (WV-X4170 / X4171 / X4571L / X4571LM)
Image capture mode | Fisheye / Double Panorama(DP) / Panorama(P) / Quad PTZ / Single PTZ / Fisheye + DP / Fisheye + P / Fisheye + Quad PTZ / Quad stream |  | 
Compression method | H.265[or H.264](1)(2) / JPEG(1)(2) |  | 
Dynamic range | WDR 84dB |  | Super-D 108dB
Sensitivity (color) | 0.3lx |  | 
Transmission mode | VBR / CBR / Framerate / Best Effort *Default : VBR |  | VBR / CBR / Framerate / Best Effort *Default : Framerate
Intelligent Auto | Yes (AI) | Yes (Non-AI) | 
Smart Coding | Smart VIQS (AI) / GOP control (AI) | Auto VIQS (Non-AI) / GOP control (Non-AI) | 
SD recording | Yes (JPEG / H.264 / H.265) |  | 
IO terminal / Monitor output | Yes *WV-X4170 / X4172 is not supported |  | 
Power Source | PoE / DC12V *WV-X4170 / X4172: PoE only |  | 
Scene change detection alarm | Standard feature | Option (WV-SAE200W) | 
Audio alarm | Yes (Audio Detection / AI Sound classification) | No | 
Extension software | App. #1 : AI-VMD / People Counting / Heat Map / Occupancy Detection App. #2 : AI Privacy Guard | WV-SAE200W : i-VMD / People Counting (Non-AI) / Heat map (Non-AI) WV-SAE303W : People Counting (Non-AI) *WV-X4170 / X4172 is not supported | 
ONVIF | Profile S / G / T / M *1 | Profile S / G / T | 
FTP | No *2 |  | Yes
12MP model
*1 Will declare profile M support after we got certified by ONVIF.
*2 SFTP will be supported by firmware upgrade in the future.

## Slide 19
4. Other Specifications

## Slide 20
4-1. DORI
*1
5MP model
Resolution : 2192 x 2192 |  | Unit : m | Unit : feet
Detect | 25ppm / 8ppf | 38.0 | 124.7
Observe | 62.5ppm / 19ppf | 13.2 | 43.3
Recognize | 125ppm / 38ppf | 4.3 | 14.1
Identify | 250ppm / 76ppf | - | -
DORI coverage DORI (Detect, Observe, Recognize, Identify) is a standard system (EN-62676-4) for defining the ability of a camera to distinguish persons or objects within a covered area. This value does not indicate the performance of the camera.
The maximum distance at which a camera/lens combination can meet these criteria is shown below:
Distance to object in center image
Detect
Observe
Recognize
Identify
Coverage radius when mounted at a height of 3m (10ft)
3m
(10ft)
D O R I
Resolution : 2192 x 2192 |  | Unit : m | Unit : feet
Detect | 25ppm / 8ppf | 20.7 | 67.9
Observe | 62.5ppm / 19ppf | 8.3 | 27.2
Recognize | 125ppm / 38ppf | 4.1 | 13.5
Identify | 250ppm / 76ppf | 2.1 | 6.9
Identify
Recognize
Observe
Detect

## Slide 21
4-1. DORI
*1
12MP model
Resolution : 2992 x 2992 |  | Unit : m | Unit : feet
Detect | 25ppm / 8ppf | 56.1 | 184.1
Observe | 62.5ppm / 19ppf | 20.6 | 67.6
Recognize | 125ppm / 38ppf | 8.4 | 27.6
Identify | 250ppm / 76ppf | 0.3 | 1.0
DORI coverage DORI (Detect, Observe, Recognize, Identify) is a standard system (EN-62676-4) for defining the ability of a camera to distinguish persons or objects within a covered area. This value does not indicate the performance of the camera.
The maximum distance at which a camera/lens combination can meet these criteria is shown below:
Distance to object in center image
Detect
Observe
Recognize
Identify
Coverage radius when mounted at a height of 3m (10ft)
3m
(10ft)
Identify
Recognize
Observe
Detect
D O R I
Resolution : 2992 x 2992 |  | Unit : m | Unit : feet
Detect | 25ppm / 8ppf | 29.9 | 98.1
Observe | 62.5ppm / 19ppf | 12.0 | 39.4
Recognize | 125ppm / 38ppf | 6.0 | 19.7
Identify | 250ppm / 76ppf | 3.0 | 9.8

## Slide 22
4-2. Supported resolution
5MP model
*1
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
1 | Fisheye (Ceiling / Wall) | Fisheye 2192x2192 1280x1280 640x640 320x320 | Fisheye 1280x1280 640x640 320x320 | Fisheye 2192x2192 1280x1280 640x640 320x320 | Fisheye 1280x1280 640x640 320x320
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 | Max 5(4.2) fps *2
2 | Double Panorama (Ceiling) | Double Panorama 1920x1080 1280x720 640x360 320x180 | Double Panorama 1280x720 640x360 320x180 | Double Panorama 1920x1080 1280x720 640x360 320x180 | Double Panorama 1280x720 640x360 320x180
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 | Max 5(4.2) fps *2
3 | Panorama (Wall) | Panorama 1920x1080 1280x720 640x360 320x180 | Panorama 1280x720 640x360 320x180 | Panorama 1920x1080 1280x720 640x360 320x180 | Panorama 1280x720 640x360 320x180
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 | Max 5(4.2) fps *2
*1 Up to 15fps(12.5fps) when Super Dynamic level is set to 30 or more.
*2 When "Off is selected for each stream transmission" and "none of the conditions of *1 are met", maximum framerate is 30fps(25fps).
*Underline is default value

## Slide 23
4-2. Supported resolution
5MP model
*1
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
4 | Quad PTZ (Ceiling / Wall) | Quad PTZ 1600x1200 1280x960 800x600 VGA QVGA | Quad PTZ 1280x960 VGA QVGA | Quad PTZ 1600x1200 1280x960 800x600 VGA QVGA | Quad PTZ 1280x960 VGA QVGA
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 | Max 5(4.2) fps *2
5 | Single PTZ (Ceiling / Wall) | Single PTZ 1600x1200 1280x960 800x600 VGA QVGA | Single PTZ 1280x960 VGA QVGA | Single PTZ 1600x1200 1280x960 800x600 VGA QVGA | Single PTZ 1280x960 VGA QVGA
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 | Max 5(4.2) fps *2
6 | Fisheye + Double Panorama (Ceiling) | Fisheye 2192x2192 1280x1280 640x640 320x320 | Double Panorama 1280x720 640x360 320x180 | Fisheye 2192x2192 1280x1280 640x640 320x320 | Double Panorama 1280x720 640x360 320x180
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
*1 Up to 15fps(12.5fps) when Super Dynamic level is set to 30 or more.
*2 When "Off is selected for each stream transmission" and "none of the conditions of *1 are met", maximum framerate is 30fps(25fps).
*3 When "Off is selected for each stream transmission", maximum framerate is 15fps(12.5fps).

## Slide 24
4-2. Supported resolution
5MP model
*1
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
7 | Fisheye + Panorama (Wall) | Fisheye 2192x2192 1280x1280 640x640 320x320 | Panorama 1280x720 640x360 320x180 | Fisheye 2192x2192 1280x1280 640x640 320x320 | Panorama 1280x720 640x360 320x180
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
8 | Fisheye + Quad PTZ (Ceiling / Wall) | Fisheye 2192x2192 1280x1280 640x640 320x320 | Quad PTZ 1280x960 800x600 VGA QVGA | Fisheye 2192x2192 1280x1280 640x640 320x320 | Quad PTZ 1280x960 800x600 VGA QVGA
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
9 | Quad Stream (Ceiling) | Single PTZ (Ch1-Ch4) 1280x960 800x600 VGA QVGA | Quad PTZ 1600x1200 1280x960 800x600 VGA QVGA |  | 
 |  | Max 30(25) fps *1 | Max 5(4.2) fps |  | 
*1 Up to 15fps(12.5fps) when Super Dynamic level is set to 30 or more.
*3 When "Off is selected for each stream transmission", maximum framerate is 15fps(12.5fps).

## Slide 25
4-2. Supported resolution
12MP model
*1
*1 Up to 15fps(12.5fps) when Super Dynamic level is set to 30 or more.
*2 If the image capture mode is Fisheye while “Stream transmission” of Stream(1) or Stream(2) is set to “On”, max. 1fps is set for resolution
“2992 x 2992”, and max. 2 fps is set in 30fps mode and max. 2.1fps is set in 25fps mode for resolution “2192 x 2192”. (See page 27)
*3 When "Off is selected for each stream transmission", maximum framerate is 15fps(12.5fps).
*Underline is default value
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
1 | Fisheye (Ceiling / Wall) | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Fisheye 1280x1280 640x640 320x320 | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Fisheye 640x640
 |  | Max 30(25) fps *1 | Max 30(25) fps *1 | Max 5(4.2) fps *2 *3 | Max 5(4.2) fps *2 *3
2 | Double Panorama (Ceiling) | Double Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | Double Panorama 1920x1080 1280x720 640x360 320x180 | Double Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | Double Panorama 1920x1080 1280x720 640x360 320x180
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
3 | Panorama (Wall) | Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | Panorama 1920x1080 1280x720 640x360 320x180 | Panorama 2560x1440 1920x1080 1280x720 640x360 320x180 | Panorama 1920x1080 1280x720 640x360 320x180
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps *3 | Max 5(4.2) fps *3

## Slide 26
4-2. Supported resolution
12MP model
*1
*3 When "Off is selected for each stream transmission", maximum framerate is 15fps(12.5fps).
*4 When “<Wall> Single PTZ” is selected for the image capture mode, 2560 x 1920 cannot be set to Stream(1) and JPEG(1).
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
4 | Quad PTZ (Ceiling / Wall) | Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA QVGA | Quad PTZ 1280x960 800x600 VGA QVGA | Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA QVGA | Quad PTZ 1280x960 800x600 VGA QVGA
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
5 | Single PTZ (Ceiling / Wall) | Single PTZ 2560x1920 *4 2048x1536 1600x1200 1280x960 800x600 VGA, QVGA | Single PTZ 1280x960 800x600 VGA QVGA | Single PTZ 2560x1920 *4 2048x1536 1600x1200 1280x960 800x600 VGA, QVGA | Single PTZ 1280x960 800x600 VGA QVGA
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps *3 | Max 5(4.2) fps *3
6 | Fisheye + Double Panorama (Ceiling) | Fisheye 2992x2992 2192x2192 1280x1280 640x640, 320x320 | Double Panorama 1280x720 640x360 320x180 | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Double Panorama 1280x720 640x360 320x180
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps | Max 5(4.2) fps

## Slide 27
4-2. Supported resolution
12MP model
*1
No. | Image capture mode | Stream (1) | Stream (2) | JPEG (1) | JPEG (2)
7 | Fisheye + Panorama (Wall) | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Panorama 1280x720 640x360 320x180 | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Panorama 1280x720 640x360 320x180
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps | Max 5(4.2) fps
8 | Fisheye + Quad PTZ (Ceiling / Wall) | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Quad PTZ 1280x960 800x600 VGA QVGA | Fisheye 2992x2992 2192x2192 1280x1280 640x640 320x320 | Quad PTZ 1280x960 800x600 VGA QVGA
 |  | Max 15(12.5) fps | Max 15(12.5) fps | Max 5(4.2) fps | Max 5(4.2) fps
9 | Quad Stream (Ceiling) | Single PTZ (Ch1-Ch4) 1280x960 800x600 VGA QVGA | Quad PTZ 2560x1920 2048x1536 1600x1200 1280x960 800x600 VGA QVGA |  | 
 |  | Max 15(12.5) fps | Max 5(4.2) fps |  | 

## Slide 28
Ref. JPEG refresh interval restrictions
Image capture mode : Fisheye
12MP model
 |  | JPEG(1) |  | JPEG(2) | 
 |  | 30fps mode | 25fps mode | 30fps mode | 25fps mode
JPEG(1) Resolution | 2992x2992 | 1fps | 1fps | 1fps | 1fps
 | 2192x2192 | 2fps | 2.1fps | 2fps | 2.1fps
 | 1280x1280 | 5fps | 4.2fps | 5fps | 4.2fps
 | 640x640 | 5fps | 4.2fps | 5fps | 4.2fps
 | 320x320 | 5fps | 4.2fps | 5fps | 4.2fps

## Slide 29
4-3. Important notice for Double Panorama Image cropping position
Conventional model *1
New model
TOP
*1 WV-S4150 / S4550L / S4550LM / X4170 / X4171 / X4571L / X4571LM
Cropping
position
When using a double panorama, align the TOP2 direction of the template with the shooting direction
(upper direction of the screen).
Front for Fisheye
Front for Double Panorama
TOP2

## Slide 30
4-4. Limitation for position adjustment in Double Panorama
Conventional model *1
New model
Pan : Every 90 deg. only
Tilt : Not adjustable
Pan : Adjustable every 1 deg.
Tilt : Adjustable every 1 deg.
*1 WV-S4150 / S4550L / S4550LM / X4170 / X4171 / X4571L / X4571LM

## Slide 31
4-5. Streaming Performance
Streaming performance
Number of concurrent access : 14 user
Max. Bandwidth : 50 Mbps
14 user
Bandwidth
Total bandwidth
less than
50 Mbps

## Slide 32
5. AI Applications

## Slide 33
5-1. Overview
Contents |  | Pre-install | KMS | License
 | AI Sound Classification | Standard feature |  | 
APP #1 | AI-VMD / AI People Counting *Installed function: AI-VMD / People Counting / Heat Map / Occupancy Detection | Yes | No | Free
APP #2 | AI Privacy Guard | No | No | Free
 | AI Processor Activation License | Yes | No | Free
About “Pre-install" and “License Free"
150MB
APP #1
AI Sound Classification
(Standard feature)
Max. 3 apps
Install up to 3 apps & Max. capacity will be 150MB
AI Processor
Activation License

## Slide 34
5-1. Overview
AI application combination
 |  | #1 | #2
#1 | AI-VMD / AI People Counting *Installed function: AI-VMD / People Counting / Heat Map / Occupancy Detection |  | Yes
#2 | AI Privacy Guard | Yes | 
*Below condition “Yes” + “AI Sound Classification” can be worked at the same time
As for the restrictions when installing multiple extension software applications on a camera, refer to the support information “Compatibility list for extension software <C0103>” at the link below.
https://i-pro.com/global/en/surveillance/training-support/support/technical-information
Notes
- All applications can be used simultaneously, but stream for privacy masking will be limited to 10fps.

## Slide 35
5-2. System support
NVR / ASM300
 |  | Application settings | People count data display |  | Heat map data display | Alarm reception *2
 |  |  | Cross Line Counting | Area Counting |  | 
iCT |  | Yes | Yes | Yes | No | No
Multi-AI Server (Web dashboard) |  | No | Yes | Yes | Yes | Yes
VMS | VI | No | Yes | No | No | Yes
 | Genetec | No | Yes | Yes | No | Yes
 | Milestone | No | No | No | No | Yes
NVR / ASM300 |  | No | No | No | No | Yes
BI Tool *3 |  | No | Yes (T.B.D) | Yes (T.B.D) | No (T.B.D) | No
iCT
Web dashboard
of Multi-AI Server
(Can be viewed from other PCs)
VMS
Multi-AI Server
BI Tool
MQTT *1
*1 Will be supported by firmware upgrade in the future.
*2 Alarm example : AI-VMD, Occupancy Detection, AI Sound Classification
3rd Party product
*3 Need to check the system operation of the third party product on site.

## Slide 36
5-3. System comparison - iCT / Multi-AI Server
 | iCT | Multi-AI Server
Use case | Collect and view count result sometimes (once a week or month etc.) | Collect and view count result in real time
Supported functions | ・People Counting (Cross Line Counting / Area Counting) | ・People Counting (Cross Line Counting / Area Counting) ・Heat Map
Data collection method | Manual | Auto / Manual
Display in real time | Not supported | Supported

## Slide 37
5-4. System comparison - People Counting / Heat Map
 |  |  | New application |  | Conventional application |  | Remarks
 |  |  | AI-VMD / AI People Counting |  | WV-SAE200W | WV-SAE303W | 
Function | People Counting | Cross Line Counting | Yes |  | Yes | Yes | 
 |  | Area Counting | Yes |  | No | No | 
 | Heat Map |  | Yes |  | Yes | No | 
Setting | Tool |  | iCT *1 |  | Camera browser | People Count Setting Tool | *1 Setup by camera browser will not be supported
Operation | Tool |  | iCT | Multi-AI Server (Web dashboard) | ASM300 | People Count Output Tool | 
 | People Counting | Data collection | Manual | Manual / Auto | Manual | Manual / Auto | 
 |  | Data display | Multi Display | Multi Display | Single Display | Multi Display *2 | *2 Display of data output by excel
 |  | Data output | Excel/CSV (T.B.D) | CSV/PDF (T.B.D) | - | Excel/CSV *3 | *3 Automatic data output function supported
 | Heat Map | Data collection | - | Manual / Auto | Manual | - | 
 |  | Data display | - | Multi Display | Single Display | - | 
 |  | Data output | - | CSV/PDF (T.B.D) | - | - | 

## Slide 38
5-5. App. #1 : AI-VMD / AI People Counting Spec
Function | Item | New application (AI-VMD/People count/Heat map /AI Occupancy Detection) | Conventional application （i-VMD/People count/Heat map）
Common specification | Supported image capture mode | Fisheye Fisheye + Double Panorama Fisheye + Quad PTZ *Wall installation is not supported | Fisheye Fisheye + Panorama Fisheye + Double Panorama Fisheye + Quad PTZ
 | Frame rate limitation | 5MP model : Max. 30fps 12MP model : Max. 15fps | Max.30fps
 | Number of simultaneous detection | Max. 100 (People / Vehicle in total) *Vehicle is supported by AI-VMD only | Max. 32
 | Number of days to save people count / heat map data | Save people count and heat map data Built-in memory : Max. 1 day Save only people count data Built-in memory : Max. 92 days | Save people count and heat map data Built-in memory : Max. 1 day SD memory card : Max. 92 days

## Slide 39
5-5. App. #1 : AI-VMD / AI People Counting Spec
Function | Item | New application (AI-VMD/People count/Heat map /AI Occupancy Detection) | Conventional application （i-VMD/People count/Heat map）
AI-VMD | Detected object | People / Vehicle (AI) *Bicycle is not supported | Moving object (Non-AI)
People Counting (Cross Line Counting) | Counted object | People (AI) | Moving object (Non-AI)
 | Number of line | Max. 8 lines | Max. 12 lines
People Counting (Area Counting) | Counted object | People (AI) | N/A
 | Number of area | Max. 8 areas | N/A
Heat Map | Counted object | People (AI) | Moving object (Non-AI)
Occupancy Detection | Counted object | People (AI) | N/A
 | Number of area | Max. 8 areas | N/A

## Slide 40
5-6. App. #2 : AI Privacy Guard Spec
Function | Item | New application (AI Privacy Guard) | Conventional application (MOR)
AI Privacy Guard | Supported image capture mode | Fisheye Panorama Double panorama Single PTZ Quad PTZ | Fisheye Panorama Double panorama Single PTZ Quad PTZ Fisheye + Panorama Fisheye + Double panorama Fisheye + Quad PTZ
 | Frame rate limitation | Max. 15fps | 1fps
 | Number of simultaneous detection | Max. 100 | N/A
 | Detected object | People (AI) *Face is not supported | All moving objects (Non-AI)

## Slide 41
5-7. Supported image capture mode
Mounting position | Image capture mode | AI-VMD | People Counting |  | Heat Map | Occupancy Detection | AI Privacy Guard
 |  |  | Cross Line Counting | Area Counting |  |  | 
Ceiling | Fisheye | Yes | Yes | Yes | Yes | Yes | Yes
 | Double Panorama | No | No | No | No | No | Yes
 | Quad PTZ | No | No | No | No | No | Yes
 | Single PTZ | No | No | No | No | No | Yes
 | Fisheye + Double Panorama | Yes | Yes | Yes | Yes | Yes | No
 | Fisheye + Quad PTZ | Yes | Yes | Yes | Yes | Yes | No
 | Quad stream | No | No | No | No | No | No
Wall | Fisheye | No | No | No | No | No | Yes
 | Panorama | No | No | No | No | No | Yes
 | Quad PTZ | No | No | No | No | No | Yes
 | Single PTZ | No | No | No | No | No | Yes
 | Fisheye + Panorama | No | No | No | No | No | No

## Slide 42
6. Appearance

## Slide 43
6. Appearance
Color: i-pro white
Finish: ABS resin
Dimensions: ø150 mm × 49.5 mm (H)
{ø5-29/32 inches × 1-15/16 inches (H)}
Weight: Approx. 420 g {0.93 lbs}
WV-S4156 / WV-S4176
Note: No change from current model except Color

## Slide 44
6. Appearance
Color: i-pro white
Finish: Aluminum die cast
Dimensions: ø164 mm × 96.3 mm (H)
{ø6-29/64 inches × 3-25/32 inches (H)}
Weight: Approx.1.3 kg {2.87 lbs} with Base bracket
Approx.880 g {1.94 lbs} with Attachment plate
WV-S4556L / WV-S4556LM / WV-S4576L / WV-S4576LM
Note: No change from current model except Color

## Slide 45
7. Standard Accessories

## Slide 46
7. Standard Accessories
[Abolition Parts]
- CD-ROM
WV-S4156 / WV-S4176
No. | Standard accessories | Qt.
1 | Installation Guide | 1 pc.
2 | Important Safety Instructions | 1 pc.
3 | Warranty card | 1 pc.
4 | Code label | 1 pc.
5 | Attachment plate | 1 pc.
6 | Audio cable | 1 pc.
7 | Power cable plug | 1 pc.
8 | External I/O terminal plug | 1 pc.
9 | Template A (for the attachment plate) | 1 pc.
10 | Cable tie | 2 pcs.
11 | Safety wire lug | 1 pc.
12 | Safety wire | 1 pc.
13 | Washer | 1 pc.
14 | Spring washer | 1 pc.
15 | Cable for easy kitting | 1 pc.

## Slide 47
7. Standard Accessories
WV-S4556L / WV-S4576L
No. | Standard accessories | Qt.
1 | Installation Guide | 1 pc.
2 | Important Safety Instructions | 1 pc.
3 | Warranty card | 1 pc.
4 | Code label | 1 pc.
5 | Base bracket | 1 pc.
6 | Attachment plate | 1 pc.
7 | Fixing screws for attachment plate (M4 x 8 mm {5/16 inches}) | 5 pcs.
8 | Template A (for the attachment plate) | 1 pc.
9 | Template B (for the base bracket) | 1 pc.
10 | Waterproof tape | 1 pc.
11 | 4P alarm cable | 1 pc.
12 | 2P power cable | 1 pc.
13 | Bit (Hex wrench, screw size 6.35 mm {1/4 inches} T20) | 1 pc.
14 | RJ45 Waterproof connecter cover | 1 pc.
15 | RJ45 Waterproof connecter cap | 1 pc.
[Abolition Parts]
- CD-ROM
WV-S4556LM / WV-S4576LM
No. | Standard accessories | Qt.
1 | Installation Guide | 1 pc.
2 | Important Safety Instructions | 1 pc.
3 | Warranty card | 1 pc.
4 | Code label | 1 pc.
5 | Attachment plate | 1 pc.
6 | Template A (for the attachment plate) | 1 pc.
7 | Waterproof tape | 1 pc.
8 | 4P alarm cable | 1 pc.
9 | 2P power cable | 1 pc.
10 | Bit (Hex wrench, screw size 6.35 mm {1/4 inches} T20) | 1 pc.
[Abolition Parts]
- CD-ROM

## Slide 48
8. Optional Accessories

## Slide 49
8. Optional Accessories
No. | Model No. | Image | Description
1 | WV-QJB500-W |  | Adaptor Box (i-PRO white) *1
2 | WV-QJB500-G |  | Adaptor Box (light gray) *1
3 | WV-QJB500-S |  | Adaptor Box (fine silver) *1
4 | WV-Q105A |  | Ceiling Mount Bracket *2
5 | WV-QCL100-W |  | Ceiling Mount Bracket
6 | WV-QCL101-W |  | Ceiling Mount Bracket
7 | WV-QWL500-W |  | Wall Mount Bracket (i-PRO white)
8 | WV-QWL500-G |  | Wall Mount Bracket (light gray)
*1 Refer to the Support Information page for the accessary combination required for installation.
*2 WV-Q105A is “for indoor use only” when installing on the ceiling.
WV-S4156 / WV-S4176

## Slide 50
8. Optional Accessories
WV-S4556L / WV-S4576L
No. | Model No. | Image | Description
1 | WV-QCL501-W |  | Ceiling Mount Bracket (i-PRO white) *1
2 | WV-Q178 |  | Ceiling Mount Bracket (light gray) *1
3 | WV-Q121BS |  | Ceiling Mount Bracket (fine silver) *1
4 | WV-QWL501-W |  | Wall Mount Bracket (i-PRO white) *1
5 | WV-Q185 |  | Wall Mount Bracket (light gray) *1
6 | WV-Q122AS |  | Wall Mount Bracket (fine silver) *1
7 | WV-QAT500-W |  | Attachment Pipe Bracket (i-PRO white) *1
8 | WV-Q179 |  | Attachment Pipe Bracket (light gray) *1
9 | WV-Q123A |  | Attachment Pipe Bracket (fine silver) *1
No. | Model No. | Image | Description
10 | WV-QSR501-W |  | Mount Bracket (i-PRO white)
11 | WV-Q186 |  | Mount Bracket (light gray)
12 | WV-Q124 |  | Mount Bracket (fine silver)
13 | WV-QJB500-W |  | Adaptor Box (i-PRO white) *1
14 | WV-QJB500-G |  | Adaptor Box (light gray) *1
15 | WV-QJB500-S |  | Adaptor Box (fine silver) *1
16 | WV-QPL500-W |  | Pole Mount Bracket (i-PRO white) *1
17 | WV-Q182 |  | Pole Mount Bracket (light gray) *1
18 | WV-Q188 |  | Pole Mount Bracket (fine sliver) *1
*1 Refer to the Support Information page for the accessary combination required for installation.

## Slide 51
8. Optional Accessories
WV-S4556L / WV-S4576L
No. | Model No. | Image | Description
19 | WV-QCN500-W |  | Corner Mount Bracket (i-PRO white) *1
20 | WV-Q183 |  | Corner Mount Bracket (light gray) *1
21 | WV-Q189 |  | Corner Mount Bracket (fine silver) *1
22 | WV-Q105A |  | Ceiling Mount Bracket *2
23 | WV-QCL100-W |  | Ceiling Mount Bracket
24 | WV-QCL101-W |  | Ceiling Mount Bracket
25 | WV-QWL500-W |  | Wall Mount Bracket (i-PRO white)
26 | WV-QWL500-G |  | Wall Mount Bracket (i-PRO white)
*1 Refer to the Support Information page for the accessary combination required for installation.
*2 WV-Q105A is “for indoor use only” when installing on the ceiling.
WV-S4556LM / WV-S4576LM
No. | Model No. | Image | Description
1 | WV-QJB501-W |  | Base bracket (i-PRO white)

## Slide 52
Appendix:
System Support Schedule

## Slide 53
Each System Support Schedule - Camera
 | Indoor |  | Outdoor | 
 | 5MP model | 12MP model | 5MP model | 12MP model
 | WV-S4156 | WV-S4176 | WV-S4556L WV-S4556LM | WV-S4576L WV-S4576LM
Product release | Nov. 2021 |  |  | 
NVR | V4.60 / E. Nov. |  |  | 
ASM300 | V4.40 / E. Nov. |  |  | 
PSV | V6.10 / E. Jul. (Released) |  |  | 
iCT | V2.30 / E. Nov. |  |  | 
SDT | V2.50 / E. Nov. |  |  | 
VI | V7.9 / Dec. |  |  | 
Genetec | 5.10.2.0 (DP10.7) / Dec. |  |  | 
Milestone | DP11.9 / E. Dec. |  |  | 

## Slide 54
Each System Support Schedule - Application
 | App #1 |  |  |  |  | App #2 | Standard feature
 | AI-VMD | People Counting |  | Heat Map | Occupancy Detection | AI Privacy Guard | AI Sound Classification
 |  | Cross Line Counting | Area Counting |  |  |  | 
Product release | Nov. 2021 |  |  |  |  |  | 
NVR | V4.60 / E. Nov. | Not support |  |  | V4.60 / E. Nov. | Not support | V4.60 / E. Nov.
ASM300 | V4.40 / E. Nov. | Not support |  |  | V4.40 / E. Nov. | Not support | V4.40 / E. Nov.
PSV | V7.00 / E. Jan. | Not support |  |  | V7.00 / E. Jan. | V6.10 / E. Jul. (Released) | V7.00 / E. Jan.
iCT | V2.30 / E. Nov. |  |  |  |  |  | 
SDT | V2.50 / E. Nov. |  |  |  |  |  | Not support

## Slide 55
Each System Support Schedule - Application
 |  | App #1 |  |  |  |  |  | App #2 | Standard feature
 |  | AI-VMD | People Counting |  |  | Heat Map | Occupancy Detection | AI Privacy Guard | AI Sound Classification
 |  |  | Cross Line Counting | Area Counting |  |  |  |  | 
Product release |  | Nov. 2021 |  |  |  |  |  |  | 
Multi-AI Server |  | V1.2.0 / M. Jan. |  |  |  |  |  | Not support | V1.2.0 / M. Jan.
 | Web dashboard | Not support | V1.2.0 / M. Jan. |  |  |  | Not support |  | 
 | plugin for VI | V1.1.0 / B. Dec. | Not support |  |  |  | V1.1.0 / B. Dec. | Not support | V1.1.0 / B. Dec.
 | plugin for Genetec | Not support |  |  |  |  |  |  | 
 | plugin for ASM300 | V1.0.0 / B. Feb. | Not support |  |  |  | V1.0.0 / B. Feb. | Not support | V1.0.0 / B. Feb.
VI |  | V7.9.1 / FY21 4Q |  | Not support |  |  | V7.9.1 / FY21 4Q | V7.9 / Dec. | 
 | VI Object Count plugin | Not support | V1.00 / Jul. (Released) *1 | Not support |  |  |  |  | 
Genetec |  | 5.10.3.0 (DP10.7) / E. Jan. |  |  | Not support |  | 5.10.2.0 (DP10.7) / Dec. |  | 
Milestone |  | DP11.9 / E. Dec. (T.B.D) | Not support |  |  |  |  | DP11.9 / E. Dec. (T.B.D) | 
*1 it is necessary to upgrade VI version (V7.9).

## Slide 56
Appendix:
Image quality comparison (5MP model)

## Slide 57
Summary
SD : ON, AGC : 48dB
H264, VBR, 30fps, image quality : 3
Zipstream : OFF
* Other setting parameters are default values.
SD : ON, iA : ON, AGC : 11
H265, VBR, 30fps, MAX bitrate : 14336 kbps, image quality : 3 Smart coding : OFF
* Other setting parameters are default values.
i-PRO S4551L
AXIS M3057-PLVE Mk II
SD : ON, iA : ON, AGC : 11
H265, VBR, 30fps, MAX bitrate : 14336 kbps, image quality : 3
Smart coding : OFF
* Other setting parameters are default values.
i-PRO S4556L
SD : ON, AGC : high
H265, VBR, 30fps, MAX bitrate : 2048 kbps
WiseStream : OFF
* Other setting parameters are default values.
Hanwha XNF-8010RV
Scoring method: Scored by deducting and adding points beginning with 3 points.
Chart: 
| Day time Outdoor | Day time Indoor | SD Day time | Night time Outdoor | Low light | IR-LED
i-PRO S4556L | 3.5 | 3.5 | 2.5 | 3 | 3.5 | 2.5
i-PRO S4551L | 3.5 | 3.5 | 2.5 | 3 | 3.5 | 2.5
AXIS M3057-PLVE MkII | 3.5 | 4.5 | 3.5 | 3 | 3 | 3.5
Hanwha XNF-8010RV | 3.5 | 3.5 | 2.5 | 2.5 | 3 | 2

## Slide 58
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
3.5 points
3.5 points
3.5 points
3.5 points
Measured bit rate: 3122kbps
Measured bit rate: 3238kbps
Measured bit rate: 2292kbps
Measured bit rate: 4241kbps
Day time Outdoor
Low peripheral resolution and high distortion
Illuminance : 50000 – 90000 lux

## Slide 59
Day time Indoor
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +1.0
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | -0.5
Resolution | +0.5
Color reproduction | +0
3.5 points
3.5 points
4.5 points
3.5 points
Measured bit rate: 1489kbps
Measured bit rate: 1443kbps
Measured bit rate: 1080kbps
Measured bit rate: 2991kbps
Illuminance : 800 – 1000 lux

## Slide 60
SD Day time
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0
2.5 points
2.5 points
3.5 points
2.5 points
Measured bit rate: 1659kbps
Measured bit rate: 1377kbps
Measured bit rate: 1150kbps
Measured bit rate: 3510kbps
Low peripheral resolution and high distortion
Illuminance: [Outside] 90000lux / [Inside] 350lux

## Slide 61
Night time Outdoor
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -0.5
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -0.5
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +1.0
Brightness | -1.0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -1.0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
3.0 points
3.0 points
3.0 points
2.5 points
Measured bit rate: 2123kbps
Measured bit rate: 1731kbps
Measured bit rate: 342kbps
Measured bit rate: 4263kbps
Illuminance : 0.1 – 0.7 lux

## Slide 62
Low light
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | -1.0
Resolution | +0
Color reproduction | +0.5
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -1.0
Brightness | +0.5
Resolution | +0
Color reproduction | +0.5
3.5 points
3.5 points
3.0 points
3.0 points
Measured bit rate: 1776kbps
Measured bit rate: 1855kbps
Measured bit rate: 237kbps
Measured bit rate: 4234kbps
Illuminance : 0.3 – 0.5 lux

## Slide 63
IR-LED
i-PRO S4556L
i-PRO S4551L
AXIS M3057-PLVE Mk II
Hanwha XNF-8010RV
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | -0.5
Brightness | +0
Resolution | +0
Color reproduction | -
2.5 points
2.5 points
3.5 points
2.0 points
Measured bit rate: 2115kbps
Measured bit rate: 3910kbps
Measured bit rate: 712kbps
Measured bit rate: 4219kbps
Illuminance : 0.1 – 0.7 lux

## Slide 64
Appendix:
Image quality comparison (12MP model)

## Slide 65
Summary
SD : ON, AGC : 48dB
H264, VBR, 30fps, image quality : 3
Zipstream : OFF
* Other setting parameters are default values.
SD : ON, iA : ON, AGC : 11
H265, VBR, 30fps, MAX bitrate : 20480 kbps, image quality : 3
Smart coding : OFF
* Other setting parameters are default values.
i-PRO X4573L
AXIS M3058-PLVE
SD : ON, iA : ON, AGC : 11
H265, VBR, 30fps, MAX bitrate : 20480 kbps, image quality : 3
Smart coding : OFF
* Other setting parameters are default values.
i-PRO S4576L
SD : ON, AGC : high
H265, VBR, 30fps, MAX bitrate : 8192 kbps
WiseStream : OFF
* Other setting parameters are default values.
Hanwha XNF-9010RV
Scoring method: Scored by deducting and adding points beginning with 3 points.
Chart: 
| Day time Outdoor | Day time Indoor | SD Day time | Night time Outdoor | Low light | IR-LED
i-PRO S4576L | 4.5 | 4 | 3 | 3.5 | 3.5 | 2.5
i-PRO X4573L | 4.5 | 4 | 3 | 3.5 | 3.5 | 2.5
AXIS M3058-PLVE | 3.5 | 3 | 2.5 | 2.5 | 2.5 | 3.5
Hanwha XNF-9010RV | 2 | 2.5 | 2 | 1 | 1.5 | 1.5

## Slide 66
Day time Outdoor
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0.5
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0.5
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | -0.5
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | -0.5
Color reproduction | +0
4.5 points
4.5 points
3.5 points
2.0 points
Measured bit rate: 4032kbps
Measured bit rate: 4368kbps
Measured bit rate: 4835kbps
Measured bit rate: 2751kbps
Illuminance : 50000 – 90000 lux

## Slide 67
Day time Indoor
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0.5
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | +0.5
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | -0.5
Brightness | +0
Resolution | -0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | -0.5
Resolution | +0.5
Color reproduction | +0
4.0 points
4.0 points
3.0 points
2.5 points
Measured bit rate: 1515kbps
Measured bit rate: 1678kbps
Measured bit rate: 1779kbps
Measured bit rate: 1138kbps
Illuminance : 800 – 1000 lux

## Slide 68
SD Day time
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | -0.5
Brightness | +0
Resolution | +0.5
Color reproduction | +0
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | -0.5
Brightness | +0
Resolution | +0
Color reproduction | +0
3.0 points
3.0 points
2.5 points
2.0 points
Measured bit rate: 1751kbps
Measured bit rate: 1885kbps
Measured bit rate: 2692kbps
Measured bit rate: 1023kbps
Illuminance: [Outside] 90000lux / [Inside] 350lux

## Slide 69
Night time Outdoor
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | -0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -1.0
Brightness | -0.5
Resolution | +0
Color reproduction | -0.5
3.5 points
3.5 points
2.5 points
1.0 points
Measured bit rate: 10896kbps
Measured bit rate: 10183kbps
Measured bit rate: 9371kbps
Measured bit rate: 419kbps
Illuminance : 0.4 – 0.7 lux

## Slide 70
Low light
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | +0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | -1.0
Resolution | +0
Color reproduction | +0
Evaluation item | Score
Face visibility | +0
Sensitivity, S/N | -1.0
Brightness | +0.5
Resolution | +0
Color reproduction | +0
3.5 points
3.5 points
2.5 points
2.5 points
Measured bit rate: 1776kbps
Measured bit rate: 1855kbps
Measured bit rate: 237kbps
Measured bit rate: 4234kbps
Illuminance : 0.5 – 1.0 lux

## Slide 71
IR-LED
i-PRO S4576L
i-PRO X4573L
AXIS M3058-PLVE
Hanwha XNF-9010RV
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | +0.5
Sensitivity, S/N | +0
Brightness | +0
Resolution | +0
Color reproduction | -
Evaluation item | Score
Face visibility | -0.5
Sensitivity, S/N | -0.5
Brightness | -0.5
Resolution | +0
Color reproduction | -
2.5 points
2.5 points
3.5 points
1.5 points
Measured bit rate: 4792kbps
Measured bit rate: 5675kbps
Measured bit rate: 2626kbps
Measured bit rate: 394kbps
Illuminance : 0.4 – 0.7 lux

## Slide 72
Appendix:
AI Sound Classification

## Slide 73
AI Sound Classification
Support identifying specific sound by AI
Identifying a specific sound
among other noises
Gunshot
Daily noise
Vehicle horn
Gunshot

## Slide 74
AI Sound Classification
Spec comparison
Function | New model | Conventional model
Audio Detection | Yes | Yes
AI Sound classification | Yes | No
SD card recording triggered by Audio Detection | No | Yes
Spec of AI Sound classification
Item | Content | 
Classification target / Examples | 1. Gunshot | 3. Vehicle Horn
 | 2. Yell | 4. Glass break
Classification condition | The level of target sound is 6dB larger than ambient sound. (sound classification can be used in indoor and outdoor environments) Target sound continues more than a second. (except for gunshot) | 

## Slide 75
Detectable distance for AI Sound classification
Ambient noise level | Example of scene | Detectable distance (Guideline) | 
 |  | Yell / Glass break (90 - 110 dB) | Gunshot / Vehicle horn (110 - 130 dB)
70 dB | Noisy streets, main roads | 4 m (13 feet) | 15 m (49 feet)
60 dB | Ordinary conversation, quiet car | 8 m (26 feet) | 30 m (98 feet)
50 dB | Residential area, office in the daytime | 16 m (52 feet) | 50 m (164 feet) *1
40 dB | Residential area at night, library | 32 m (105 feet) | 50 m (164 feet) *1
Microphone requirements for AI Sound classification
  Frequency characteristics: support 200 Hz to 8 KHz
  Omnidirectional microphone
Confirmed microphone
  Built-in mic (WV-S4156, WV-S4176)
  ECM-CS3 (SONY) *2, AT9904 (audio-technica) *2
*1 The detectable distance may change depending on the surrounding environment, such as when the building blocks it.
*2 may not be available in your region
AI Sound Classification

## Slide 76
Restrictions
In the following cases, target sound may not be detected by AI sound identification.
Target sound is too short
Multiple types of target sounds occur at the same time (only one of them is detected)
It's raining (especially when rain drops hit the microphone directly)
Target sound is too quiet or too loud
Other sounds that are very similar to the target sound may be detected.
[Example]
Detects tire puncture as "gunshot"
If the sound of glass breaking and the impact sound is strong, it is detected as "gunshot".
Detects bird calls as “yell"
Detects an emergency vehicle siren as a “yell"
Detects the sound of tableware breaking as "glass break“
AI Sound Classification

## Slide 77
Setting screen
Select On/Off.
Select detection sensitivity for the volume from Low/Middle/High.
Select sound for the target of alarm.
*In order to link the alarm with the NX recorder or ASM300, it is necessary to register the message ID of the alarm.
See next page.
"Other" is detected by volume.
Select when there is no sound to be classified in the setting items.
It is not recommended to select "Other" in duplicate with other analytics target (such as a “Gunshot”).
When a gunshot actually occurs, “Gunshot" and “Other" are detected
and two alarms are notified.
In particular, when linking an alarm with the NX recorder, it is possible
that the “Gunshot" detection cannot be received because
the NX recorder has set a period during which notifications are not
continuously accepted (Alarm disarm duration [default : 2 seconds]).
In iCT V2.0 or later, you can adjust the judgment threshold of Gunshot/Yell/Vehicle horn/Glass break.
AI Sound Classification

## Slide 78
Ref. Extension software alarm setting - Recorder Setting
Extension software alarm setting
Extension software alarm
Go to [REC & event]-> [Advanced setup] tab -> [Extension software alarm], and click “Setup” to open the [Extension software alarm] setup screen.
Name
Enter the name of alarm.
Ex. “AI Sound Classification (Gunshot)”
Message ID
Enter an ID (Gunshot:70 / Glass break:71 / Vehicle horn:72 / Yell:73) for AI Sound Classification alarm.
No.
No.1-4: reserved for AI-VMD
No.5-8: available
Set an ID for AI Sound Classification alarm in an available line from No.5 to 8.

## Slide 79
Ref. Extension software alarm setting - ASM300 Setting
Extension software alarm setting
Intruder
Loitering
Direction
Cross Line
User-defined 1
User-defined 2
User-defined 3
User-defined 4
Name
Enter the name of alarm.
Ex. “AI Sound Classification (Gunshot)”
Message ID
Enter an ID (Gunshot:70 / Glass break:71 / Vehicle horn:72 / Yell:73) for AI Sound Classification alarm.
No.
No.1-4: reserved for AI-VMD
No.5-8: available
Set an ID for AI Sound Classification alarm in an available line from No.5 to 8.
Match the setting order of each message ID of No. 1 to No. 8 on the Extension software alarm setting screen of the recorder, and No. 1 to No. 8 of this setting screen.

## Slide 80
Appendix:
Other Specifications

## Slide 81
Easy Kitting for Indoor Model
Kitting Window
Conventional model *1
Change of packing specifications
New model
Note : Easy Kitting for Outdoor model has been supported from current model
Cable for easy kitting
(Standard Accessories)
*1 WV-S4150 / S4550L / S4550LM / X4170 / X4171 / X4571L / X4571LM

## Slide 82
Frame rate mode setting
25fps mode is added
Conventional model *1
New model
*1 WV-S4150 / S4550L / S4550LM / X4170 / X4171 / X4571L / X4571LM

## Slide 83
Restrictions on Super Dynamic / Wide dynamic range
If the Super Dynamic / Wide dynamic range level is set to 30 or more, maximum frame rate will be 15fps.
Level Setting: Default=27
# Up to 30 fps transmission is available
Level | 27 | 28 | 29 | 30 | 31
Framerate | 30fps | 30fps | 30fps | 15fps | 15fps
Dynamic range *1 | 96dB | 102dB | 108dB | 114dB | 120dB
*1 : It is theoretical value and may change depending on an environment.
Level Setting: Default=29
# Up to 30 fps transmission is available
Level | 29 | 30 | 31
Framerate | 30fps | 15fps | 15fps
Dynamic range *1 | 72dB | 78dB | 84dB
5MP model
12MP model

## Slide 84
Note for time to refresh images during camera control (Pan/Tilt/Zoom)
 | Conventional model （1600x1200） | New model （1600x1200） | AXIS （1600x1200）
 | WV-S4150 | WV-S4151 | M3057-PLVE
Quad PTZ | 0.13(s) | 0.31(s) | 0.18(s)
 | Conventional model （2560x1920） | New model （2560x1920） | AXIS （2560x1920）
 | WV-X4171 | WV-X4573L | M3058-PLVE
Quad PTZ | 0.24(s) | 0.56(s) | 0.38(s)
5MP model measurement results
12MP model measurement results
Measurement PC spec. : HP Elite Desk 800 G5 SF (Core i7-9700/CPU 3GHz x8 core/Memory 16GB)

## Slide 85
Privacy zone setting
Privacy mask can be set by designating 4 points on the screen.
Privacy mask can be set by rectangle.
Conventional model *1
New model
*1 WV-S4150 / S4550L / S4550LM / X4170 / X4171 / X4571L / X4571LM

## Slide 86
Other changes
 | Conventional model | New model
Frame rate (When Monitor Output is Used) | - | When “Audio out” is set to “Monitor”, the frame rate may be reduced. After camera installation is completed, “Audio out” is set to “Audio”.
Double panorama | The number of pixels in the upper and lower images is same at all resolution. | 5MP Model [Resolution of 1280 x 720] Upper image : 1280 x 362 / Lower image : 1280 x 358 12MP Model [Resolution of 320 x 180] Upper image : 320 x 92 / Lower image : 320 x 88
Auto Pan (Image Refresh time) | Pan speed Approx. 6 deg. / sec Image refresh interval Approx. 1 deg. / step | Pan speed Approx. 6 deg. / sec Image refresh interval Approx. 2.4 deg. / step

## Slide 87
Case where conventional 360-degree camera and new 360-degree camera are mixed
New system will not support conventional 360-degree camera
In the case conventional and new 360-degree camera are mixed, each software will be required
Conventional people count
(people count output tool)
Data collection
Auto / Manual
Camera replaced
New people count（iCT）
Data collection
Manual
■conventional system
■conventional and new system mixed
Conventional people count
(people count output tool)
Data collection
Auto / Manual

## Slide 88
Output IF
 | App. #1 : AI-VMD / AI People Counting |  |  |  |  |  | Standard feature
Function | AI-VMD |  | People Counting |  | Heat Map | Occupancy Detection | AI Sound Classification
Output data | Alarm | Meta information | Meta information |  | Meta information | Alarm | Alarm
 |  | Detection frame | Count data | Detection frame | Heat map data |  | 
ONVIF | Yes | Yes | Yes *1 | No | Yes *1 | Yes | Yes
CGI | Yes | No | Yes | No | Yes | No | Yes
TCP alarm protocol | Yes | No | No | No | No | Yes | Yes
Additional information in video stream | Yes | Yes | Yes | Yes | No | Yes | Yes
HTTP POST | No | No | Yes | No | No | No | No
MQTT | No | No | Yes *2 | No | No | No | No
30
25
*1 Data format is proprietary.
*2 Will be supported by firmware upgrade in the future.

## Slide 89
Version History

## Slide 90
Version History
No | Update contents | Page No. | Version | Update
1 | 1st Version | - | 1.00 | 10.Sep.2021
2 | Corrected the system support information. | P.34 | 1.01 | 28.Sep.2021
3 | Corrected the AI ​​Privacy Guard support information of NVR / ASM300 to “Not support". | P.53 | 1.01 | 28.Sep.2021
4 | Added notes when extension software alarm setting. | P.78 | 1.01 | 1.Oct.2021
5 | Removed AI Privacy Guard from pre-installation. | P.32 | 1.01 | 1.Oct.2021
6 | Corrected the link page of the caution statement. | P.24 | 1.02 | 25.Oct.2021
7 | Corrected system support information. | P.34 | 1.02 | 25.Oct.2021
8 | Corrected support schedule of camera. | P.52 | 1.02 | 25.Oct.2021
9 | Corrected support schedule of application. | P.53, P.54 | 1.02 | 11.Nov.2021
10 | Corrected the linked URL. | P.33 | 1.02 | 12.Nov.2021
11 | Corrected Important notice for Double Panorama Image cropping position. | P.28 | 1.03 | 18.Nov.2021
12 | Corrected system support information. | P.34 | 1.03 | 24.Nov.2021
13 | Added description about supported image capture mode. | P.40 | 1.04 | 29.Nov.2021
14 | Corrected support schedule of camera. | P.52 | 1.04 | 9.Dec.2021
15 | Corrected support schedule of application. | P.54 | 1.04 | 9.Dec.2021

## Slide 91
Version History
No | Update contents | Page No. | Version | Update
16 | Support company name change | - | 1.05 | 14. Jul. 2022
17 | Corrected streaming performance information. | P.30 | 1.06 | 10. Aug. 2022